## Slide 1: Head of line blocking issue for WiFi
Date: 2023-05-01
Authors:

## Slide 2: Introduction
The WiFi MAC typically is designed to provide in-order data delivery to upper layers.
  Packets are transmitted in increasing Sequence Numbers.
  Reorder buffer at recipient holds the received packets as long as there is a ‘hole’ preceding it.
In many applications the in-sequence delivery is desirable, and the current design works great.
However, the in-sequence delivery restriction can also result in head-of-line blocking issue:
  a packet that’s held in reorder buffer is not forwarded up if there is a hole.
  Sender needs to TX packets with lower SN before it can TX one that’s higher.
Since improving peak latency is key goal for UHR, in addition to channel access improvements, we should also look at resolving the head-of-line blocking problem.

## Slide 3: Example scenarios
STA is transmitting frames belonging to multiple SCS streams that happen to map to same TID.
  Note: it is possible for transmitter to group packets based on flow and intelligently assign SN. However, once there is a hole, all following frames are held up even if they belong to different flows which could affect latency performance.
STA is transmitting frames belonging to different QUIC/SCTP streams that belongs to the same connection.
  Note: QUIC protocol already has mechanism to ensure in-sequence delivery by handling this at application layer => not always necessary to repeat it again.
A STA is txmitting frames that map to TID x after assigning SN when it receives instruction to TX a high priority frame that also maps to TID x.

## Slide 4: Recap CCMP/GCMP encryption for unicast frames
PN space is shared across all TIDs. However, for each TID there is a unique counter that tracks the highest PN received so far for that TID.
At transmitter side each MPDU is incremented using PN.
At receiver side,
  Once a MPDU has been released from reorder buffer, the PN of that MPDU (RCVPN) is compared against the highest received PN (HRPN) for that TID; the frame passes replay check if RCVPN is higher than HRPN and HRPN value is set as RCVPN.
Notes: For CCMP:
  a MIC is computed on Data part using PN, Source Address and Priority.
  The MIC and CCMP header containing PN are added to MPDU.
  The MIC+plain text Data is then encrypted. The CCMP and MAC header are transmitted in clear.

## Slide 5: Proposal
Allow the MAC-SAP to deliver out-of-order packets optionally for a subset of TIDs.
  Maybe limit to 1 or 2, may use only when a flow that can benefit from OOO delivery is established (i.e., following a corresponding SCS negotiation).
This is similar to out-of-order delivery by PDCP in 3GPP.
Frame replay detection:
  Today the in-order delivery sequence allows for easy frame replay detection (i.e., just check if the PN number is greater than last highest PN number).
  For out-of-order delivery, the frame replay detection needs to change (e.g., by maintaining a sliding scoreboard of PNs).
  Need a way to separate the PN space used by frames requiring OOO delivery vs ones that require IO.

## Slide 6: Example out-of-order delivery procedure
Originator
Recipient
SN=x, PN = 50
SN=11, PN = 51
50
113
hole
PN window; max length: 64
51
…
BA
SN=11, PN = 51
BA
114
hole
PN window
51
…
Data frame
Mgt frame
SN=x+63, PN = 113
SN=74, PN = 114
…
BA scoreboard = 64 = PN window bitmap
113

## Slide 7: Conclusion
Propose to allow out-of-order delivery of frames at layer-2 without losing reliability provided by BA.
The solution roughly involves using a sliding window bitmap based approach for replay detect of frames that can be delivered out-of-order.

## Slide 8: Summary of overall proposal
BA scoreboarding
Duplicate Detection per SN
MPDU Decryption
BA Buffering and Reordering per SN
Replay Detection Per PN
Rx STA maintains a per-TID scoreboard
for MPDUs that were received or not based on SN
Rx STA insert received MPDUs to a reorder buffer. Forward MPDUs up if there is no hole. Holes are moved on rxing a new MPDU or on BAR.
Detect replay if received PN < Highest rxed PN for that TID; update counter for highest received PN for that TID.
MSDU Flow Receiving
Rx STA maintains a per-TID scoreboard
for MPDUs that were received or not based on SN
Baseline Rx STA behavior
Proposed Rx STA behavior for TIDs with OOO delivery
Same as baseline except MPDUs are forwarded up even if there is a hole.
Maintain PN window bitmap.
If rxed PN matches an entry, then detect replay. PN window updated to [last PN – size, Last PN]