## Slide 1: TGbh PICS
Date: 2023-04-25
Authors:

## Slide 2: Abstract
Presentation for discussion, to reach consensus on TGbh PICS
r0 – initial version

## Slide 3: TGbh PICS status
Currently, D0.2 has a PICS statement, that only references Device ID
Since we added IRM recently, need to add PICS coverage for IRM
Current PICS has Device ID depend on PC34, which is RSNA support
  Should this (also) depend on “infrastructure STA and AP” (not Mesh, not IBSS, etc.)?
CID 62 resolution added (slightly different) text (which is a conflict), and with dependency on CFAP or CFSTAofAP.
Do we want/think it’s useful to have a single option for a “Changing MAC address” condition in the PICS?

## Slide 4: Proposed PICS for TGbh
IUT configuration: Add a row:
Item | IUT configuration | References | Status | Support
CFCMA | Support for changing MAC address | 12.2.11 (Changing MAC address) | PC34 AND CFAP:O PC34 AND CFSTAofAP:O | Yes o No o
MAC protocol capabilities: Add 2 rows:
Item | Protocol Capability | References | Status | Support
PC<ANA> | Device ID | 12.2.11.1 (Device ID indication) | CFCMA:O | Yes o No o
PC<ANA> | IRM | 12.2.11.2 (Identifiable Random MAC address operation) | CFCMA:O | Yes o No o