## Slide 1: A response to the response to CID3033 in LB2270 on 802.11m D2.0
1 May 2023
Authors:
Name | Company | Phone | email
Andrew Myles | unaffliated | +61 418 656587 | andrew@myles.au

## Slide 2: In LB258, TGme expressed some sympathy for the problem highlighted by CID2323, but not the solutions
  CID2323 (author: Thomas Derham) in LB258 commented on the Regulatory Info subfield and suggested some changes
  In 11-22-0350 (author: Andrew Myles), I proposed an alternative solution to that suggested by Derham in CID2323
  Both proposed changes (by Derham & Myles) were rejected by TGme in their response to CID2323
  TGme’s response seemed to accept that while the premise of Derham’s comment in CID2323 is false, the problem highlighted by CID2323 is real
  It therefore seems to be accepted that a change of some sort is required, but the question is what change?

## Slide 3: In LB270, Myles provided a response in CID3033 to the questions in TGme’s response to CID2323
  In rejecting the changes proposed in 11-22-0350 (author: Andrew Myles), TGme seemed to display some sympathy for the reasoning & suggested proposal for further generalisation, albeit with questions
  The author responded in CID3033 in LB270 to the questions posed in TGme’s response to CID2323, noting that:
    An ANA assignment is indeed required, as suggested by TGme. Myles agreed that this can be achieved by separate motion in the future
    The need for a formal definition of C2C can be avoided. Myles proposed some new text to achieve this goal
    TGme is correct that the text probably should not contain "shall" or "shall not", as any enforcement is a regulatory issue. Myles proposed new text that avoided "shall" and "shall not"
    This signalling from the AP to the client is required so that the client can know about the APs choices

## Slide 4: A replacement to Table E-12 will allow administrators to have management control over enablement
  In the response to Myles’ comment in CID3033 in LB270, TGme was ambiguous about next steps
  It appears, assuming that the need for change is accepted and generalisation is a good direction, that TGme wants Myles to provide a full and explicit set of changes
  The following page contains the proposed change, which is to replace Table E-12 on pp 5529-30 of 802.11me D3.0
    This proposal provides mechanisms to allow an indoor AP or indoor standard power AP to signal whether it consents to being used to enable another AP
    This allows flexibility for administrators to have management control over whether other APs are enabled by their infrastructure

## Slide 5: It is proposed that the table below replaces Table E-12 on pp 5529-30 of 802.11me D3.0
Proposed Table E-12 revisions
Value | Description | Enablement
0 | Indoor AP (Enabler) An AP whose operation does not require control from an external system such as an Automated Frequency Coordination (AFC) system but that is subject to additional regulatory requirements intended to prohibit outdoor operation | Value indicates the Indoor AP (Enabler) consents to being used to enable operation of an Indoor Enabled AP if such enablement is allowed by regulations
1 | Standard Power AP An AP whose operation requires control from an external system such as an AFC system. | Value indicates the Standard Power AP does not consent to being used to enable operation of another AP
2 | Very Low Power AP An AP whose operation does not require control from an external system such as an AFC system, is not subject to additional regulatory requirements intended to prohibit outdoor operation, and is restricted to very low transmit power. | Value indicates the Very Low Power AP does not consent to being used to enable operation of another AP
3 | Indoor Enabled AP An AP whose operation relies on being able to successfully receive an enabling signal (as defined by the regulatory rules) from an Indoor AP (Enabler) or an Indoor Standard Power AP (Enabler). | Value indicates the Indoor Enabled AP does not consent to being used to enable operation of another AP
4 | Indoor Standard Power AP (Enabler) An AP whose operation requires control from an external system such as an AFC system and that is subject to additional regulatory requirements intended to prohibit outdoor operation. | Value indicates the Indoor Standard Power AP (Enabler) consents to being used to enable operation of an Indoor Enabled AP if such enablement is allowed by regulations
5 | Indoor AP An AP whose operation does not require control from an external system such as an Automated Frequency Coordination (AFC) system but that is subject to additional regulatory requirements intended to prohibit outdoor operation. | Value indicates the Indoor AP does not consent to being used to enable operation of another AP
6 | Indoor standard power AP An AP whose operation requires control from an external system such as an AFC system and that is subject to additional regulatory requirements intended to prohibit outdoor operation. | Value indicates the Standard Power AP does not consent to being used to enable operation of another AP
7 | An AP that does not operate according to any of the descriptions for values 0-6. | Value indicates the Standard Power AP does not consent to being used to enable operation of another AP