## Slide 1: AMP IoT Medium Access
Date: 2023-05-15
Authors:

## Slide 2: AMP Medium Access Control
Consensus Straw Poll from [1]:
Simplified MAC (on top of existing WLAN technologies) + Enhanced power saving/power management
Consider frequency bands of Sub-1 GHz and 2.4 GHz
Question: How to implement medium access in AMP-only IoT devices?
Listen-before-Talk consumes significant power [3]
AP-driven medium access necessary to limit power consumption of AMP-only IoT devices
Which types of AP-driven medium access mechanisms are already specified?

## Slide 3: Type 1: HT Reverse Direction Protocol
TXOP owner sends Reverse Direction (RD) grant in PPDU
  TXOP owner denoted as “RD initiator”
“RD responder” sends one or more PPDUs as response
RD initiator finishes RD grant
Multiple RD grants per TXOP to different STAs possible
PPDU + RD grant
RD response burst
RD initiator final PPDU
Backoff
TXOP
RD initiator
RD responder

## Slide 4: Type 2: S1G Bidirectional TXOP
Extension of RDP to multiple sequences
  Separated by SIFS
  Inspired by Polling mechanisms in obsolete Point Coordination Function
PS-Poll + BDT
Data (more data = 1)
Data/Poll (more data = 1)
Data (more data = 1)
Data/Poll (more data =0)
Data (more data =0)
BlockAck
1st sequence
2nd sequence
3rd sequence
TXOP

## Slide 5: Type 3: EHT Triggered TXOP Sharing
Initiated by a MU-RTS TXS trigger frame
  Only one User Info field, addressed to an associated non-AP STA
Allocates time for uplink data
MU-RTS TXS Trigger
CTS
Data to AP in non-TB PPDU
Backoff
Time allocated in MU-RTS TXS TF
EHT AP
EHT non-AP STA
BlockAck
TXOP

## Slide 6: Type 4: HE Triggered Uplink
Initiated by Basic TF
  Containing common & user-specific info (time allocated, RU allocation, transmission parameters, ...)
Supports
  Multi-user aggregation
  Random access procedure (UORA)
Basic Trigger Frame
Backoff
Time allocated in Basic TF
HE AP
HE non-AP STA1
MU-BlockAck
TXOP
HE non-AP STA2
Data to AP in TB PPDU
Data to AP in TB PPDU
P
P

## Slide 7: AP-Driven Random Access
Random access is required for “unknown” AMP devices
  E. g., initial identification of the device
Question: How to realize AP-driven random access?
  AP signals a “set of resources”
  AMP device selects one of the resources randomly and transmits
  AP replies with success/failure status
  Assumption: AMP devices cannot do LBT or channel sensing

## Slide 8: Type 1: Random access in time
Similar to random access procedure known from RFID [4]
Add random access to Bidirectional TXOP
  Backoff (BO) is also controlled by the AP, using “BO counter frames” and PIFS to wait for reply
PS-Poll + BDT + CW: 0...15
AP
AMP-only
IoT device
Draw “2”
PIFS
0?
PIFS
1?
PIFS
2?
SIFS
Data
ACK, 6?
SIFS

## Slide 9: Type 2: Random access in frequency
Use random access procedure of HE Triggered Uplink
  UORA: RUs are dedicated for random access by AP, STA selects RU randomly
Trigger Frame
AP
AMP-only
IoT device
Draw “2”
SIFS
ACK
Data
SIFS

## Slide 10: Strawpoll
Do you agree to define a medium access method for AMP WLAN that bases on the principles of HE Triggered Uplink?
  Details are TBD
  Y / N / A
  Notes: Details are, for example,
  How the AP signals duration, frequency resources, transmit parameters, etc... in a trigger frame
  How the AMP STAs select and reply in separate frequency resources
  UORA-like random-access procedure

## Slide 11: References
[1] Yinan Qi et al., “Proposal for consensus straw poll and motion,” IEEE 802.11 submission 11-23/0406r1
[2] Weijie Xu et al., “Technical Report on support of AMP IoT devices in WLAN,” IEEE 802.11 submission 11-23/0436r0
[3] Xiaogang Chen et al., “Low Power Listening Mode,” IEEE 802.11 submission 11-22/1414r1
[4] GS1, “EPC Radio-Frequency Identity Protocols Generation-2 UHF RFID Standard,” Release 2.1, Jul., 2018