## Slide 1: Discussion of Existing Technologies and Technical Challenges in AMP
Date: 2023-05-13
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Doc.: IEEE 802.11-23/0836r0
May 2023

## Slide 2: Abstract
The purpose of this presentation is to summarize existing technologies that can be reused and further enhanced, and identify some main technical challenges in AMP.
Doc.: IEEE 802.11-23/0836r0

## Slide 3
PHY
    Low complexity waveform: OOK to reduce the complexity of the receiver
    Narrower channel bandwidth:
      Reduce power consumption and complexity
      Adapt to the scarcity of available frequency bands for S1G, e.g., 802.11ah
      Legacy preamble with 20MHz for co-existing, e.g., 802.11ba
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-23/0836r0
May 2023

## Slide 4
MAC (1/2)
    Shortened Frames
      Motivation: reduce power consumption for transmission and reception of the frames
      Shortened MAC headers
      Beacon frames and NDP frames
    Grouping
      Motivation: Limit the number of stations accessing the channel with station grouping based on position
      The AP divides the space into several spatial sectors and divides the time into Sector Intervals accordingly
      A group of stations can only access the channel in their own sector interval.
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-23/0836r0
May 2023

## Slide 5
MAC (2/2)
    Target Wake Time (TWT)
      Motivation: reduce contention and the TWT station can stay in the doze state for longer time to reduce power consumption
      A device can negotiate with the AP to specify the duration and frequency of its wake-up intervals.
      During these intervals, the device can transmit and receive data as needed, and then go back to sleep until the next scheduled wake-up time.
    Restricted Access Window (RAW)
      Motivation: decrease collision probability with thousands of stations and thus to improve power efficiency
      A time interval during which a device is not allowed to transmit or receive data.
      During a Restricted Access Window, a device must remain silent and can only listen to the wireless medium for incoming transmissions.
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-23/0836r0
May 2023

## Slide 6
Main Technical Challenges (1/2)
Channelization
  Regulation issue in China and EU
  Technical issues
    More channels, e.g., 20 channels for S1G in China
    Narrower BW, e.g., 250kHz for S1G in China
Frequency hopping
  Mandatory hopping in China and EU
  Technical issues
    Hopping pattern
    Beacon hopping: static beacon
    Discovery with FH: static discovery
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-23/0836r0
May 2023

## Slide 7
Main Technical Challenges (1/2)
Preamble
  Co-existence with legacy 802.11ah, especially in UL
  Technical issues
    How to create OFDM preamble? Pseudo- preamble, TXOP without preamble
    OOK Preamble with ED
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-23/0836r0
May 2023

## Slide 8: Summary
Review of existing technology that can be reused or further enhanced for AMP
Identify the main technical challenges
Doc.: IEEE 802.11-23/0836r0