## Slide 1: ETSI TC BRAN news
Date: 2023-05-16
Authors:

## Slide 2: Work Items (WIs) under development [1]
EN 301 893 (5 GHz)
  Document ready
  Final discussions regarding Energy Detection Threshold (EDT) description
EN 303 687 (6 GHz)
  In EN Approval Procedure (ENAP)
  ENAP closes 2023-06-27
EN 303 753 (60 GHz)
  ENAP & Harmonised Standard Technical Advisory Consultant (HASTAC) review requested
EN 302 502 (5.8 GHz)
  Broadband Fixed Wireless Access
  Inactive since 2019
TR 103 721 (5.8 GHz coexistence)
  To be published by ETSI

## Slide 3: Relevance to IEEE 802.11
Target
EN 303 687 & revised EN 301 893 listed as Harmonized Standards (HSs) in the Official Journal of the EU (OJEU)
  Once in OJEU, manufacturers may use these HSs to self-assess products
Current version of EN 301 893 does not consider any 5 GHz PHY beyond IEEE 802.11ac
  Today, products implementing commonplace features of IEEE 802.11ax and beyond require notified body approval
In Europe, 5945 MHz to 6425 MHz available for license-exempt operation
  IEEE 802.11 products dependent on notified body approval until EN 303 687 in OJEU

## Slide 4: ETSI TC BRAN activities since ETSI TC BRAN plenary #118
ETSI TC BRAN conducted two ad hoc meetings (#118a and #118b)
  Open schedule
  A third to follow, next week
Ad hoc meeting #118a mostly discussed plans at ECC/CEPT for updated receiver requirements
  Might impact requirements in Harmonized Standards
  Also discussions in other ETSI groups (ERM TG11 etc.)
Ad hoc meeting #118b discussed concerns about EDT requirements
  On the one hand, there are concerns about “loopholes”
  On the other hand, there are concerns about operation at bandwidth larger than 20 MHz and at the cell edge
  Waiting for compromise

## Slide 5: Upcoming meetings
ETSI TC BRAN plenary #119
  2023-06-12 until 2023-06-16
ETSI TC BRAN plenary #120
  2023-09-18 until 2023-09-22
ETSI TC BRAN plenary #121
  2023-10-23 until 2023-10-27
ETSI TC BRAN plenary #122
  2023-12-11 until 2023-12-15
Meetings scheduled until end of 2024
Proposal for meeting dates for the years 2025, 2026, and 2027 to be discussed during BRAN #119
  See BRAN(23)118005r1

## Slide 6: References
ETSI, “Work Programme,” accessed 2023-05-16. [Online]. Available: https://portal.etsi.org/tb.aspx?tbid=287&SubTB=287#/50611-work-programme