## Slide 1: Efficient Coordinated Spatial Reuse
Date: 2023-09-11
Authors:

## Slide 2: Abstract
Coordinated Spatial Reuse (C-SR) is one of the Multi-AP transmission techniques that is being considered for UHR.
C-SR only requires RSSI or pathloss feedback as opposed to complete CSI between all APs and STAs.
C-SR can be implemented using the protocols used for CBF and JT [1],[2].
A unified multi-AP protocol is preferred but may not be the most efficient especially for C-SR.
In this contribution, we propose an efficient protocol for C-SR.

## Slide 3: General Procedure for C-SR
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
Interference Measurement
Phase
Interference measurement phase
  The sharing/shared APs measure interference or pathloss to each other’s target STA.
Transmission phase
  Initiated by the sharing AP. The sharing AP controls the transmit power and MCS of the shared APs.
Transmission Phase

## Slide 4: Shared AP Transmit Power and MCS
During the transmission phase, we assume that AP1 first decides its own transmit power and MCS. Based on these decisions, it computes the transmit power and MCS of the shared AP.
Transmit power of AP2- AP2 transmit power depends on the interference from AP2 to STA1 (X2).
MCS of AP2- The sharing AP (AP1) may indicate a maximum MCS of the shared AP. The MCS depends on the interference from AP1 to STA2 (X1).
Problem: While X1 can be measured directly by AP1, X2 needs to be obtained from either AP2 or STA1.

## Slide 5: Interference Measurement Phase and Feedback Collection
MAP
TF
AP1
(sharing AP)
NDPA
NDPA
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
NDP
NDP
BFRP
There are two options to obtain X1 and X2. Both options require the same number of steps.
For option 2, only X2 needs to be transferred (marginally more efficient).
We prefer a way where neither X1 nor X2 needs to be transferred, i.e. eliminate final BFRP-BFR exchange.
measure X2
BFR
X2
BFR
X1
Option1
MAP
TF
AP1
(sharing AP)
NDPA*
NDPA*
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
NDP
NDP
BFRP
measure X2
measure X1
BFR
X2
measure X1
Option 1
Option 2

## Slide 6: Proposed C-SR transmission method
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
MAP
TF
DL Data Frame
DL Data Frame
BA
BA
MCS,ARIL
We propose that the MAP TF does not directly indicate TP for the shared AP.
Instead, the MAP TF indicate an acceptable interference level (ARIL) parameter.
The shared AP can determine its transmit power based on the ARIL and its own measured X2.
Works well with Option 2 of Interference Measurement Phase. How to apply the same concept for Option 1 interference measurement phase is TBD.
MAP
TF
NDPA*
NDPA*
NDP
NDP
measure X2
measure X1
TP=f(X2,ARIL)
Interference Measurement
Phase (Option 2)
Transmission Phase

## Slide 7: Example
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
MAP
TF
DL Data Frame
DL Data Frame
BA
BA
ARIL=-80 dBm
MAP
TF
NDPA*
NDPA*
NDP
NDP
X2 = -70 dBm
TP=ARIL+20-X2= 10 dBm
20 dBm
AP2 – STA1 Pathloss =90 dB
MCS, ARIL
IL = -80 dBm
The example shows how the sharing AP can control the interference of the shared AP without directly indicating the transmit power.
The transmit power of the PPDU (NDP) where X2 was measured needs to be known by AP2. How to signal this is TBD.

## Slide 8: Benefits of the proposed CSR method
Very low overhead.
Simple implementation – very similar to PSR-based SR transmit power determination.
Distributed processing. Allow shared APs to compute parameters by themselves to reduce interference measurement procedure overhead.

## Slide 9: Conclusion
We discussed a way to reduce the overhead of CSR by simply changing the transmit power signaling by the Sharing AP to the Shared AP.
The proposed method may require a specific interference measurement procedure to achieve the most gain.

## Slide 10: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1097-00-00be-sounding-procedure-in-ap-collaboration.pptx
[2] https://mentor.ieee.org/802.11/dcn/19/11-19-1134-01-00be-consideration-of-multi-ap-sounding.pptx