## Slide 1: Announcement for R-TWT Coordination
Date: 2023-08-07
Authors:
Name | Affiliation | Address | Phone | Email
SunHee Baek | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | sunhee.baek@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
DongJu Cha |  |  |  | dongju.cha@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10225 Willow Creek Rd, San Diego, CA, USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
The previous contribution[1] shared the protection for R-TWT service periods in the Multi-BSS environment.
  There are some limitations of R-TWT defined in 11be during the exchange of the latency sensitive traffic in several adjacent BSSs.
  There is no way to coordinate the R-TWT service periods(SPs) of each BSS in Multi-BSS.
Some contributions, [2] ~ [7], presented methods for coordination of R-TWT SPs in Multi-BSS based on Multi-AP scenarios, AP coordination schemes(e.g., C-TDMA, C-OFDMA, C-SR), etc.
In this contribution, we share which OBSS R-TWT SP should be announced in Multi-BSS.
  The R-TWT SP scheduled by the neighboring APs named OBSS R-TWT SP in this contribution.

## Slide 3: Overview
Announcement of OBSS R-TWT schedule information to associated STAs would be helpful for the reasons below;
  To protect the intended SPs within each BSS.
    For example, if OBSS occupies channels in a BSS, a STA in the BSS may fail to obtain its TXOP because the channel can be busy during its service period.
    For example, if interference occurs between neighboring AP and AP, the UL/DL transmissions fail.
However, the AP should not announce all OBSS R-TWT schedule information to associated STAs. The unnecessary announcement causes overprotection to the STAs and beacon bloating.
We consider which OBSS R-TWT SP should be announced by AP and protected by associated STAs in this contribution.

## Slide 4: Announcement of OBSS R-TWT SPs
The R-TWT SPs can be classified as follows depending on whether the SPs are coordinated(adjusted) between APs.
  Coordinated R-TWT SP
    The coordinated R-TWT SPs are the shared/agreed SPs to schedule R-TWT SP between APs.
      The coordination between APs can be through wireless or wired communication.
    Also, the coordinated R-TWT SPs may be assigned by a central(/management) entity of APs.
  Non-Coordinated R-TWT SP
    The non-coordinated R-TWT SPs aren’t the shared/agreed SPs to schedule R-TWT SP between APs.
      For example, it can be the schedule information of OBSS R-TWT SP in an overhearing beacon frame.
Announcement of the coordinated R-TWT SPs to associated STAs would be helpful to protect the associated STA’s SPs and OBSS R-TWT SPs.
  In this contribution, we share the considerations of the announcement of the coordinated R-TWT SP from an overlapped/non-overlapped point of view.

## Slide 5: Announcement of Overlapped Coordinated R-TWT SPs
Overlapped Coordinated R-TWT SPs can be considered as one of the coordinated R-TWT SP types.
  For example, each AP can have the same R-TWT schedules in which the APs can operate the SPs based on AP coordination schemes(e.g., C-TDMA/C-OFDMA/C-SR).
    In this case, the TWT interval and TWT SP duration can be negotiated to set the same values, but TWT(target wake time) should be negotiated by considering different TSF of each AP.
It is expected that each AP would announce the Overlapped Coordinated BSS’s SPs as the schedule in its BSS, not OBSS.
  The associated EHT/UHR STAs supporting (enhanced) R-TWT will follow the protection rules or participate in the SP to transmit/receive UL/DL low latency traffic.
Overlapped Coordinated R-TWT SP scheduled by AP 1 and AP 2
The STA associated with AP 1 will end its TXOP.
The STA associated with AP 2 will end its TXOP.

## Slide 6: Announcement of Non-overlapped Coordinated R-TWT SPs
Non-overlapped coordinated R-TWT SPs are the coordinated R-TWT SPs scheduled so that there is no overlap between them by APs.
  For example, each R-TWT SP is mainly operated in each BSS and the APs may operate the SPs based on AP coordination schemes(e.g., C-TDMA/C-OFDMA/C-SR).
The AP announces the schedule information of the non-overlapped coordinated OBSS R-TWT SPs and non-overlapped coordinated R-TWT SPs.
  Also, AP can indicate whether the associated STAs follow the protection rule of R-TWT SP for OBSS as mandatory or conditionally mandatory based on additional information about the OBSS R-TWT SP(s).
    We can discuss the additional information which expects to enable to exchange frames in a BSS without the impact on OBSS, i.e., enable to ignore the protection rule (e.g., power level).
  So, the associated STAs will end their TXOP before the start time of non-overlapped coordinated R-TWT SPs, and may end their TXOP before the start time of non-overlapped OBSS coordinated R-TWT SPs.
    The EHT/UHR STAs supporting R-TWT may end their TXOP before the start time of non-overlapped OBSS coordinated R-TWT SPs depending on how associated AP consists of the announcement about the SPs.
Non-Overlapped Coordinated R-TWT SP scheduled by AP 1
Non-Overlapped Coordinated R-TWT SP scheduled by AP 2
The STA associated with AP 1 will end its TXOP.
The STA associated with AP 2 will/may end its TXOP.
The STA associated with AP 2 will end its TXOP.
The STA associated with AP 1 will/may end its TXOP.

## Slide 7: Announcement of Non-Coordinated R-TWT SPs
The APs may announce the non-coordinated R-TWT SPs to associated STAs.
  The non-coordinated R-TWT SPs can be the OBSS R-TWT SPs noticed through overhearing Beacon frame.
  We assume that the announcement of non-coordinated R-TWT SP doesn’t give any advantage to the associated STAs because they should protect the OBSS R-TWT SP whenever receiving it.
  Also, when an AP announces the non-coordinated OBSS R-TWT SP but the neighboring AP doesn’t announce it, the associated STAs could not do anything during the OBSS SPs.
APs may use the schedule information of non-coordinated R-TWT without announcing the OBSS R-TWT SPs to the associated STAs.
  For example, an AP uses it to schedule R-TWT SPs not to overlap with the OBSS R-TWT SPs.
  When the associated STAs overhear the Beacon frame announced by neighboring AP, the STAs can request R-TWT not to overlap with the OBSS R-TWT SP.
    Also, the STAs can share whether the requested R-TWT SPs don’t overlap with the OBSS R-TWT SPs to the associated AP.

## Slide 8: Summary
In this contribution, we have shared which OBSS R-TWT SP should be announced from AP and protected by associated STAs.
  Coordinated R-TWT SP
    Overlapped Coordinated R-TWT SP
    Non-overlapped Coordinated R-TWT SP
  Non-Coordinated R-TWT SP
We discussed the announcement and protection of the schedule information based on the above classified R-TWT SP in terms of AP and the associated STAs.

## Slide 9: References
[1] 23/771 Coordinated of R-TWT Protection in Multi-BSS
  [2] 23/226 Coordination of R-TWT for Multi-AP Deployment
  [3] 23/250 AP coordination with R-TWT
[4] 23/291 R-TWT Multi-AP Coordination
[5] 23/293 Follow-up on TWT-based Multi-AP Coordination
[6] 23/297 rTWT for Multi-AP
[7] 23/355 Enhanced R-TWT and M-AP operation