## Slide 1: Low Power and Long Range Preamble
June 2023
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Malcolm Smith | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 

## Slide 2: A Low Power Listening Mode was proposed in 22/1414 and 22/1841 …
Hart et al (Cisco Systems)
The initial frame provides flexibility for implementation on the listening operation.
Different implementations can choose their preferred alternative to leverage the initial frame and trade off.
Client only has its lower-power mode radio awake (low MCS-capable, 1SS)
RTS/Trigger indicates the recipient and lists many PHY parameters (NSS, bandwidth, MCS)
Based on RTS/Trigger, client can wake up and tune the resources needed for its high-power radio

## Slide 3: … yet this seems inefficient
Hart et al (Cisco Systems)
This is a Trigger frame sent before transmitting on the downlink
The NSS, MCS and BW fields are already signaled in the preamble of the main PPDU – so this is sending SIG info duplicates
Is there a more efficient option that allows for just CTS2self, or no MAC protection at all?
For context:
    Signalable eMLSR transition delays are 0/16/32/64/128/256 usec
    CTS2self at non-HT/MCS0 is 60 usec
    RTS + SIFS + CTS + SIFS at non-HT/MCS0 is 128 usec long; then “UHR-SIG” info adds a further N*4 usec.

## Slide 4: Proposal: Preamble Extension
Hart et al (Cisco Systems)
A Preamble Extension field is inserted between:
      Signaling of recipient(s) and their NSS(s), BW(s) and MCS(s) (etc)
      When that signaling is utilized
The minimum duration of the Preamble Extension field needed by the recipient is negotiated with it
An indication of the duration of the Preamble Extension field is provided in an earlier field (e.g., USIG)
LSTF
LLTF
LSIG
R-LSIG
USIG
UHR SIG
Preamble Extension
UHR STF
UHR LTF
Data
PE
Padding used to wake up hi-capability RX
Single copy of SIG parameters
Hi-capability receiver finishes processing the PPDU
Lo-capability receiver initially processes the PPDU
Signaling of Preamble Extension field duration
Alternative location for Preamble Extension

## Slide 5: Contents of Preamble Extension
Hart et al (Cisco Systems)
Four natural options for the contents of the Preamble Extension field:
      Extended UHR STF
        Simplest
      Repeated USIG and UHR SIG
        Also enables longer range if the entire Preamble Extension is not required to wake up the hi-capability receiver
      Repeated UHR LTF (and move Preamble Extension field after UHR STF)
        Also enables improved channel estimation and interference suppression if the entire Preamble Extension is not required to wake up the hi-capability receiver
      Some mix of these options
LSTF
LLTF
LSIG
R-LSIG
USIG
UHR SIG
UHR STF
UHR LTF
Data
PE
R-UHR STF
R-USIG
R-UHR SIG
UHR STF
R-UHR LTF
Assume UHR picks one of these options

## Slide 6: Summary
Hart et al (Cisco Systems)
We propose an extended preamble for power savings
When the preamble is extended via a repeated U-SIG and repeated UHR-SIG, the preamble can also provide for long range operation.
Especially when a hi-capability receiver can be woken up relatively quickly, the extended preamble provides greater efficiency than a Trigger frame sent before transmitting on the downlink