## Slide 1: CFO Impact and Pilot Design for dRU
Date: 2023-07-09
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
To overcome PSD limitations which are defined per 1 MHz, dRU was introduced in [1]
We presented our view on dRU design ways for a tone plan, pilot and signaling in [2]
In this contribution, we compare the pilot design methods introduced in [2] and investigate performance considering various values of residual CFO
We also provide rRU performance as a baseline

## Slide 3: Pilot Design (1/2)
Option 1: define new pilot position
  In order to build a 26-tone dRU, 26 distributed tones are allocated and then two tones among them are selected as pilot tones
    E.g., the 7th and 20th tones in each 26-tone dRU can be determined as the pilot tones similar to the middle 26-tone rRU in 20 MHz
  For dRUs larger than 26, we can simply define data and pilot tones based on 26-tone dRUs or pilot tones can be changed for a better performance
    We are open and need further study
…
…
…
…
…
…
…
…
…
…
1st tone
6th tone
7th tone
19th tone
20th tone
26th tone
Data tones
Pilot tones

## Slide 4: Pilot Design (2/2)
Option 2: maintain conventional pilot position
  In order to build a 26-tone dRU, 24 distributed tones are allocated as data tones and then two tones among the conventional pilot tones are additionally allotted as pilot tones
    One possible approach to select two pilot tones is considering the mapping rule between rRU and dRU as shown in [3], i.e., pilot tones for an rRU corresponding to a certain dRU can be allocated to the dRU as pilot tones
  For dRUs larger than 26, we can simply define data and pilot tones based on 26-tone dRUs and in this approach the conventional pilot position can be still maintained
…
…
…
…
…
…
…
…
…
…
1st tone
6th tone
7th tone
19th tone
20th tone
24th tone
Data tones
Pilot tones selected out of the conventional pilot tones

## Slide 5: Performance Comparison (1/3)
We investigate PER performance for two options considering various residual CFO values
  Performance for rRU is also provided
Assumptions
  20 MHz UL TB PPDU with nine 26-tone dRUs / nine 26-tone rRUs
  SISO with Channel D NLoS
  1000 data bits per each STA
  MCS 0/3/5/8 with LDPC coding
  Residual CFO for each STA: [+rCFO –rCFO +rCFO –rCFO …]
    Different rCFO values are considered depending on the MCS level
  Pilot position for dRU
    Option 1: 7th and 20th tones in each 26-tone dRU
    Option 2: pilot tones of x-th 26-tone rRU for x-th 26-tone dRU
  PERs for the first 26-tone dRU and first 26-tone rRU are provided

## Slide 6: Performance Comparison (2/3)
Simulation results
  MCS 3
    When there is no residual CFO (rCFO = 0 Hz), dRU provides a significant performance gain
    dRU has a wider performance gap between with and without a residual CFO
      dRU still outperforms rRU even though a certain residual CFO is present
    Option 1 offers better performance than option 2 when rCFO > 0 Hz
PERs for MCS 0 / 5 / 8 are shown in Appendix and the trend is similar

## Slide 7: Performance Comparison (3/3)
When there is no residual CFO, dRU achieves quite better performance than rRU, no matter what the pilot option is
  That is because dRU can obtain a significant frequency diversity gain
As a residual CFO increases, dRU performance deteriorates much faster
  That is because dRU is more vulnerable to the residual CFO
  However, its performance is still better than that of rRU
In addition, thanks to the higher transmit power for dRU, dRU performance can be further enhanced
Option 1 provides better performance than option 2
  That is because option 1 may produce more appropriate pilot position compared to the approach employed in option 2
  Note that there is still a room to improve the performance for option 2, and we can come up with a better approach on how to select two pilot tones out of the conventional ones

## Slide 8: Conclusion
We have introduced two pilot options for dRU
  Option 1: define new pilot tone indices
  Option 2: maintain conventional pilot tone indices
We have also shown various simulation results for both options comparing with rRU
We have confirmed that dRU with well-designed pilot tones can outperform rRU regardless of the amount of a residual CFO and the higher transmit power can further enhance the dRU performance
Option 1 is better in terms of the performance while option 2 may be less complex and can be further improved
  We need a further study on how to improve the performance for option 2

## Slide 9: References
[1] 11-23-0037-00-0uhr-uhr-feature-to-overcome-psd-limitations-distributed-tone-resource-units
[2] 11-23-0281-00-0uhr-considerations-on-ru-mru-designs-for-uhr
[3] 11-23-1117-00-0uhr-dru-signaling-for-uhr

## Slide 10: Appendix
Simulation results
  MCS 0
    The performance for option 1 is quite bad when rCFO = 1 KHz

## Slide 11: Appendix
Simulation results
  MCS 5
    Trend is similar

## Slide 12: Appendix
Simulation results
  MCS 8
    When rCFO = 200 Hz, it seems that all of the cases cannot achieve 10 % PER