## Slide 1: Features to consider for efficient Relay operation
Date: 2023-07-07
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St San Diego, CA 92131 |  | sanggook.kim@lge.com
July. 2023

## Slide 2: Introduction
As described in [1,2], Relay operation in UHR is able to provide the improvement of reliability as well as throughput in terms of RvR.
To achieve this improvement or benefit from the Relay operation, we should consider the following.
  The selection of appropriate non-AP STA for relay operation
  The information of channel between Relay STA and Non-AP STA(s)
In this contribution, we take into account the ways for two considerations addressed above.

## Slide 3: Selection of non-AP STA(s) (1/3)
Generally, Relay operation can be applied to non-AP STA(s) that are located far from AP and have a poor signal reception from AP.
  AP can recognize the non-AP STA’s status throughout the frame exchanges in a BSS.
  In spite of the non-AP STA satisfies the above condition, if it does not locate near Relay STA, we can’t adapt the relay operation to this STA.
Therefore, we should need to identify whether those STAs are located near the Relay STA.
  In addition, since either the associated non-AP STA or Relay STA can have mobility in a BSS, a non-AP STA near relay STA may be changed.
  So, it is required the periodic check of the existence of non-AP STA near Relay STA.
AP
Relay STA
Non-AP STA1
Non-AP STA2
Non-AP STA3
Non-AP STA4
Non-AP STA5

## Slide 4: Selection of non-AP STA(s) (2/3)
To select the appropriate associated non-AP STA, we can consider the following procedure.
  To confirm which associated non-AP STA that has a weak reception is suitable for relay operation, AP transmits the Triggering frame to the Relay STA and the non-AP STA(s).
    As a triggering frame, a newly designed trigger frame may be taken into account and both the non-AP STA(s) and Relay STA can recognize the starting of this procedure as the reception of this frame.
      It may be composed of the user field addressed to the non-AP STA that AP wants to check as well as the user field for the Relay STA.
        After the Relay STA receives the trigger frame from the AP, it acts as a recipient.
  The non-AP STA(s) addressed by the triggering frame sends the signal to the allocated BW/RU.
    Since the purpose of signal transmission is the detection of non-AP STA, the corresponding signal may not include a data field.

## Slide 5: Selection of non-AP STA(s) (3/3)
  AP can identify the non-AP STA(s) near Relay STA with the neighbor non-AP STA report transmitted by Relay STA.
    The neighbor non-AP STA report may be composed with follows
      AID of the non-AP STA
      The received signal power, for example, RSSI.
AP
Relay STA
Non-AP STA(s)
UL PPDU
SIFS
Neighbor non-AP STA report
SIFS
Triggering frame
Performing detection
Report Request
SIFS

## Slide 6: Channel information between Relay STA and non-AP STA(s) (1/3)
To provide the improved QoS (i.e., reliability and throughput) in Relay operation, the channel information between Relay STA and non-AP STA(s) should be measured.
  However, since the Relay STA locates between AP and non-AP STA, AP can’t figure out the channel information between Relay STA and non-AP STA (i.e., Relay link).
  So, we should consider ways to measure the channel information of the Relay link.
    In addition, the channel information is used to determine the appropriate transmit parameters for Relay links such as MCS, BW, etc.
In the next slides, we describe the procedure of channel estimation for a Relay link led by an AP.
AP1
STAn
STA1
AP link
Relay link
Relay STA

## Slide 7: Channel information between Relay STA and non-AP STA(s) (2/3)
DL sounding for the channel between Relay STA
  AP sends a triggering frame to both Relay STA and non-AP STA(s) to initiate the sounding of the Relay link.
    The triggering frame can be composed with the following information.
      For example, DL/UL indication, Transmitter/receiver, BW, RU allocation, Nss, etc.
  The Relay STA sends a sounding PPDU to the non-AP STA(s).
    Regarding the sounding PPDU, for example, an NDP may be used.
  AP and non-AP STA exchange the report request and feedback frame.
AP
Relay STA
Non-AP STA(s)
SIFS
Sounding PPDU
SIFS
Feedback
SIFS
Triggering of channel estimation for Relay link
Report request

## Slide 8: Channel information between Relay STA and non-AP STA(s) (3/3)
UL sounding for the channel between Relay STA
  It is similar to the DL case described in the previous slide.
  However, after receiving the triggering frame from the AP, the STA transmits the sounding PPDU to relay STA on the allocated BW/RU.
    The roles of transmitter and receiver for Relay STA and non-AP STA(s) are set contrary to DL.
    Regarding the sounding PPDU used in UL sounding, we need to discuss the ways how to define it.
      As an example, we can consider the PPDU format such as TB ranging NDP defined in 11az.
  Regarding the feedback, we need further consideration to apply the various UL transmission schemes into the Relay operation.
AP
Relay STA
Non-AP STA(s)
SIFS
Sounding PPDU
SIFS
Feedback
SIFS
Triggering of channel estimation for Relay link
Report request

## Slide 9: Summary
In this contribution, we introduced the two features that needed to be considered in the Relay operation to provide improved reliability and throughput in perspective RvR.
  The selection of non-AP STA(s) for relay operation
    The efficiency of Relay operation can be maximized by selecting the non-AP STA(s) suitable (i.e., the signal reception from AP is poor and there is a Relay STA nearby) for Relay operation.
  The information on the channel between Relay STA and Non-AP STA(s)
    The optimal parameters for transmission between Relay STA and non-AP STA(s) can be set by accurately identifying the channel status between Relay STA and non-AP STA(s).

## Slide 10: Reference
[1] 11-23-0042-00-0uhr-Thought for Range Extension in UHR
[2] 11-22-1908-00-0uhr-UHR rate-vs-range enhancement with relay