## Slide 1: Considerations for AMP Devices
Date: 2023-07-10
Authors:

## Slide 2: Abstract
We present an analysis for several limitations that should be considered when designing a standard for an ultra-low power and low-complexity energy harvesting based AMP-STAs
These are not physical or mathematical limitations, but rather some common, current technology features that were found by our analysis with significance to AMP-STAs
We suggest to take such analysis into consideration when chosing between several options for the AMP standard

## Slide 3: Ambient Power STAs Have Small Energy Reserves
For AMP-STAs, energy is extremely limited
  Very small battery (e.g. printed 30-80mAh)
  Scarce light conditions (PV within building or on a very cloudy day)
  Small capacitor for RF energy harvester (nJ-uJ)
An example of a transmission of 30us with EIRP=-10dBm:
  The energy spread to the air = 3nJ
  Actual devices are usually less efficient and energy consumption of 30nJ is reasonable
AMP-STAs are ultra-low complexity as well as ultra-low power
  In order to fit cost and size of sticker form factor, requirements for several external components should be limited
  This is especially true for external components that consumes energy

## Slide 4: Impact of Clock Generation for an Active Transmitter AMP-STA
For active transmitter AMP-STAs, we would like to reduce the need for a stable clock with accuracies in the orders of 40ppm
Stable crystal-based clocks usually consume non-neglectable power and also take some time to turn on, until reaching stability
In addition, they require an external component on top of the silicon chip. This increases the bill of matrial (BOM) of the product and also limits massive deployments with a sticker form factor
Depending on exact system design, it is possible to use a simpler, lower power, internal oscilators [1-3]. Such oscilators are usually characterized with lower clock accuracies. However, by using various low power calibrations, they can reach an accuracy of 1000ppm
We recommend to reduce the clock accuracy required from an AMP-STA to 1000ppm
The AMP-AP clock accuracy can still hold the 802.11-2020 clock accuracy requirement – as it is not required to be ultra-low complexity or ultra-low power

## Slide 5: Impact of Memory Retention
AMP-STAs are required to support energy harvesting power delivery.
This means these devices are not always powered on, and most of the time are either powered off or work on the remaining energy from last energizing
One of the biggest energy cosuming blocks is the memory.
While on dynamic power regime, the memory power consumption is comaparable to the rest of the circuitry operating within the AMP-STA.
But while staying non-active/standby (meaning no transmit or receive) any requirement to retain memory values is energetically expensive - especially if this is required for long times [4].
Various SRAM technologies with low retension power consumption exist, but between 20-200fW/bit are achievable in commercial products.
So, holding 1Kbyte for 1 minute takes 10nJ, which is comparable to the transmission energy.

## Slide 6: Impact of Non-Volatile Memory
An alternative to retaining memory is the use of a non-volatile memories.
One such component is OTP, which allows for a device to write once, and then read multiple times.
This component can be integrated into the Si, without the need to increase complexity of end-device.
Between the write and the read there is no need for energizing, and the written values stay written without any energy consumption.
However, it is basically a one-time write, so multiple writes can be done only a few predetermined times.
Our analysis revealed that such component can consume as much as 50-500uJ per writing of 32 bits. This is orders of magnitude more energy compared to the energy used by the transmission.

## Slide 7: Impact of Idle/Wait Times
While the AMP-STA is non-active, during either idle or wait times, it is desirable that the device will consume the minimum amount of energy possible.
Since these times can be much longer than active times (depending on the system architecture), the power cosumption during these times is non-neglegable.
For Example, by using a lower accuracy clock, we can minimize energy consumption. This clock can be used for either operating a low power receiver (WUR) or as a synchronizer for waking up.
Our analysis suggests that such clock can operate with an accuracy of 10,000ppm for a 100KHz clock [2].

## Slide 8: Summary
An analysis for few possible limitations for AMP-STAs was presented
Only mainstream technology was analyzed on each of the suggested parameters, so these limitations can be further updated
We suggest to consider these limitations when compering between different options for adoption in the standard
By limiting the requirements from an AMP-STA according to the analysis, AMP-STAs can reach lower cost and be based on energy harvesting.
Additionally, it will provide significant diffrentiation from devices implementing other existing low power standards.

## Slide 9: References
  Wheeler et. al., “Crystal-Free Narrow-Band Radios for Low-Cost IoT,” 2017 IEEE Radio Frequency Integrated Circuits Symposium.
  Jiang et al, “A 0.4-V 0.93-nW/kHz Relaxation Oscillator Exploiting Comparator Temperature-Dependent Delay to Achieve 94-ppm/°C Stability,” IEEE JOURNAL OF SOLID-STATE CIRCUITS, VOL. 53, NO. 10, OCTOBER 2018
  McCorquodale et al, “A 25-MHz Self-Referenced Solid-State Frequency Source Suitable for XO-Replacement,” IEEE TRANSACTIONS ON CIRCUITS AND SYSTEMS—I: REGULAR PAPERS, VOL. 56, NO. 5, MAY 2009
  J. Kwong, et al, “A 65 nm sub-Vt microcontroller with integrated SRAM and switched-capacitor DC-DC converter,” in IEEE Int. Solid-State Circuits Conf. (ISSCC) Dig. Tech. Papers, 2008, pp. 318–319.