## Slide 1: Smooth Beamforming with Feedback Overhead Reduction
Date: 2023-08-28
Authors:
Name | Affiliation | Address | Phone | Email
Insik Jung | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insik0618.jung@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
Smooth beamforming enables obtaining smoothing gain at the receiver side when beamforming is applied [1]-[6].
Previous works [1]-[6] propose to conduct V matrix optimization to resolve the discontinuity of the estimated channel
In this contribution, we propose a method to reduce additional feedback overhead to deliver the optimized phase rotations for V matrix

## Slide 3: Recap: V matrix Optimization
It is shown in [4] that optimized column-wise phase shift resolves discontinuity of beam-steering matrices among adjacent tones
Resolving discontinuity results in obtaining channel smoothing gain at the receiver side
Discontinuty has been resolved after V matrix optimization

## Slide 4: Beamformer Side Optimization
Channel estimation (BFee)
  Estimate of the channel matrix H
  H=U VH
Feedback (BFee)
  Feedback of VD, where D is the diagonal matrix to make last row of V to be real values
Optimization (BFer)
  BFer optimizes D* using VD
Beamforming (BFer)
  BFer conducts VDD* beamforming
 No additional signaling
BFer
BFee
NDPA
NDP
Compressed beamforming feedback
data PPDU
Estimation of H
D* optimization

## Slide 5: Beamformee Side Optimization
Channel estimation (BFee)
  Estimate of the channel matrix H
  H=U VH
Optimization (BFee)
  STA optimizes D* using VD
Feedback (BFee)
  Feedback of VD, where D is the diagonal matrix to make last row of V to be real values
  Additional feedback of D*
Beamforming (BFer)
  AP conducts VDD* beamforming
BFer
BFee
NDPA
NDP
Compressed beamforming feedback
data PPDU
-Estimation of H
-D* optimization

## Slide 6: Comparison: BFer and BFee side
FER of BFer-side and BFee-side optimization is almost same
If BFer has optimization capability, we observed that BFer side optimization might be advantageous than BFee-side optimization in terms of throughput.
Parameters | Values
Ng | 4
MCS | 7
BW | 40MHz
MIMO configuration | 4 by 2

## Slide 7: Possible Scenarios
Scenario 1: BFer has an optimization capability
  BFer side optimization might be a better option in terms of throughput
Scenario 2: BFer doesn’t have an optimization capability
  If BFer is a non-AP STA, it may not have optimization capability because of the computation cost
  In this scenario, BFee may conduct optimization instead of BFer and feedback the optimization result to the BFer. For example, it might be conducted in UL SU MIMO
In our contribution, we propose a overhead reduction method for Scenario 2.

## Slide 8: Part-of-tone Optimization
Notice that discontinuity on euclidean distance happens intermittently.
  Then, we don’t have to optimize every tones
Proposal
  Just optimize for the tones from the first discontinuity
    We may set threshold value to detect the first discontinuity
  Only feedback D* for the optimized tones
Benefit
  Reduction of feedback overhead for D*
First discontinuity happens in the tone index n
We don’t have to optimize these tones
threshold
The first discontinuity based on the threshold

## Slide 9: Simulation Settings
General parameters
  BW = 40MHz
  MCS = 7
Antenna configuration
  4 by 2
Quantization
  (Phi, psi) = (6,4) bits
Channel model
  TGnD, NLoS
Receiver option
  LMMSE receiver
  LS channel estimation

## Slide 10: Simulation Results
Baseline: w/o optimization
Option 1: Full tone optimization
Option 2: Part of tone optimization
  Option 2-1) Threshold = 1.2
  Option 2-2) Threshold = 0.8
  Option 2-3) Threshold = 0.4
 | Option 1 | Option 2-1 | Option 2-2 | Option 2-3
Additional bits | 1464 | 801.6 (45.2% reduction) | 1106.6 (24.4% reduction) | 1357.7 (7.2% reduction)
Compare w/ baseline | 24% increased | 13.1% increased | 18.14% increased | 22.3% increased
[Overhead analysis]
[FER]
Note: # of additional indication bits (e.g. optimization starting tone index) has been considered as 9 bits (which can be 12 bits for 320MHz BW)
Notes: FB bits for compressed beamforming FB: 122 (FB tones) * 10 (# of angles) * 5 (avg. quantization bits)

## Slide 11: Conclusion
In this contribution, the part of tone optimization and feedback method has been proposed.
The simulation results has shown that proposed method reduces feedback overhead without significant FER loss.

## Slide 12: References
[1] 11-05-1635-01-000n-wwise-preambles-and-mimo-tx-beamforming
[2] 11-22-1392-00-0uhr-beamforming-improvement-for-uhr
[3] 11-22-1820-01-0uhr-bf-feedback-with-the-optimal-svd
[4] 11-22-1842-00-0uhr-channel-information-feedback-for-smooth-beamforming
[5] 11-22-1869-01-0uhr-txbf-based-on-the-optimal-svd
[6] E. Jeon, M. Ahn, S. Kim, W. B. Lee and J. Kim, "Joint Beamformer and Beamformee Design for Channel Smoothing in WLAN Systems," in Proc. IEEE 92nd Veh. Technol. Conf. (VTC2020-Fall), Nov. 2020, pp. 1-6.

## Slide 13: Appendix
2 by 2 MIMO performance

## Slide 14: Appendix
Discussions
  FER
    Effect of discontinuity is smaller than that of 4 by 2
      Additional smoothing gain provided by optimization is about 1dB
    Smooth beamforming still provides about 2dB smoothing gain
  Overhead
    When threshold is 0.8, proposed scheme reduces 60.8% overhead compared to the full-tone optimization scheme