## Slide 1: Relaying for Low Latency Traffic in UHR
Date: 2023-07-11
Authors:

## Slide 2: Introduction
Two of the three main objectives within the scope of P802.11bn [1]:
  “Enabling at least one mode of operation capable of increasing throughput, as measured at the MAC data service Access Point, at different Signal to Interference and Noise Ratio (SINR) levels (Rate-vs-Range), compared to EHT MAC/PHY operation”
  “Enabling at least one mode of operation capable of improving the tail of the latency distribution and jitter compared to EHT MAC/PHY operation, with mobility between BSSs”
Low latency has already been an important consideration for 11bn [2-6]
  E.g., Preemption, scheduling, multi-AP operation, PPDU design, frame overhead reduction
Rate-vs-range enhancement may be an important consideration for 11bn [7-9]
  Some candidates: Relaying, finer MCS grid, long range PHY mode, MIMO/TXBF enhancement, multi-AP operation
In this contribution, we consider relaying operations to support low latency traffic in UHR

## Slide 3: Low latency traffic
Deterministic low latency traffic
  Periodic pattern with burst arrival of packets in each interval
  Can be supported by R-TWT and SCS mechanisms in 11be
  If an R-TWT scheduling AP has established SCS stream(s) described by QoS Characteristics element(s) with an R-TWT scheduled STA whose TID and Direction fields match an R-TWT TID, the AP should follow the rules specified in 35.17 (EHT SCS procedure) for scheduling of downlink or uplink QoS Data frames
Event-based low latency traffic
  Non-periodic, unpredictable patterns
  Hard to schedule
  Cannot be supported by existing 11be mechanisms
  New scheduling and preemption mechanisms needed

## Slide 4: Relays in general
Basics
  Communication range may be extended
  End-to-end throughput may be extended
  Communication may be single hop or multi hop
Challenges
  End-to-end channel reservation may be needed
  Delays due to relay processing
Related standards
  802.11ah (S1G relay)
  802.11ad (DMG relay)
Fig. 1. Relay communications

## Slide 5: Relays for 11bn
Relay properties
  Relaying should be able to handle low latency traffic
  Relay processing should be manageable (both time-wise and complexity-wise)
  Relays may be STAs with relaying capabilities (no AP capability as in S1G relays)
  Relays may be multi-link devices (benefit from using multiple links)
Fig. 2. A possible relay configuration for 11bn

## Slide 6: How to achieve low latency with relays
STA
While relaying important and low latency traffic, (R) Relay (e.g., STA with relaying capabilities) may not know if there is a time-limit (e.g., delay bound, remaining transmission time, etc.) to relay the data to (D) STA
Should be relayed to (D) STA
(S) STA
(R) Relay
(D) STA
Data
Data
ACK
RTS
CTS
CTS
(R) Relay transmits the data without knowing the delay bound
Data may be delayed or discarded
RTS
Data to STA
Latency sensitive data to be transmitted by this time
ACK

## Slide 7: An option: Low latency info aware relaying
The relay may receive an indication of LL data frame and transmission completion time info. Relay may calculate the remaining time for transmission and transmit/discard data accordingly
Indication of low latency packet transmission
(S) STA
(R) Relay
(D) STA
Data
Data
RTS
CTS
RTS
CTS
Low latency transmission completion time info
(R) Relay transmits within transmission completion time
ACK
Latency sensitive data to be transmitted by this time
STA
Data to STA
ACK

## Slide 8: How to achieve low latency with MLD relays
In case of a busy link, the MLD relay may use the other link to transmit the PPDU to the destination STA after receiving the PPDU
Challenges: Suitable link selection, link switching operation
While this approach leverages multiple links, if the PPDU has a long duration, relayed PPDU may be received after the transmission completion time
(S) STA
(R) Relay
(D) STA
PPDU
Link-1
Link-2
Link-1
Link-2
Link-1
Link-2
Normal TX duration
ACK
Busy
PPDU
ACK
Latency sensitive data to be transmitted by this time
(R) Relay starts relaying in a different link
(R) Relay transmits within completion time
(S) STA may inform (R) Relay of LL ML relaying
OPTION-1

## Slide 9: How to achieve low latency with MLD relays
(R) Relay starts relaying in a different link
Latency sensitive data to be transmitted by this time
Alternatively, for a shorter transmission duration, the MLD relay may start decoding, re-encoding, and transmitting portions of the PPDU in one link, while still receiving the PPDU in another link
Challenges: Determining when to start relaying, determining receiver and destination addresses while still receiving the PPDU, maintaining reliability of the transmission
(S) STA
(R) Relay
(D) STA
PPDU
Link-1
Link-2
Link-1
Link-2
Link-1
Link-2
Shorter TX duration
ACK
PPDU
(R) Relay transmits within completion time
(S) STA may inform (R) Relay of LL ML relaying
ACK
OPTION-2

## Slide 10: Conclusion
Different relaying operations to support low latency traffic in 11bn are considered
If a relay receives transmission completion time info (e.g., delay bound, remaining transmission time, etc.) from a source STA, it may use the info for relaying the low latency data frame
For the operation of MLDs, in case a relay receives low latency ML relaying information, the relay may start transmitting the data frame to the destination STA in another link after receiving the whole data frame or while still receiving the data frame
In case of either low latency ML relaying options, design challenges should be further investigated

## Slide 11: References
[1] 23/0480r0, UHR Proposed PAR
[2] 22/1556r1, Multi-AP Coordination for Low Latency Traffic Delivery
[3] 22/1939r0, PPDU Design for Short Frames
[4] 22/1923r1, Enhanced Trigger-Based Uplink Transmission
[5] 23/0045r1, Urgency-based Delivery of Latency Sensitive Traffic
[6] 23/0378r0, Enhanced Scheduling Method for Low Latency Traffic
[7] 22/2049r2, UHR PAR Discussion
[8] 22/1908r1, UHR Rate-vs-Range Enhancement with Relay
[9] 23/0042r0, Thought for Range Extension in UHR