## Slide 1: Obfuscation Computation Procedure
Date: 2023-07-07
Authors:

## Slide 2: Abstract
The contribution focuses on the computation procedure used to obfuscate the values of the CPE parameters (e.g. OTA MAC Address, SN, PN, TID). It is a part of the ERCM procedure already presented in 22/114r3
The CPE parameters obfuscation computation procedure is based on the standardized PRF (section 12.7.1.2 -IEEE Std 802.11-2020) executed in parallel by the CPE Client and the CPE AP with a shared private information (ERCM key) and a shared public information (CPE STA @MAC) without explicit exchange over the air
Only one execution of the computation procedure is necessary to generate at once the values of multiple CPE parameters

## Slide 3: 11bi requirement
R7 | 11bi shall define a mechanism for a CPE Client to initiate changing its own OTA MAC Address used with a CPE AP in Associate STA State 4 without any loss of connection.
R9 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted SN and the scrambler seed on downlink and uplink to uncorrelated new values in Associate STA State 4, without any loss of connection when the OTA MAC address of the CPE Client is changed
R10 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted PN on downlink and uplink to uncorrelated new values in Associate STA State 4, without any loss of connection when the OTA MAC address of the CPE Client is changed.
R11 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the CPE Client’s AID to an uncorrelated new value in Associate STA State 4, without any loss of connection when the OTA MAC address of the CPE Client is changed.
R30 | 11bi shall define a mechanism for a CPE Client and CPE AP to obfuscate the transmitted TID to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection.

## Slide 4: Obfuscation Procedures
For each CPE parameter, two obfuscation procedures can be considered
  Reset-based procedure for which the OTA value of the CPE parameter is obfuscated by resetting directly its “internal” value with a new uncorrelated (and randomized) one
  Reset-free procedure for which the OTA value of the CPE parameter is obfuscated by applying an obfuscation. In such a case, its “internal” value is not reset. Several obfuscation operations can be envisaged as XOR, addition or an Offset

## Slide 5: CPE Parameters (CPE_PARAM)
CPE Parameters | Requirement | Obfuscation procedure | MLD
MLD MAC address, SMAC, DMAC | 7 | reset-based | Core and Per-Link
UL/DL SN | 9 | reset-free | Core or Per-Link
UL/DL Scrambler Seed | 9 | reset-based | Per-Link
UL/DL PN | 10 | reset-free | Core
AID | 11 | reset-based | Core
UL/DL TID | 30 | reset-free | Core
In MLO, assign a mask/value per-link or per-MLD (common to all links)
Assign only one mask for both UL and DL could be sufficient
A mask per TID can be also envisaged for SN

## Slide 6
CPE Parameters Obfuscation Computation
The objective of the computation procedure is to assign at once a new reset value for each reset-based CPE parameter and a new mask for each reset-free CPE parameter
It is executed in parallel by the CPE Client and the CPE AP with a shared private information (ERCM key) and a shared public information (CPE STA @MAC) by using the standardized PRF (section 12.7.1.2 -IEEE Std 802.11-2020)
Only one execution of the computation procedure is necessary to obfuscate the list of CPE Parameters
CPE_PARAM (n+1) = PRF-M\L( ERCM Key, “ERCM”, @MAC (n))
ERCM Key is the private key used to the specific purpose of obfuscation
@MAC (n) is the current MAC address of the CPE Client (MLD @MAC, SMAC or DMAC)
M = 128, 192, 256, 384, 512 or 704
L the leftmost bits corresponding to the sum of the lengths of the CPE parameters
Ensure the privacy
Ensure a different output set at each execution
New set of obfuscation parameters to obfuscate CPE Parameters

## Slide 7: ERCM Key
The ERCM Key is specific to each CPE client. In such a case, it is derived from the PTK and more particularly from a KDK generated especially for ERCM
ERCM Key = KDF-Hash-256(KDK, "ERCMK", @MAC_Client || @MAC_AP)
  KDF-Hash-256 generates the 256 bits of the ERCMK Key
  KDK derived from PTK is generated specifically for ERCM procedure
  @MAC_Client and @MAC_AP are the MAC addresses of the CPE Client and CPE AP used for 4-way Handshake.
  “ERCMK” is a context string name for ERCM and is treated as an ASCII string.
Alternatively, the ERCM Key is a common group temporal key known by all CPE Clients. It is a 256-bits random value shared during the 4-way Handshake generated by the AP and encrypted by the KEK of the PTK in the message 3 (with GTK, IGTK and BIGTK)

## Slide 8: CPE Parameters Obfuscation Computation
The output CPE_PARAM (n+1) is split into predetermined chunks, each chunk corresponding either to a new reset value for each reset-based CPE parameter or a new shared mask for each reset-free CPE parameter
CPE_PARAM (n+1) = PRF-256\250( ERCM Key, “ERCM”, @MAC (n))
Illustrative obfuscation for non-MLD Client and one TID
1 1 ……… 0 1 …….. 1 0 ………1 0……..10 1……...1 0……... 1 1 ..…… 0 1 …… 1 0…… 1 ……….0 1 …..1
bit 1 …….… 47………. 93 ……… 105 ……… 117 ……. 165 ……. 213 …… 229……236…..… 243....… 247….250
OTA SMAC
Mask
UL_SN
Mask
DL_SN
Mask
DL_PN
OTA
AID
Mask
UL TID
OTA DMAC
Mask
DL TID
Mask
UL_PN
OTA UL
Scrambler
Seed
OTA DL
Scrambler
Seed

## Slide 9: CPE Parameters Obfuscation Computation
OTA AID (n+1) = CPE_PARAM (n+1) [213..228]
OTA UL_SS (n+1) = CPE_PARAM (n+1) [229..235]
OTA DL_SS (n+1) = CPE_PARAM (n+1) [236..242]
OTA UL_TID (n+1) = UL_TID + CPE_PARAM (n+1) [243..246]
OTA DL_TID (n+1) = DL_TID + CPE_PARAM (n+1) [247..250]
Remark : the obfuscation of the AID is also managed by the computation procedure of the ERCM procedure. It means notably that the AP doesn’t need to transmit it. The potential AID collisions issue is addressed in 23/336
1 1 ……… 0 1 …….. 1 0 ………1 0……..10 1……...1 0……... 1 1 ..…… 0 1 …… 1 0…… 1 ……….0 1 …..1
bit 1 …….… 47………. 93 ……… 105 ……… 117 ……. 165 ……. 213 …… 229……236…..… 243....… 247….250
OTA SMAC
Mask
UL_SN
Mask
DL_SN
Mask
DL_PN
OTA
AID
Mask
UL TID
OTA DMAC
Mask
DL TID
Mask
UL_PN
OTA UL
Scrambler
Seed
OTA DL
Scrambler
Seed
OTA SMAC (n+1) = CPE_PARAM (n+1) [1..46]
OTA DMAC (n+1) = CPE_PARAM (n+1) [47..92]
OTA UL_SN (n+1) = UL_SN + CPE_PARAM (n+1) [93..104]
OTA DL_SN (n+1) = DL_SN + CPE_PARAM (n+1) [105..116]
OTA UL_PN (n+1) = UL_PN + CPE_PARAM (n+1) [117..164]
OTA DL_PN (n+1) = DL_PN + CPE_PARAM (n+1) [165..212]

## Slide 10: CPE Parameters Obfuscation Computation
CPE Parameters | Number of parameters given MLD | Number of TIDs | Obfuscation parameter length (mark or value) in bits | Total Obfuscation length
MLD MAC Address SMAC,DMAC | 1+4 |  | 46 | 230
UL/DL SN | 2 | 8 | 12 | 192
UL/DL Scrambler Seed | 2 |  | 7 | 14
UL/DL PN | 2 |  | 48 | 96
AID | 1 |  | 16 | 16
UL/DL TID | 2 | 8 | 4 | 64
Total |  |  |  | 626
Example with a CPE MLD Client with 2 affiliated STAs
The computation procedure is based on a PRF-704\626 to generate the list of CPE parameters
Remark : if necessary, the PRF can be launched several times

## Slide 11: Benefits
No explicit exchange of the privacy values of the CPE parameters
Implementation complexity and costs reduction as only single execution of the PRF is necessary to obfuscate the multiple CPE parameters

## Slide 12
Straw Poll #1
Do you support the computation procedure used to obfuscate the values of CPE parameters as described at slide 6
Yes
No
Abstain

## Slide 13: References
[1] IEEE 802.11-21/1848r16 : Requirements Document
[2] IEEE 802.11-22/0114r3 : Enhanced Randomized and Changing MAC address
[3] IEEE 802.11-23/0166r1 : Mechanism of simultaneous changes to SN scrambler seed PN AID and TID
[4] IEEE 802.11-23/336r1 : AID modification upon MAC address change
[5] IEEE 802.11-23/411r1 : Obfuscation of Multiple CPE Parameters
[6] IEEE 802.11-23/268r1 : OTA MAC Address Change
[7] IEEE 802.11-23/873r0 : Client Frame Tracking Countermeasures