## Slide 1: CR for status code
Date: 2023-07-12
Authors:

## Slide 2: CR List-1
134 | Jarkko Kneckt | Technical | 1 | 12.2.11.1 | 31 | 25 | The "Not Identified" operations in the STA are not clear. What the STA shoud do? Why there is such a recommendation? | Please remove recognized and not recognized signaling and actions.
15 | Chaoming Luo | Technical | 1 | 12.2.11.2 | 32 | 53 | Why we need IRM Status field in the IRM element and IRM KDE? How should it be used? There is no normative description of the corresponding AP and non-AP behaviour for this field. | Remove the IRM Status field in the IRM element and IRM KDE.
17 | Chaoming Luo | Technical | 1 | 12.2.11.1 | 31 | 20 | The Device ID Status field is useless to a non-AP STA, why an AP send this information to the non-AP STA? When it's "Recognized", the identity of the non-AP STA makes sense in the AP, but has no impact on the non-AP STA's behaviour. When it's "Not Recognized", there is no change of non-AP STA's behaviour, the difference only occurs in the AP's hehaviour, | Remove the Device ID Status field in the Device ID element and Device ID KDE.
132 | Jarkko Kneckt | Technical | 1 | 9.4.2.307b | 28 | 30 | The recgnized / not recognized field is not needed. The field causes no actions on the STA. Also it is not clear how the STA should show such information to end user. | Please delete the recognized / not recognized bit.

## Slide 3: CR list-2
100 | Daniel Harkins | Technical | 1 | 12.7.2 | 34 | 1 to 10 | The device ID status is pointless. The non-AP STA can't make any use of that knowledge. And to what would it apply anyway? The device ID the non-AP STA sent? But it's getting another back from the AP so what purpose is there in saying whether or not the previous one was "recognized"? | get rid of the device ID status in the KDE.
101 | Daniel Harkins | Technical | 1 | 9.4.2.307a | 27 | 24-44 | The device ID status is pointless. The non-AP STA can't make any use of that knowledge. And to what would it apply anyway? The device ID the non-AP STA sent? But it's getting another back from the AP so what purpose is there in saying whether or not the previous one was "recognized"? | get rd of the device ID status in the element

## Slide 4: Background
Trouble shooting is widely used in current residential environment(or other place)
-->It’s benefit for ISP to address some performace issue or connectivity issue without onsite support.
Trouble shooting broken issue caused by RCM is in the scope of 11bh group
-->Several senarios mentioned in use case 4.15

## Slide 5: How troubleshooting works
after the AP deployed in enduser environment, the enduser may create a an account to allow all the log information save in the cloud
--> enduser will install an application to manage it’s AP
-->enduser create an account in the cloud server
-->enduser agree to save their log info/activity info. in the cloud too.
ISP will create a folder to save each user’s information in the server
--> ISP may create a profile for each STA(Based on STA MAC) under enduser’s folder.
-->ISP may only keep the latest log for each end user to save the memory
End user report the network trouble via call , website, or application
-->encounter low performance issue, connectivity issue, etc.
-->ISP is allowed to visit the user’s profile in the cloud once end user provides their account information(get user’s consent explicitly)
-->ISP grab the log information and analysis the issue locally, and then provide the further online support to the user

## Slide 6: trouble shooting network topology-1
Cloud
ISP
end user
online support

## Slide 7: trouble shooting network topology-2
Several AP nodes deployed in the residential environment to enlarge Wi-Fi coverage
--> the APs may have the same or different SSIDs.
-->the STA may associate with different APs each time.
Cloud

## Slide 8: The usage of status code in trouble shooting case
The 11bh identifier will be used to identify each STA in user’s folder
  permanent identifier (like long term device ID) is prefered
it can help ISP to converge the issue without access user’s database
  Visit user’s database may still have some legal issue even if get enduser’s consent explicitly
  in single AP case, the unrecognized issue may be caused by certain STA profile expired
  in multi APs case, the issue may be caused by the synchornized issue between two APs.
How the STA vendor handle the status code?
  STA vendor just report such error code to the GUI.
How the enduser handle such unrecognized issue?
  report the error info show the GUI to the ISP
  waiting for the next instruction from the ISP during online support
  google a certain error code and address it by themselves

## Slide 9: example: not recognized information shown in the GUI
similar to error 404, snap such information and report to the ISP or google the solution based on such error code.

## Slide 10: summary
analysis the trouble shooting working machansim
Illustrate how to use status code to address several issues in trouble shooting procedure
Recommandated to show all kinds of error code to the end user, rather than visit the user’s privacy datebase in trouble shooting case.

## Slide 11: resolution for CR 15,17,100,101,132,134
Rejected--
At least,the status code is benefit for trouble shooting and on-line service notification use case, the detail analysis on the trouble shooting use case can be found in this contribution.