## Slide 1: Discussion on AIML model sharing use case in federated learning scenario
Date: 2023-08-08
Authors:
Jing Ma (Toyota)
Aug. 2023

## Slide 2: Introduction
Model sharing is One of the main use case of AIML TIG [1]
  Efficient AIML model distribution is essential for the success of AIML-based operations as well as the performance and user experience of IEEE 802.11 WLANs in 1) centralized learning or centralized AIML model generation/refinement , 2) Distributed learning or distributed AIML model generation/refinement, and 3) Federated learning or hybrid AIML model training/refinement
We discuss the technique feasibility related to federated learning in 3) Federated learning or hybrid AIML model training/refinement scenario[1]
Jing Ma (Toyota)

## Slide 3
Discussion on workflow in federated learning scenario
AP/
central server
Client
Client
Participating
devices/ clients
① client selection and global model distribution
③ model update
④ Model
aggregation
② Local model training
③ local model upload
④ Model
Aggregation
and update
Repeat ① with updated global model
  In federated learning, usually only the selected participating devices perform local training in each round, the trained local models are then aggregated by the central server to update the global model and sent back to the clients selected for next round. This process is repeated for multiple communication rounds until the global model converges.[2]
Jing Ma (Toyota)

## Slide 4
As for global model distribution and local model upload, the current technical feasibility discussion has pointed out that IEEE 802.11bc has defined UL and DL EBCS services which may provide baseline technology for efficient AIML model sharing and distribution [1].
However, client selection which is an important aspect of federated learning seems that it has not been discussed yet
Technical feasibility discussion on federated learning scenario
Jing Ma (Toyota)

## Slide 5
Client selection is an important aspect as it directly benefits the overall performance by
  Ensure that the local models can be efficiently aggregated into a global model
  Reduce the communication costs
Client selection can be implemented in a centralized or distributed way [3-5]
  An example of centralized way to select clients [3]
Thoughts on technical feasibility
  IEEE 802.11 broadcast technology, e.g. IEEE 802.11bc, can
  be leveraged to efficiently deliver parameters/function for
  client selection.
Technical feasibility discussion on federated learning scenario
AP/
central server
Client
Client
Participating
devices/ clients
broadcasts parameters for client selection
③ model update
AP/server selects clients and distribute the global model
every clients calculate and send parameters for client selection
Jing Ma (Toyota)

## Slide 6
We would like to propose to add the following text at the end of the first paragraph of 2.3.4.2 in current technical report
“ The mechanism for selecting participating devices should be considered for efficient AIML model training/refinement. “
Technical feasibility discussion on federated learning scenario
Jing Ma (Toyota)

## Slide 7: References
[1] 11-22-0987-08-aiml-aiml-tig-technical-report-draft
[2] Brendan McMahan et al., "Communication-Efficient Learning of Deep Networks from Decentralized Data”, Proceedings of the 20 th International Conference on Artificial Intelligence, 2017
[3] Narisu Cha et al., “Fuzzy Logic Based Client Selection for Federated Learning in Vehicular Networks”, IEEE open journal of computer society, 2022
[4] J. Xu and H. Wang, “Client selection and bandwidth allocation in wireless federated learning networks: A long-term perspective,” IEEE Trans. Wireless Commun., vol. 20, no. 2, pp. 1188–1200, Feb. 2021
[5] Y. J. Cho, J. Wang, and G. Joshi, “Client selection in federated learning: Convergence analysis and power-of-choice selection strategies,” 2020, arXiv:2010.01243.