## Slide 1: AMP Device Channel Occupancy Analysis
Date: 2023-08-08
Authors:
Name | Affiliation | Address | Phone | Email
Yinan Qi | OPPO |  |  | v-qiyinan@oppo.com
Weijie Xu |  |  |  | xuweijie@oppo.com
Doc.: IEEE 802.11-23/1354r0
August 2023

## Slide 2: Abstract
The purpose of this presentation is to analyse the channel occupancy of AMP devices.
Doc.: IEEE 802.11-23/1354r0

## Slide 3
Assumptions
    Considered typical use cases
      Smart manufacturing: inventory and environment/production line sensing and monitoring
      Indoor positioning: positioning in giant shopping mall, factories, warehouses, etc.
    Payload size
      Inventory: 128 bits
      Sensor: 96 bits
      Positioning: 256 bits
    Signalling overhead: 50%
    Peak data rate: 51.2 kbps, 250 kbps, 1 Mbps
    Device density: 1.5 per m2, 10 per m2
    Coverage: 10m
    Retransmission: no retransmission, packet is dropped when received incorrectly
Yinan Qi (OPPO)
Slide 3
Doc.: IEEE 802.11-23/1354r0
August 2023

## Slide 4
Smart Manufacturing: Inventory
    Number of AMP devices associated with one AMP AP
      Low density: 471
      High density: 3142
    Channel occupancy time for data transmission for one AMP device
      Low rate: 5 ms
      Mid rate: 1 ms
      High rate: 0.256 ms
    Overall channel occupancy time
      Low density
        Low rate: 2.36 s
        Mid rate: 0.47 s
        High rate: 0.12 s
      High density
        Low rate: 15.6 s
        Mid rate: 3.1 s
        High rate: 0.8 s
Yinan Qi (OPPO)
Slide 4
Doc.: IEEE 802.11-23/1354r0
August 2023

## Slide 5
Smart Manufacturing: Inventory
    Number of Inventory per hour: 1/h, 0.1/h
    Overall channel occupancy percentage
      1/hour: 0.0033% - 0.4%
      0.1/hour: 0.00033% - 0.04%
    Observation 1: Overall channel occupancy time can be up to 15.6 s in a extreme case but the overall channel occupancy percentage is extremely small, e.g., up to 0.4%.
    Observation 2: For majority cases, overall channel occupancy time is expected to be from a few hundred milliseconds to a few seconds and have negligible impact on other legacy devices
Yinan Qi (OPPO)
Slide 5
Doc.: IEEE 802.11-23/1354r0
August 2023

## Slide 6
Smart Manufacturing: Sensor
    Number of AMP devices associated with one AMP AP
      Low density: 471
    Channel occupancy time for data transmission for one AMP device
      Low rate: 3.75 ms
      Mid rate: 0.75 ms
      High rate: 0.192 ms
    Overall channel occupancy time
      Low density
        Low rate: 1.77 s
        Mid rate: 0.35 s
        High rate: 0.09 s
Yinan Qi (OPPO)
Slide 6
Doc.: IEEE 802.11-23/1354r0
August 2023

## Slide 7
Smart Manufacturing: Sensor
    Number of sensor data reporting per hour: 10/h, 1/h, 0.1/h
    Overall channel occupancy percentage
      10/hour: 0.025% - 0.49%
      1/hour: 0.0025% - 0.049%
      0.1/hour: 0.00025% - 0.0049%
    Observation 1: Overall channel occupancy time is up to 1.77 s in a extreme case and has negligible impact on other legacy devices
    Observation 2: The overall channel occupancy percentage is extremely small, e.g., up to 0.49%.
Yinan Qi (OPPO)
Slide 7
Doc.: IEEE 802.11-23/1354r0
August 2023

## Slide 8
Indoor Positioning: Positioning
    Number of AMP devices associated with one AMP AP
      Low density: 471
    Channel occupancy time for data transmission for one AMP device
      Low rate: 10 ms
      Mid rate: 2 ms
      High rate: 0.512 ms
    Overall channel occupancy time
      Low density
        Low rate: 4.72 s
        Mid rate: 0.94 s
        High rate: 0.24 s
Yinan Qi (OPPO)
Slide 8
Doc.: IEEE 802.11-23/1354r0
August 2023

## Slide 9
Indoor Positioning: Positioning
    Number of Inventory per hour: 0.1/h
    Overall channel occupancy percentage
      0.1/hour: 0.00066% - 0.08%
    Observation 1: Overall channel occupancy time is up to 4.72 s in a extreme case but the overall channel occupancy percentage is extremely small, e.g., up to 0.08%.
    Observation 2: For majority cases, overall channel occupancy time is expected to be from a few hundred milliseconds to a few seconds and have negligible impact on other legacy devices
Yinan Qi (OPPO)
Slide 9
Doc.: IEEE 802.11-23/1354r0
August 2023

## Slide 10
Summary
    Base on the analysis, only in some extreme case, e.g., low rate and high density smart manufacturing, deployment of AMP devices August affect legacy devices during the peak time. However, such case is normally special case and isolated from other legacy devices.
    For other use cases, the overall channel occupancy time is only up to a few seconds and the overall channel occupancy percentage is less than 0.5%.
    In majority cases, the impact of AMP devices to legacy devices is negligible.
Yinan Qi (OPPO)
Slide 10
Doc.: IEEE 802.11-23/1354r0
August 2023