## Slide 1: Discussions on Low Latency Traffic Delivery in UHR
Date: 09/10/2023
Authors:

## Slide 2
Abstract
In this contribution, we discuss the potential solutions to enhance the low latency traffic delivery in UHR.

## Slide 3: Introduction
One of the project scopes of 802.11bn is to enable [1]
  At least one mode of operation capable of reducing latency by 25% for the 95th percentile of the latency distribution compared to the Extremely High Throughput MAC/PHY operation
Many contributions [2]-[10] have been presented in UHR to show the potential solutions to enhance two types of Low Latency (LL) traffic delivery
  Deterministic or predictable low latency traffic
  Event based or unpredictable low latency traffic
In this contribution, we will discuss the potential solutions to enable the LL traffic delivery, especially the unpredictable LL traffic

## Slide 4: Challenges of the LL Traffic Delivery
In some applications, the latency requirement becomes more stringent [2], e.g., end to end latency requirement is from 0.1 to 1 msec
Different challenges may be encountered in two types of LL traffic delivery, but more challenges exist in the unpredictable LL traffic delivery
    The data arrival time, data amount, the transmitter STA and the recipient STA may be unpredictable
    Different latency requirements may require different aspects of considerations:
      TXOP level latency requirement: LL traffic indication and LL traffic scheduling
      PPDU level latency requirement: LL traffic transmission
Backward compatibility
  Reduce the LL traffic delivery time while minimizing the impact on the legacy devices

## Slide 5: LL Traffic Delivery Scenarios 1-3
The LL traffic does not come from the TXOP holder and arrives in the middle of TXOP
TXOP level latency requirement may be applicable to these 3 secenarios
It may require mechanism to support LL traffic indication, LL traffic scheduling (see the following 3 slides)
STA1 is TXOP holder; STA2 is the TXOP responder
LL STA is the STA with LL traffic data to transmit

## Slide 6: LL Traffic Indication (1/2)
Scenario 1: LL STA is the TXOP responder and LL traffic recipient is the TXOP holder
  Propose to transmit a low latency traffic indication either along with BA frame or an independent frame [5], [7]
  Alternatively, A-control field (e.g., CAS) may be used to indicate the reverse traffic
Scenario 2: LL STA is neither the TXOP holder nor the TXOP responder and LL traffic recipient is the TXOP holder
  Increase the time gap between the PPDUs with non-LL data within one TXOP such that the LL STA may grab the channel to indicate LL Traffic [5], [6]
    The new operation may only be understood by the UHR STA
  New frame is proposed to indicate LL traffic even during the transmission of TB PPDU from another STA [8]

## Slide 7: LL Traffic Indication (2/2)
Scenario 2 (Cont.): LL STA is neither the TXOP holder nor the TXOP responder and LL traffic recipient is the TXOP holder
  It becomes more challenging when multiple STAs have LL traffic [5-8]
    Use trigger frame (e.g., NFRP trigger frame [6], UORA process [7]) to solicit multiple LL transmission request
    May need to differentiate between the legacy trigger frame and the enhanced trigger frame for soliciting LL indication to avoid the contention with the legacy STA(s)
    May consider to allow a group of UHR STAs to contend the channel access
Scenario 3: LL STA is the TXOP responder and LL traffic recipient is neither the TXOP holder nor the TXOP responder
  TXOP sharing may be used to support this scenario
  May need a mechanism to ensure the potential recipient of LL STA is aware of the LL traffic indication

## Slide 8: LL Traffic Scheduling
Scenario 1: LL STA is the TXOP responder and LL traffic recipient is the TXOP holder
  It may require the TXOP holder to grant the transmission to the TXOP responder.
  To be compatible with the legacy operation, the existing solutions, e.g., reverse direction operation, may be used
Scenario 2: LL STA is neither the TXOP holder nor the TXOP responder and LL traffic recipient is the TXOP holder
  After LL traffic indication, the TXOP holder, e.g., AP, may transmit a trigger frame to solicit the transmission(s) of LL data [5], [6]
  rTWT may be used to as a vehicle to support the unpredictable LL data exchange
Scenario 3: LL STA is the TXOP responder and LL traffic recipient is neither the TXOP holder nor the TXOP responder
  It may require the TXOP holder to grant the transmission to this LL STA
    If TXOP sharing is used (e.g., STA1 is the AP), it may need to make sure the AP set the TXOP Sharing Mode to 2

## Slide 9: LL Traffic Delivery Scenarios 4-5
The LL traffic comes from the PPDU transmitter and arrives in the middle of an ongoing PPDU
PPDU level latency requirement may be applicable to Scenarios 4 and 5
It may require mechanism to support LL traffic transmission
Different transmission schemes may be used to meet the different latency requirement
STA1 is the transmitter of the ongoing PPDU; STA2 is the receiver of the ongoing PPDU
LL STA is the STA with LL traffic data to transmit

## Slide 10: LL Traffic Transmission
Scenario 4: LL STA is the transmitter, and the recipient of LL traffic is receiver
  Preemption PPDU is proposed in [3], [4] to meet low latency requirement
  Dedicated RU is to reserve a RU for the transmission of the ultra low latency data [2]
Scenario 5: LL STA is the TXOP holder, but the recipient of the LL traffic is not the responder of TXOP
  Preemption PPDU or dedicated RU may be used to support this scenario
  If the latency requirement is PPDU level,
    The Preemption PPDU may need to switch the intended STA
    The Dedicated RU may need to indicate the STA(s) which are the potential recipient(s) of LL traffic
STA3
STA2
STA2
STA2

## Slide 11: Considerations of Handling Unpredictable LL Traffic in Different Scenarios
Scenario | TXOP Level LL Req. | PPDU Level LL Req.
1 | LL traffic indication & scheduling | N/A
2 | LL traffic indication & scheduling | N/A
3 | LL traffic indication & scheduling | N/A
4 | N/A | LL traffic transmission
5 | N/A | LL traffic transmission

## Slide 12: Summary
In this contribution, we focus on the unpredictable LL traffic delivery.
Five typical scenarios are considered for unpredictable LL traffic delivery
  LL traffic indication and LL traffic scheduling are discussed for Scenario 1-3
  LL traffic transmission is discussed for Scenario 4-5.

## Slide 13: References
11-23/480r3, UHR Proposed PAR
11-23/1155r0, Ultra-Low Latency with Wi-Fi
11-22/1393r0, Latency Reduction Scheme for UHR
11-22/1880r1, Latency and Reliability enhancements for UHR
11-23/1174r0, TXOP Preemption Follow Up
11-23/1229r1, Preemption for Low Latency Application (follow up)
11-23/0798r0, Low Latency Traffic Report
11-23/1194r0, Overlapped Indication to Support Preemption
11-23/0378r0, Enhanced Scheduling Method for Low Latency Traffic
11-23/355, Enhanced rTWT and MAP operation