## Slide 1: Further Considerations on dRU
Date: 2023-09-10
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
To overcome PSD limitations which are defined per 1 MHz, dRU was introduced in [1]
We presented our view on dRU design ways for a tone plan, pilot and signaling in [2]
In [3], detailed methods to design dRU tone plans and how to indicate each dRU by reusing the conventional RU Allocation field were introduced
In [4] and [5], we compared several options for pilot designs by investigating their performance
In this contribution, we discuss further issues to consider in designing a dRU tone plan

## Slide 3: Further Considerations
Channel widths used for dRU transmissions
  Channel widths in which dRU tone plans should be designed
dRU transmission given preamble puncturing
  How to perform a dRU transmission when preamble puncturing is applied
dRU sizes allowed in each channel width
  Minimum and maximum dRU sizes depending on the channel width

## Slide 4: Channel Widths Used for dRU Transmissions
In [3], we provided a general way to design dRU tone plans for 20 / 40 / 80 MHz
In 11be, 160 MHz operation in a 6 GHz band is mandatory for AP STAs while it is optional for non-AP STAs
  Non-AP STAs support only up to 80 MHz mandatorily
However, for UHR, support for 160 MHz may become more common along with hardware improvement and it may be also possible that this support becomes mandatory for non-AP STAs
Moreover, large dRUs can achieve a further transmit power gain in a 160 MHz channel
Thus, it would be better to define dRU tone plans up to 160 MHz
  We are not arguing that all of the dRU tone plans should be mandatory

## Slide 5: dRU Transimission given Preamble Puncturing (1/2)
In 11be, some of the preamble puncturing cases for larger than or equal to 80 MHz are defined as mandatory features in a 6 GHz band
For UHR, preamble puncturing cases should be considered in 6 GHz as in 11be, and thus, how to perform a dRU transmission can be determined by taking into account them
  Option 1: design a new dRU tone plan by distributing tones of each dRU across an occupied channel, e.g., tones for each dRU are distributed across 60 MHz when 20 MHz is punctured in 80 MHz
  Option 2: combine dRU tone plans, e.g., 20 MHz and 40 MHz tone plans are combined for a 60 MHz dRU transmission

## Slide 6: dRU Transmission given Preamble Puncturing (2/2)
Option 1 obtains a better transmit power gain and higher throughput using larger dRUs while option 2 is simple
If we apply a multiple dRU concept where several dRUs are aggregated and allocated to a certain STA for a PPDU transmission, throughput for option 2 can be improved
  E.g., in a 60 MHz transmission by combining 20 MHz and 40 MHz tone plans, one dRU in 20 MHz and one dRU in 40 MHz can be aggregated
Moreover, the most useful environment for dRU is a low power indoor case in 6 GHz where preamble puncturing may not be considered
Hence, it would be better to minimize the implementation burden in designing a dRU tone plan, and thus, we slightly prefer option 2 if preamble puncturing needs to be considered

## Slide 7: dRU Sizes Allowed in Each Channel Width
Defining various kinds of dRU may be better in terms of the flexibility but may increase implementation complexity
For the tone plans in [3], *narrow bandwidth capable STAs (e.g., 20 MHz operating STAs) cannot participate in a dRU transmission where the 40 / 80 MHz dRU tone plan is applied since all tones in each dRU are distributed across 40 / 80 MHz channel
  Small dRUs are necessary for a dRU tone plan defined in a narrow channel (e.g., 20 MHz) while it may not be the case in a wide channel
Moreover, in wide channels such as 80 / 160 MHz, large dRUs can obtain a higher transmit power gain over narrow channels
Thus, in a wide channel dRU tone plan, it may be possible to consider excluding small dRUs and defining only some large ones
  * Note that 20 MHz operating STAs can still participate in a dRU transmission for a wider bandwidth PPDU when the 20 MHz dRU tone plan is applied to a specific 20 MHz channel

## Slide 8: Summary
We have discussed several consideration points in designing a dRU tone plan as follows
  Channel widths used for dRU transmissions
  dRU transmission given preamble puncturing
  dRU sizes allowed in each channel width

## Slide 9: References
[1] 11-23-0037-00-0uhr-uhr-feature-to-overcome-psd-limitations-distributed-tone-resource-units
[2] 11-23-0281-00-0uhr-considerations-on-ru-mru-designs-for-uhr
[3] 11-23-1117-00-0uhr-dru-signaling-for-uhr
[4] 11-23-1115-00-0uhr-cfo-impact-and-pilot-design-for-dru
[5] 11-23-1447-00-0uhr-cfo-impact-and-pilot-design-for-dru-follow-up