## Slide 1: Cross Interference During Coordinated Spatial Reuse
Date: 2023-09-11
Authors:

## Slide 2: Abstract
Coordinated Spatial Reuse (C-SR) is one of the Multi-AP transmission techniques that is being considered for UHR.
C-SR only requires RSSI or pathloss feedback as opposed to complete CSI between all APs and STAs.
Based on the RSSI or pathloss feedback, a sharing AP decides the transmit powers and MCSs of all shared APs during the C-SR transmission phase.
In this contribution, we talk about considerations regarding cross interference during the C-SR transmission phase.

## Slide 3: General Procedure for C-SR
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
Interference Measurement
Phase
Interference measurement phase
  The sharing/shared APs measure interference or pathloss to each other’s target STA.
Transmission phase
  Initiated by the sharing AP. The sharing AP controls the transmit power and MCS of the shared APs.
Transmission Phase

## Slide 4: Interference Measurement Phase
An interference measurement phase can be one of the following.
  General Multi-AP channel sounding [1],[2]
  Active RSSI measurement procedure [3]
  Opportunistic RSSI measurements [4]
Regardless of the interference measurement phase, a sharing AP obtains an estimate of cross interference of all APs and STAs participating in the C-SR transmission phase. It uses these estimates to determine the transmit powers and MCS of the shared APs.

## Slide 5: Shared AP Transmit Power and MCS
During the transmission phase, we assume that AP1 first decides its own transmit power and MCS. Based on these decisions, it computes the transmit power and MCS of the shared AP.
Transmit power of AP2 - AP2 transmit power depends on the interference from AP2 to STA1 (X2) and MCS to be used by AP1.
MCS of AP2 - The sharing AP (AP1) may indicate a maximum MCS of the shared AP. AP2 MCS may depend on the interference from AP1 to STA2 (X1) and transmit power of AP1.

## Slide 6: Cross Interference during C-SR Transmission Phase
Additional restrictions may be necessary to prevent unexpectedly large cross interference during the C-SR transmission phase.
For example, the following may be disallowed (or allowed with explicit signaling) for the shared APs in order for the sharing AP to accurately decide the C-SR transmit parameters.
  Beamforming restrictions
  Bandwidth/RU size restrictions
  PPDU alignment restrictions

## Slide 7: Shared AP Beamforming (1/2)
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
MAP
TF
DL Data Frame
DL Data Frame
(Beamformed)
BA
MCS,TP
A Shared AP may perform beamforming (non-coordinated) to STA2 to increase its own transmission’s reliability under the TP and MCS limitation set by the sharing AP.
A beamformed PPDU may cause a higher interference to the Sharing AP’s transmission than a non-beamformed PPDU.
Beamformed
Interference

## Slide 8: Shared AP Beamforming (2/2)
Simulation Parameters
AP1 – 2 Antennas
AP2 – 2 Antennas
PPDU Format: SU PPDU/80 MHz
Channel Model: TGn Channel B
AP2 Beamforming: Strongest beam/eigenvector.
1000 Iterations
PPDU1
PPDU 100
PPDU2
1000 Iterations
As seen in the figure, the interference of AP2 may experience amplification on some subcarriers due to beamforming. The AP1 must account for this effect when deciding the transmit power of AP2.
Interference amplification
Note: x-axis is concatenated PPDU subcarrier samples (980) of all PPDUs

## Slide 9: Use of smaller BW/RU
AP2’s transmission may also result in a higher interference than AP1 may expect if AP2 uses a smaller BW or RU than AP1 expects. AP1 must account for this possibility when deciding the transmit power of AP2.
AP1
(sharing AP)
AP2
(shared AP)
STA1
(Associated with AP1)
STA2
(Associated with AP2)
MAP
TF
DL Data Frame
80 MHz
DL Data Frame
(20MHz)
BA
MCS,TP
Narrower band PPDU
Interference
AP1
AP2
STA 1
STA 2
Interference

## Slide 10: Synchronized vs Non-Synchronized C-SR
AP2 may also introduce unexpectedy high interference to the Sharing AP when it transmits a PPDU that is not fully aligned with the PPDU of the Sharing AP.
AP1
(sharing AP)
AP2
(shared AP)
MAP
TF
MCS,TP
Pre-UHR
UHR
Pre-UHR
UHR portion
unsynchronized
offset
Simulation Parameters
AP1 – 2 Antennas
AP2 – 2 Antennas
PPDU Format: SU PPDU/80 MHz
Channel Model: TGn Channel B
AP2 transmission offset: 4 us
PPDU1
PPDU 100
PPDU2
1000 Iterations
Note: x-axis is concatenated PPDU subcarrier samples (980) of all PPDUs

## Slide 11: Proposed Solution
Restrict the following during C-SR
  Non-coordinated beamforming
  Bandwidth/RU size changes for range extension
  Unsynchronized PPDU transmissions
Option 1 – Disallow
Option 2 – Explicit Allowance/Disallowance

## Slide 12: Conclusion
We presented considerations regarding cross interference during the C-SR transmission phase.
We showed through simulation results how some transmission parameter choices by the shared AP may result in higher interference to the sharing AP’s transmission when left unrestricted.

## Slide 13: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1097-00-00be-sounding-procedure-in-ap-collaboration.pptx
[2] https://mentor.ieee.org/802.11/dcn/19/11-19-1134-01-00be-consideration-of-multi-ap-sounding.pptx
[3] https://mentor.ieee.org/802.11/dcn/23/11-23-0668-02-0uhr-coordinated-measurement.pptx
[4] https://mentor.ieee.org/802.11/dcn/20/11-20-0576-00-00be-coordinated-spatial-reuse-protocol.pptx