## Slide 1
  Proposed 8th Generation IEEE802.11 WLAN PHY:
  Dynamic Polarization Spatial Multiplexing and Beamforming
  Carlos A Rios
  CEO, Terabit Wireless Internet LLC
  Sep 12, 2023

## Slide 2: Agenda
Proposed 8th Generation 802.11 WLAN
DPSMXBF Mathematical Model
Representative DPSMXBF AP
Representative DPSMXBF Client
2

## Slide 3
3
Proposed 802.11Gen8 “DPSMXBF” WLAN
Specifications
  Up to 32 IEEE802.11be RF spatial streams
  32x32 MIMO Spatial Multiplexing
  32x32 MIMO Beamforming
  5-7 GHz UNII Spectrum Operation
  4096 QAM
  320 MHz BW
  92,224 Mbps peak AP Data Rate
  2882 Mbps peak Client Data Rate
  >2 km AP-Client Free-Space Range

## Slide 4
4
Contemplated DPSMXBF WLAN Architecture
DPSMXBF AP
DPSMXBF CLIENT

## Slide 5
Reciprocally Interference-Free Cochannel Propagation of Up to 32 WLAN Spatial Streams in the Terrestrial DLOS Channel
Data “D” is modulated into “n” parallel RF spatial streams [S]
[S] is MIMO Tx and Rx beamformed and launched directionally across Terrestrial DLOS channel to arrive at the receiver SDMX as [S*], all represented by [H]
SDMX computes and applies the inverse transfer function [H-1] to [S*] in order to recover [S] (= [S’]). [S’] are then demodulated and aggregated back into D
DPSMXBF Tutorial
5

## Slide 6: The DPSMXBF Spatial Multiplexer
[HDP]: DPSMXBF Propagation Channel
  n Tx “DPA” antennas “Polarization Modulate” [S] IAW n distinct Walsh-m sequences
  The DLOS channel aggregates and transports n pol-mod [S] onto n Rx DPAs
  Rx DPAs pol-demod [S] aggregates with the same Walsh-n codes to yield [S*]
A2

## Slide 7: [HDP] Operation
A3
  The one [HDP] output [S*] DP-matched Si component is clearly identical to the [HDP] input [S] Si component, so is represented by a “1” in the [HDP] matrix
  The n-1 [S*] DP-mismatched Sj≠i components comprise [S] Sj≠i components each missing constituent symbols, and are represented within [HDP] by a variable “rij” corresponding to the measured similarity (or correlation) between Si and S*j

## Slide 8: [HDP] Representation
A4
  At this point, the [HDP] transfer function matrix can be represented as follows:
  rij roughly equals the Si:S*j Walsh sequences cross-correlation (i.e., always 50%)
  The rij are time-invariant, deterministic and uniform, a constant “r” close to 0.5000
  The precise value of r corresponds to the cross-polarization isolation exhibited between the orthogonally polarized elements comprising the Rx DPA antennas
    For example, commercial X-band antennas spec cross-pol isolation at -25dB typical
    Which gives us the definitive
Polarization-matched Rx Sii symbols propagate 1.0000x
Ideal polarization-mismatched Rx Sj≠i symbols propagate 0.0000x
rij = 0.5000
6 GHz polarization-mismatched Rx Sj≠i symbols propagate 0.0032x
rij = 0.5016
TxSi symbols

## Slide 9: Dynamic Polarization Summary
A5
Finally, the comprehensive Dynamic Polarization MIMO Tx-Rx model:
  DP spatial multiplexing polarization-decorrelates the Si into S*i per [S*] = [S] x [HDP]
  DP spatial demultiplexing matrix-inverts the deterministic, time-invariant and uniform [HDP] into a corresponding DT-IU [HDP-1]
  The SDMX operation [S’] = [S*] x [HDP-1] is equivalent to the n equations
  S’i = s S*i – t Σ S*j≠i for i, j = 1, 2, … n
  IOW, faithfully reproducing the originally transmitted [S] comprises arithmetically manipulating the received [S*] n times, a trivial exercise even for very large n

## Slide 10: TSI Technology Demonstrator
B1
625 Mbps SISO/ 10 Gbps DP16 LEOSat Tx-Rx
Data Rate vs SNR Test Setup
DPNW
Client
DPNW
Server