## Slide 1: IEEE 802.11 and Bluetooth Coexistence Simulations
Date: 2023-09-13
Authors:

## Slide 2: Introduction
Multiple contributions on coexistence of Listen-Before-Talk (LBT) based wideband (“Wi-Fi”) with Narrow-Band Frequency Hopping (NBFH) (“Bluetooth” or “BLE”) in the same spectrum (5.945 GHz to 6.425 GHz)
  IEEE 802.11-23/0453:
    eDAA claimed to be inadequate
    LBT (for NBFH) appears to work quite well
  IEEE 802.11-23/0877:
    NBFH with eDAA can co-exist with Wi-Fi without LBT
Contributions are based on simulations
  What are the underlying assumptions / models?
  What is the impact of changing the assumptions on the results?
  Which assumptions are realistic / need to be considered?

## Slide 3: Assumption 1: Spectrum Usage / Channelization
Wi-Fi
3 ⨯ 160MHz channels (channel number 15, 47, 79)
  Primary-20 always the first 20MHz
Bluetooth
1 MHz channels with 0.5MHz guard band left & right
  Maximum 480MHz ÷ 2MHz = 240 channels
  3 advertising channels (0, 79, 159)
  233 data channels (highest prime number below 237)
  Center frequency of channel 0 at 5.947MHz
Each connection selects its frequency hopping size randomly between 44 and 94
  Scaled up from 2.4GHz operation (37 channels, hopping size 7 to 15)

## Slide 4: Assumption 2: Scenario
Six Bluetooth links
  Constant bitrate traffic
  320B/20ms (≙128kb/s) 640B/20ms (≙256kb/s) 1280/20ms (≙512kb/s) KPI: Packet delay
1, 2, or 3 Wi-Fi links
  Infinite number of 10 MB file downloads via FTP
  ~3 s start delay
  KPI: File download delay
Channel model
  AWGN with Line-of-Sight for d < 5 m (pathloss coefficient 2.0), Non-Line-of-Sight for d > 5 m (3.5)

## Slide 5: Assumption 3: Capabilities
Wi-Fi
1 ⨯, 2 ⨯, or 3 ⨯ non-overlapping 160MHz channels
23dBm transmit power
Receiver Noise Figure 6dB
LBT: Energy detection threshold −71dBm/20MHz according to EN 303 687
Optional: Puncturing of 20 MHz channels
Bluetooth
233 data channels + 3 advertising channels
10dBm transmit power
Receiver Noise Figure 8dB
10ms connection interval between connection events
1 Mb/s PHY
Optional: enhanced Detect-And-Avoid (eDAA)
Optional: LBT before connection event

## Slide 6: Scenario Impact: Bluetooth Load
320B payload every 20ms:
  Two segments fit into one connection event
  Every other connection event remains idle
  ~16 % channel usage
1280B payload every 20ms:
  Five segments, require two connection events
  ~57 % channel usage
Saturation at ~1600B/20ms
  Idle time required to handle retransmissions
  Build-up of transmit queues, unusable delay values

## Slide 7: Scenario Impact: Channel Conditions
Static & deterministic channel model
  Received power only depends on frequency and distance
Allows calculation of possible channel conditions
Without interference:
  Wi-Fi has perfect conditions
  Bluetooth has perfect conditions

## Slide 8: Scenario Impact: Channel Conditions
Wi-Fi interfered by Bluetooth
Interference triggers ED at STA & AP
Very strong interference at STA
  -49.5dBm received signal power vs. -44dBm received interference power
  SINR = −27 dB (on 1 MHz)
Impact depends on Packet error model
Bluetooth interfered by Wi-Fi
Slightly interfered
  Interference is spread over 160 MHz
  Large distance to AP
Interfered by AP: SINR = 33dB
Interfered by STA: SINR = 15dB
Essentially no impact

## Slide 9: Assumption 4.1: Wi-Fi Packet Error Model
PER Model A (average Mutual Information, according to 11ax evaluation methodology PHY abstraction “optimistic”)
PER Model B (Mutual Information of C/I “pessimistic”)
average MI
= 159 ∕ 160 × MI(36dB) + 1 ∕ 160 × MI(-27dB)
= 159 ∕ 160 × 10b + 1 ∕ 160 × 0b
= 9.93b
⇒ OK
(strong narrow-band interference is averaged out)
MI(C/I)
= MI( -71dBm/MHz × 160MHz – -44dBm/MHz × 1MHz )
= MI (-49dBm – -44dBm)
= MI(-5dB)
= 0b
⇒ Failed
(strong narrow-band interference dominates the packet error probability)

## Slide 10: Assumption 4.2: Bluetooth Packet Error Model
For every reception
  Calculate SINR for every bit
  Map SINR to bit error rate
  Random number draw per bit
  Decision on success/failed reception

## Slide 11: Coexistence mechanisms

## Slide 12: Bluetooth: LBT before Connection Event (CE-LBT)
Sense current channel before every connection event
  Idle: transmit
  Busy: defer until next connection event

## Slide 13: Bluetooth: eDAA combined with CE-LBT
CE-LBT detects channel as busy
  Defer transmission to the next connection event
  Block channel and all channels belonging to the corresponding 20MHz block from future use
  Special case: if channel is centered between two 20MHz blocks, then block all channels belonging to the right and left block
Same procedure for two consecutive CRC failures within a connection event
At least 15 unblocked channels remain

## Slide 14: Wi-Fi: Puncturing
LBT without Puncturing
AIFS / Backoff countdown starts on primary 20MHz only
Energy Detection (ED) on all channels begins 25µs before each transmission
Only transmit if all sub-channels are idle
LBT with Puncturing
Puncturing allows 20MHz “holes” in the spectrum
Primary 20MHz must be idle
Assumption: puncturing is fully dynamic and flexible concerning which 20MHz is punctured

## Slide 15: Results

## Slide 16: No Interference
Wi-Fi
FTP download delay slightly higher than 100ms
Bluetooth
Packet delay depends on size and if fragments fit into one connection event
Small chance of collisions of the six links

## Slide 17: Baseline: No Coexistence Mechanisms
⇐ Wi-Fi
High impact of Bluetooth interference
  Depending on Bluetooth load
Optimistic PER model: impact only due to LBT
Pessimistic PER model: impact due to LBT (interference first) and packet errors (interference second)
  Approx. factor 2 delay for 320B/20ms, unusable for 1280B/20ms
Bluetooth ⇒
No impact of Wi-Fi interference on packet delay
Optimistic PER Model
Pessimistic PER Model
320B / 20ms load
1280B / 20ms load

## Slide 18: Coexistence 1: Bluetooth with CE-LBT (but no eDAA)
⇐ Wi-Fi (only for 1280B Bluetooth packets)
Significant improvement vs. Bluetooth without LBT
Bluetooth ⇒
Introduction of delay steps due to missed Connection Events (CEs)
Reduction of capacity leads to oversaturation case for many BSSs or large packet size
Optimistic PER Model
Pessimistic PER Model
320B / 20ms load
1280B / 20ms load

## Slide 19: Coexistence 2: Bluetooth with CE-LBT and eDAA
⇐ Wi-Fi (only for 1280 B Bluetooth packets)
Bluetooth has essentially no impact on Wi-Fi
Bluetooth ⇒
One or two BSS, i.e., at least 160 MHz idle: Good coexistence
Three BSS: Links fail to find idle channels, oversaturation case even for 320B per 20ms
Optimistic PER Model
Pessimistic PER Model
320B / 20ms load
1280B / 20ms load

## Slide 20: Coexistence 3: Wi-Fi with Puncturing
⇐ Wi-Fi (only for 1280 B Bluetooth packets)
Significant improvement over no coex mechanism
Channel access delay is reduced to interference-free case, only packet errors remain
Bluetooth ⇒
Same results as in no interference case
Optimistic PER Model
Pessimistic PER Model
320B / 20ms load
1280B / 20ms load

## Slide 21: Coexistence 4: Wi-Fi with Puncturing, Bluetooth with CE-LBT & eDAA
⇐ Wi-Fi (only for 1280B Bluetooth packets)
Significant improvement over no coex mechanism
Channel access delay is reduced to interference-free case, only packet errors remain
Bluetooth ⇒
Same results as if Wi-Fi does not puncture
Optimistic PER Model
Pessimistic PER Model
320B / 20ms load
1280B / 20ms load

## Slide 22: Conclusions
Wi-Fi interfered by Bluetooth
Increased channel access delay due to LBT
  Counteracted by puncturing
May increase packet errors due to strong, narrow-band interference
  Is it possible to enhance resilience if only 1MHz of 160MHz is interfered?
Bluetooth interfered by Wi-Fi
Robust against wideband interference (in this scenario)
Introduction of CE-LBT (together with eDAA)
  may increase delays and
  may suppress connections, depending on Wi-Fi channel usage

## Slide 23: Assumption 2B: Scenario B
Decrease Bluetooth transmit power to 0dBm
  Less signal strength at headsets
Increase Bluetooth device distance to 2m
  More pathloss
Move Bluetooth links to the center between the Wi-Fi links
  More interference by the downlink-heavy Wi-Fi traffic

## Slide 24: Scenario B Impact: Channel Conditions
Wi-Fi interfered by Bluetooth
Interference still triggers ED at STA & AP
Less (but still significant) interference at STA
  C/I = 11dB
  SNR = −11dB (on 1MHz)
Bluetooth interfered by Wi-Fi
Strong interference
  SNR from 52dB down to 6dB if AP is transmitting

## Slide 25: Scenario B Impact: Baseline / No Coexistence Mechanisms
Scenario B
Scenario A
Increased packet delay for Bluetooth due to packet errors and retransmissions in the next connection event
Slightly higher delay for Wi-Fi due to increased Bluetooth interference

## Slide 26: Scenario B Impact: Wi-Fi with Puncturing
Scenario B
Scenario A
Increased packet delay for Bluetooth due to higher interference power in non-punctured channels
Wi-Fi delay slightly better than in Scenario A – less interference power from Bluetooth due to larger distance

## Slide 27: Scenario B Impact: Wi-Fi with puncturing, Bluetooth with CE-LBT & eDAA
Scenario B
Scenario A
Bluetooth results are slightly worse than in Scenario A
Wi-Fi completely recovers, similar as in Scenario A

## Slide 28: Conclusions (ii)
Wi-Fi interfered by Bluetooth
Increased channel access delay due to LBT
  Counteracted by puncturing
May increase packet errors due to strong, narrow-band interference
  Is it possible to enhance resilience if only 1MHz of 160MHz is interfered?
Bluetooth interfered by Wi-Fi
Introduction of CE-LBT (together with eDAA)
(i) reduces packet error rate caused by interference,
(ii) may increase delays and
(iii) may suppress connections, depending on Wi-Fi channel usage
Bluetooth requires some form of CE-LBT to reduce interference impact
The assumed approach is too sensitive – Bluetooth may be completely suppressed by Wi-Fi
Wi-Fi with puncturing eliminates the LBT access delay resulting from narrow-band interference

## Slide 29: Appendix: All Simulation Results

## Slide 30: Baseline: No Coex mechanisms

## Slide 31: Scenario A, optimistic PER model

## Slide 32: Scenario A, pessimistic PER model

## Slide 33: Scenario B, optimistic PER model

## Slide 34: Scenario B, pessimistic PER model

## Slide 35: Coex: BLE with LBT

## Slide 36: Scenario A, optimistic PER model

## Slide 37: Scenario A, pessimistic PER model

## Slide 38: Scenario B, optimistic PER model

## Slide 39: Scenario B, pessimistic PER model

## Slide 40: Coex: BLE with LBT & eDAA

## Slide 41: Scenario A, optimistic PER model

## Slide 42: Scenario A, pessimistic PER model

## Slide 43: Scenario B, optimistic PER model

## Slide 44: Scenario B, pessimistic PER model

## Slide 45: Coex: Wi-Fi Dynamically Punctures Occupied 20 MHz

## Slide 46: Scenario A, optimistic PER model

## Slide 47: Scenario A, pessimistic PER model

## Slide 48: Scenario B, optimistic PER model

## Slide 49: Scenario B, pessimistic PER model

## Slide 50: Coex: Wi-Fi Dynamically Punctures Occupied 20 MHz, BLE with LBT & eDAA

## Slide 51: Scenario A, optimistic PER model

## Slide 52: Scenario A, pessimistic PER model

## Slide 53: Scenario B, optimistic PER model

## Slide 54: Scenario B, pessimistic PER model