## Slide 1: Proposed Amendments to Multi-AP Coordination Language in EHT SFD
Sept 2023
Authors:
Name | Affiliation | Phone | email
Brian Hart | Cisco Systems |  | brianh@cisco.com
Binita Gupta | Cisco Systems |  | 
Juan Carlos Zuniga | Cisco Systems |  | 
Stephen Orr | Cisco Systems |  | 
Jerome Henry | Cisco Systems |  | 
Stephen Rodriguez | Cisco Systems |  | 
Federico Lovison | Cisco Systems |  | 

## Slide 2: Introduction
Multi-AP Coordination (MAPC*) was a feature originally targeted at EHT
The EHT Specification Framework Document (SFD) recorded several important agreements for standardizing MAPC[1]
It was proposed to recycle the MAPC aspects of the EHT SFD for UHR[2]
As the same time, during the UHR SG, we have had new and rich discussions on MAPC, and there are opportunities to upgrade the EHT SFD’s MAPC language …
* Since MAP means Maximum A Posteriori to members with a PHY background, and M-AP will collapse to MAP, therefore MAPC is recommended.

## Slide 3: UHR SG presentations on MAPC have gone well beyond the EHT SFD agreements …
UHR SG presentations have considerably extended the MAPC discussion from EHT in several important areas:
Use of out-of-band coordination synergistically with in-band coordination [3]-[14]
Per-TXOP sharing need not be the only sharing mechanism: for instance, discussion on Coordinated (R)TWT is ongoing [11][12], [15]-[23]
As a corollary, the active MAPC discussions make it clear that MAPC is an evolving area and vendors will learn a lot during product bring-up and subsequent experimentation. Such experimentation should be supported by allowing for vendor specific extensions.

## Slide 4: … and the EHT SFD agreements look overly constraining
For instance, section 9.2 includes:
“An EHT AP which obtains a TXOP and initiates the multi-AP coordination is the sharing AP.”
… which implies that all multi-AP coordination is per individual TXOPs.
Therefore, we propose various amendments ….

## Slide 5: Proposed Amendments to EHT SFD’s MAPC language 9.1 General
This section describes features related to multi-AP operation.
802.11bn defines both in-band and out-of-band coordination modes of operation. In-band coordination supports 1-hop coordination. Out-of-band coordination is not limited by wireless hop count.
Where in-band and out-of-band coordination require the same parameters to be exchanged, 802.11bn shall define a common message format, except, when the timing of an in-band transmission is significant, 802.11bn shall define an alternative mechanism to signal time for out-of-band coordination (TBD; e.g., including source/destination TSF (or a bitslice thereof), time wrt a common timebase, etc).
802.11bn shall support out-of-band multi-AP coordination via tunneling of frames defined by 802.11.
802.11bn shall support vendor-specific extensions in all Multi-AP Coordination frames.

## Slide 6: Proposed Amendments to EHT SFD’s MAPC language 9.2 Setup
A UHR# AP supporting the multi-AP coordination can send a frame (e.g., Beacon or other Management frame) including capabilities of Multi-AP transmission schemes.
NOTE – Multi-AP transmission schemes are TBD (e.g., coordinated OFDMA).
A UHR AP which obtains a TXOP and initiates per-TXOP multi-AP coordination is the sharing AP.
A UHR AP which is coordinated for per-TXOP multi-AP transmission by the sharing AP is the shared AP.
NOTE – The name of the sharing AP and the shared AP can be modified.
802.11bn supports the following:
Sharing AP and shared AP may not have the same primary 20 MHz channel.
The primary 20 MHz channel of the shared AP shall be within the BSS operating channel width of the sharing AP.
The primary 20 MHz channel of the sharing AP shall be within the BSS operating channel width of the shared AP.
802.11be supports defining the modes of per-TXOP AP coordination that share frequency resources with one or more APs within the AP candidate set only for 20 MHz channels allocated by a sharing AP to a shared AP within the BSS operating channel of the shared AP.
NOTE – These are 20 MHz channels allocated by a sharing AP within the 20 MHz channels on which the sharing AP gained channel access.
#Trivial deletions are not shown for clarity

## Slide 7: Proposed Amendments to EHT SFD’s MAPC language 9.4 Coordinated transmission
802.11bn shall define an AP candidate set* as follows:
An AP candidate set is a set of APs that can initiate or participate in per-TXOP multi-AP coordination.
An AP in an AP candidate set can participate as a shared AP in per-TXOP multi-AP coordination initiated by a sharing AP in the same AP candidate set.
At least one AP in an AP candidate set shall be capable of being a sharing AP.
NOTE – The name* can be changed.
Define a procedure for an AP to share its frequency/time resources of an obtained TXOP with a set of APs.
Set of APs is TBD.
An AP that intends to use the resource (i.e., frequency or time) shared by another AP shall be able to indicate its resource needs to the AP that shared the resource.
In all modes of operation wherein an AP shares its frequency/time resource of an obtained TXOP with a set of APs:
Define a mechanism for the sharing AP to optionally solicit feedback from one or more APs from the AP candidate set to learn the resource needs and the intent to participate in a coordinated AP transmission.
In all modes of operation wherein an AP shares its frequency resource with a set of APs, the AP shall share its frequency resource in multiples of 20 MHz channels with a set of APs in an obtained TXOP.
PPDU format of the transmission on the shared resource is TBD.
Coordinated OFDMA is supported in 11bn, and in a coordinated OFDMA, both DL OFDMA and its corresponding UL OFDMA acknowledgement are allowed.
802.11bn will adopt coordinated UL MU-MIMO as a multi-AP coordination scheme for UL transmissions in R2.
NOTE – Not for joint reception.
802.11bn believes the hidden node problem in multi-AP environments (e.g. coordinated AP transmission) should be addressed.

## Slide 8: Summary
We show how to generalize the EHT MAPC-related text to account for or make room for the fresh UHR discussions:
      Out-of-band coordination
      A sequence of TXOPs, such as from Coordinated (R)TWT
      Vendor Specific extensions

## Slide 9: References
[1] 19/1262r23, “Specification Framework Document”, Edward Au (Huawei)
[2] 22/1516r0, “Considerations on Multi-AP Coordination”, Yusuke Tanaka (Sony)
Wired or out of band coordination or a common coordination or mgmt. entity presentations
[3] 23/0480r3, UHR proposed PAR, Laurent Cariou (Intel)
[4] 22/1394r1, Virtual BSS And Multi AP Transmissions, Vamadevan Namboodiri (Samsung)
[5] 22/1512r0, Multi-AP Coordination for UHR, Yee (MediaTek)
[6] 22/1567r0 C-OFDMA throughput analysis in various mesh backhaul scenarios, Sigurd Schelstraete (MaxLinear)
[7] 22/1580r1 A Perspective on Proposed UHR Features For Enterprise Use Cases, Brian Hart (Cisco Systems)
[8] 22/1899r0, Multi-AP Operation for Low Latency Traffic Delivery - Follow up, Liuming Lu (OPPO)
[9] 23/0041r0, Considerations on Coordinated TDMA, Yanjun Sun (Qualcomm)
[10] 23/0046r2, Multi-AP Coordination for Low Latency Traffic Delivery: Usage Scenarios and potential features, Liuming Lu (OPPO)
[11] 23/0291r0, R-TWT Multi-AP Coordination, Muhammad Kumail Haider (Meta)
[12] 23/0297r0, rTWT for Multi-AP, Laurent Cariou (Intel)
[13] 23/0665r1, Resource Management for Multi-AP Coordination, Peshal Nayak (Samsung)
[14] 23/0839r0, Multi-AP Coordination based on SCMA, Gang Xie (BUPT)
R-TWT/C-TWT presentations
[15] 23/0226r2, Coordination of R-TWT for Multi-AP Deployment, Abdel Karim Ajami (Qualcomm Inc.)
[16] 23/0250r0, AP coordination with R-TWT, Liwen Chu (NXP)
[17] 23/0291r0, R-TWT Multi-AP Coordination, Muhammad Kumail Haider (Meta)
[18] 23/0293r0, Follow-up on TWT-based Multi-AP Coordination, Rubayet Shafin (Samsung Research America)
[19] 23/0297r0, rTWT for Multi-AP, Laurent Cariou (Intel)
[20] 23/0355r0, Enhanced rTWT and MAP operation, Hanqing Lou (InterDigital)
[21] 23/0771r0, Coordinated R-TWT Protection in Multi-BSS, SunHee Baek (LG Electronics)
[22] 23/0860r0, Further thoughts on coordinated TWT, Rubayet Shafin (Samsung Research America)
[23] 23/1087r0, Announcement for R-TWT Coordination, SunHee Baek (LG Electronics)

## Slide 10: Backup

## Slide 11: Proposed Amendments to EHT SFD’s MAPC language 9.3 Channel Sounding
9.3 Channel sounding
802.11bn shall provide a joint NDP sounding scheme as optional mode for multiple-AP systems.
Sequential sounding scheme that each AP transmits NDP independently and sequentially without overlapped sounding period of each AP can also be used in multi-AP systems.
Joint NDP sounding scheme for multi-AP system with less or equal to total 8 antennas at AP has all antennas active on all LTF tones and uses 802.11ax P matrix across OFDM symbols.
Multiple APs can sequentially use an 802.11ax-like sounding sequence to collect CSI from the in-BSS STAs and OBSS STAs.
The sounding sequence of each AP is similar to the 802.11ax sounding protocol with multiple STAs (NDPA + NDP + BFRP TF + CSI report).
In sequential channel sounding sequence for multi-AP, the NDPA frame and BFRP TF frame will include ID info for OBSS STA.
The details of the NDPA, BFRP TF and the ID info are TBD.
In sequential channel sounding sequence for multi-AP, 802.11bn supports the following:
STA can process the NDPA frame and the BFRP Trigger frame received from the OBSS AP.
If polled by the BFRP trigger frame from the OBSS AP, the STA responds with the corresponding channel state information (CSI) to the OBSS AP
NOTE 1 – Details of the CSI report are TBD. NOTE 2 – The OBSS AP belongs to the multi-AP set serving the STA and the details regarding formulation of the multi-AP set are TBD. NOTE 3 – This feature is for R2.

## Slide 12: Proposed Amendments to EHT SFD’s MAPC language 9.5 Other Multi-AP coordination schemes
9.5 Other Multi-AP coordination schemes
802.11bn supports introducing a coordinated spatial reuse operation in 802.11bn.
Whether it is in R1 or R2 is TBD.
802.11bn supports adding to 802.11bn SFD “Joint transmission for single and multi user” under the multi-AP topic.
NOTE – This feature is for R2
802.11bn supports adding “Multi-AP Coordinated BF” to 802.11bn SFD as one of the multi-AP coordination schemes.
NOTE – This feature is for R2.