## Slide 1: Follow-up discussion on AIML model sharing use case
Date: 2023-09-11
Authors:
Jing Ma (Toyota)
Sep. 2023

## Slide 2: Introduction
Model sharing is one of the main use case of AIML TIG [1]
11-23/1349/r1 discussed that client selection is essential for model sharing use case [2]
As for follow-up, the example client selection process is discussed in this submission
Jing Ma (Toyota)

## Slide 3
Assumptions
AP/central server owns the global model
Many clients (participating devices) with different channel quality,
computation capability, data samples, etc..
Each client is willing to train the model using local data.
Work flow
① Client selection
AP distributes client select function/parameters
Each client calculates select function result
e.g. channel quality, battery, computation capability of the
client could be considered
Select clients
→ e.g. all clients send select function results to AP, then AP selects top m clients for current round training
Discussion on example client selection process
Jing Ma (Toyota)
STA2
STA 3
AP
AP distributes client selection function/parameters
STA 4
STA 1
STA 2
STA 3
AP
STA 4
STA 1
Each client calculates its select function result
STA2
STA 3
AP
Each client sends its selection function result to AP
STA 4
STA 1
AP selects clients for current training round
Involving all clients to training process may cause inefficiency

## Slide 4
Discussion on example client selection process
Jing Ma (Toyota)
Work flow
② AP distributes the global model to the selected clients
③ Selected clients do local model training and upload local model to AP
④ AP aggregates and updates global model for next training round
Then go back to Step① until certain criteria are met.
STA 2
STA 3
AP
Selected clients do local model training and upload Local model to AP
STA 4
STA 1
STA2
STA 3
AP
AP sends global model to selected clients
STA 4
STA 1
It’s been proved that client selection can reduce the communication cost, meanwhile improve learning efficiency [3-6]
  In [3], using a subset of clients (1/6) achieved higher test accuracy with much smaller communication (8%) compared with learning with all participating devices,

## Slide 5: Summary
 | Description | Thoughts on standardization
① Client selection | ・AP distributes client selection parameters ・Each device calculates select function ・participants send selection function results ・AP selects top m clients for current round training | ・Sounding protocol could be leveraged ・Standardize the related signaling ・Client select function or parameters, learning model/parameters may be left for implementation
② Global model distribution | AP sends global model to selected clients | 
③ local model training & upload | Selected clients do local model training and upload to AP | 
④ Global model updates | AP aggregates and updates global model for next training round | 

## Slide 6: Comment on current technical report draft
AIML benefits description related Federated learning or hybrid AIML model training/refinement is as following
3）Federated learning or hybrid AIML model training/refinement
In this scenario, all participating devices, such as STAs or APs, are capable of computing AIML models and generating their local models and subsequently:
    share their local models to a central point, such as the AP or a central server, likely in the UL direction, and the AP or central server generates a global model using the received local models as input and distributes the global model to all participating devices, likely in the DL direction;
    share their local models to all participating devices, likely in the UL direction and peer-to-peer, and all participating devices generate the global model using the received local models as input.
As for the third case, We would like proposed to add extra description for better covering a subset of participating devices case which have been discussed in this submission

## Slide 7: Comment on current technical report draft
The proposed text modification is as below
3）Federated learning or hybrid AIML model training/refinement
In this scenario, all participating devices, such as STAs or APs, are capable of computing AIML models and generating their local models and subsequently:
    ALL or a subset of participating devices share their local models to a central point, such as the AP or a central server, likely in the UL direction, and the AP or central server generates a global model using the received local models as input and distributes the global model to all or a subset of participating devices, likely in the DL direction;
    ALL or a subset of participating devices share their local models to all participating devices, likely in the UL direction and peer-to-peer, and all participating devices generate the global model using the received local models as input.

## Slide 8: References
[1] 11-22-0987-11-aiml-aiml-tig-technical-report-draft
[2] 11-23/1349/r1- aiml-Discussion on AIML model sharing use case in federated learning scenario
[3] Brendan McMahan et al., "Communication-Efficient Learning of Deep Networks from Decentralized Data”, Proceedings of the 20 th International Conference on Artificial Intelligence, 2017
[4] Narisu Cha et al., “Fuzzy Logic Based Client Selection for Federated Learning in Vehicular Networks”, IEEE open journal of computer society, 2022
[5] J. Xu and H. Wang, “Client selection and bandwidth allocation in wireless federated learning networks: A long-term perspective,” IEEE Trans. Wireless Commun., vol. 20, no. 2, pp. 1188–1200, Feb. 2021
[6] Y. J. Cho, J. Wang, and G. Joshi, “Client selection in federated learning: Convergence analysis and power-of-choice selection strategies,” 2020, arXiv:2010.01243.