## Slide 1: PHY Considerations for AMP Devices
Date: 2023-09-11
Authors:

## Slide 2: Abstract
We provide some considerations about the PHY design of AMP devices, which should be taken into account once PAR limitations are being discussed

## Slide 3: Should AMP Use Only Legacy 802.11 PHY?
Yes:
  Support by existing devices - much easier, mostly SW updates, wider market adoption
  Protection from OBSS interferences (marginal)
  Avoid introducing new waveform in the 802.11
But better allow some changes:
  Lower the energy consumption (up to ~x60 times lower)
  Efficient BW/channel use (~6000%)

## Slide 4: Legacy Mode Protection
By using legacy mode waveforms, the AMP-STA is protected from OBSS
  Each station that missed the AP trigger message can detect the legacy 802.11 preamble and header and avoid interfering with that AMP-STA transmission
  Much better protection compared to CCA protection, which is unreliable and detects energy (-95dBm vs -75dBm)
DL AP Legacy protection >> UL AMP-STA legacy protection:
  AMP-STA UL: Preamable time ~ data transmission time, for short frames expected. Thus protection probability is low.
  Non-symmetric LB: AP DL EIRP e.g. 20dBm while AMP-STA UL transmits e.g. <-20dBm. In addition, AMP-STA is very near to AP to be able to receive WUR.
  Analysis in the next page

## Slide 5: Non Symmetric Legacy Protection Analysis [Friis]
Parameter | Value [example]
AP-EIRP | 20dBm
OBSS STA legacy sensitivity | -95dBm
AMP-STA-EIRP | -20dBm
AMP-STA DL sensitivity | -55 dBm
Analysis shows protection from legacy on AMP-STA UL is non-existing compared to legacy transmitted from AP DL [6km vs 60m]
Legacy protection from AP
AMP-STA range
Legacy protection from AMP-STA
Legend

## Slide 6: Lower Energy Consumption
Use of DSSS is x20 times longer for 200 bits transmissions
  DSSS requires 200us preamble + headers
  200 bits takes 200us @1Mbps (DSSS) compared to e.g. 20us@10Mbps
Frequency accuracy:
  Crystal in the AMP-STA (increases energy consumption by at least x10 times)
  or
  Over-the-air calibration (increases energy consumption x3 and complexity of AMP-STA receiver, as well as maintaining robust calibration flows)
BW/Channel use analysis: changing the above will improve also the efficiency of using the channel by factor of x60

## Slide 7: Summary
We presented considerations about PHY layer for AMP devices that should be taken into account during a drafting phase
As both legacy and non-legacy modes have strong market motivations, we prefer to maintain both modes as options before the drafting phase
We believe PAR should enable discussions on PHY level as well, to avoid market bottlenecks
It is possible to limit non-legacy waveforms for use by very low power devices (e.g. <-20dBm)

## Slide 8: References