## Slide 1: Reverse TXOP sharing in UHR
Date: 2023-09-13
Authors:
Name | Affiliations | Address | Phone | Email
Sindhu Verma | Broadcom |  |  | sindhu.verma@broadcom.com
Shubhodeep Adhikari |  |  |  | shubhodeep.adhikari@broadcom.com
Matthew Fischer |  |  |  | matthew.fischer@broadcom.com
Vinko Erceg |  |  |  | vinko.erceg@broadcom.com
Kamal Singhal |  |  |  | kamal.singhal@broadcom.com
Bijoy Bhukania |  |  |  | bijoy.bhukania@broadcom.com
Notes: November 2012

## Slide 2: Abstract
This contribution discusses the benefits and mechanism for Reverse TXOP Sharing i.e. allowing a TXOP acquired by a non-AP STA to be shared with an AP and further, allowing the AP to utilize the shared TXOP for carrying appropriate Downlink and Uplink traffic

## Slide 3: Problem Statement (1)
During normal operation in 802.11, only an AP can share its TXOP with its clients in the following manner:
  11ax onwards, using Triggered allocations for Uplink transmissions
  11be onwards, using TXS Mode 1 for SU Uplink transmissions and TXS Mode 2 for P2P-like transmissions
In certain scenarios, such sharing by the AP is beneficial in reducing channel access attempts and collisions at the clients to transmit UL data.
In other scenarios where there is significant OBSS congestion, it is beneficial to keep the clients contending for channel access so that the BSS in question gets a commensurate share of the medium. However this entails the following problems:
  Each client can utilize its TXOP only for its own Uplink transmissions
  There is no mechanism to share the unutilized portion for Downlink data and Uplink data corresponding to other clients even if there is pending latency-sensitive/control traffic

## Slide 4: Problem Statement (2)
There can also be cases where the AP is unable to win channel access or when it wins access, it is not aligned with the availability of idle medium at the client i.e. there may be hidden node issues at the client which would make it more optimal for the client to be the initiator of TXOPs
For these reasons, it is beneficial to have a scheme that allows a TXOP acquired by a non-AP STA to be shared with an AP and further, allows the AP to utilize the shared TXOP for carrying appropriate Downlink and Uplink traffic
The Reverse Direction (RD) protocol allows TXOP sharing between an RD Initiator and Responder, where the Initiator can be a non-AP STA. However, the protocol allows only a limited version of such TXOP sharing. For example, the RD Responder (say an AP) can transmit data only to the RD Initiator (say a non-AP STA) and inclusion of traffic to other STAs can only be done in an MU-MIMO fashion and without extending the duration of transmission to the RD Initiator.

## Slide 5: Proposed Solution
In UHR, a non-AP STA can be required to share its TXOP with the AP optionally after utilizing it for its own transmission or mandatorily
The full duration or remainder of this TXOP can be shared with the AP
The indication to the AP will consist of the remaining duration as well as the AC with which the TXOP was acquired
In this TXOP acquired and shared by a non-AP STA, the AP can prioritize low latency control/data to any non-AP STAs. It can also schedule corresponding UL transmissions from non-AP STAs. It can also transmit or schedule other data depending on the AC with which the TXOP was acquired
TXOPs can be shared between STAs in different BSSs via inter-BSS coordination.
SIFS gap is mandated between consecutive transmissions with the option of PIFS-based recovery

## Slide 6: Benefits of the Proposed Solution
The proposed solution allows the non-AP STAs to contend for channel access and share the resources with the AP for better QoS management across the BSS:
  The AP can prioritize latency-sensitive and control traffic
  The AP can manage fairness between Downlink and Uplink traffic as well as among multiple non-AP STas
It also allows efficient utilization of TXOPs and less idle time in the medium (due to channel access gaps between shorter transmissions from individual non-APs)
It allows the BSS to continue to have a commensurate share of the medium while having the advantages of scheduled access
It allows management of hidden node situations where the non-AP may have better visibility of the Downlink interference situation and hence, can poll for Downlink transmissions

## Slide 7: Conclusion
Reverse TXOP sharing has the following advantages
  Efficient resource utilization: bandwidth efficiency
  Low latency and control traffic prioritization
  QoS management
  Mitigation of hidden node issues
The 802.11 specification changes required in UHR are minimal. They can simply be an extension of the 11be TXS modes 1 and 2.

## Slide 8: References
[1] IEEE P802.11be™/D4.0
[2] 11-20-0005-01-00be-Proposals on Latency Reduction