## Slide 1: Discussion on Decline Duration Indication field
Date: 2021-08-24
Authors:
Name | Affiliation | Address | Phone | Name
Rui Du | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | ray.du@huawei.com
Naren |  |  |  | 
Zhuqing Tang |  |  |  | 
Yiyan Zhang |  |  |  | 

## Slide 2: Related CIDs
CID | Page. Line | Clause Number | Comment | Proposed Change
3515 | 116.35 | 9.6.7.55 (Protected) SBP Response frame format | Decline Duration Indication field is included Sensing Measurement Response frame. Do we need a similar field for SBP Response frame ? | Add 'Decline Duration Indication' field to SBP response frame if needed.
3516 | 123.56 | 9.6.21.9 DMG Sensing Measurement Response frame format | Do we need a 'Decline Duration Inidcation' field for DMG Sensing Measurement Resposne frame ? | Add 'Decline Duration Indication' field to DMG Sensing Measurement Request frame if needed.
3517 | 127.50 | 9.6.21.13 DMG SBP Response frame format | Do we need a 'Decline Duration Inidcation' field for DMG SBP Resposne frame ? | Add 'Decline Duration Indication' field to DMG SBP Request frame if needed.

## Slide 3: Background
Decline Duration Indication field is used in Sensing Measurement Response frame and this field is present if the Status Code is set to REQUEST_DECLINED.
The Decline Duration Indication field indicates a time duration within which the sensing initiator is requested not to send a new Sensing Measurement Request frame after its request has been declined.

## Slide 4: The frames to be discussed
This function can be added to the other frames in 11bf, such as
SBP Response frame
DMG Sensing Measurement Request frame
DMG SBP Response frame
E.g. when Decline Duration Indication field is included in the SBP response frame, this field indicates a time within which the SBP initiator is requested not to send a new SBP request frame after its request has been declined.

## Slide 5: SP
Do you support to add ‘Decline Duration Indication field’ to the follow frames:
SBP Response frame
DMG Sensing Measurement Request frame
DMG SBP Response frame
Note: the definition of ‘Decline Duration Indication field’ to be added in the above frames is same with the field in Sensing Measurement Response frame (i.e. request the initiator not to send a new request frame within the time indicated in this field).
Yes:
No:
Abstain: