## Slide 1: Considerations on BSS color for Multi-AP
Date: 2023-11-10
Authors:
Name | Affiliation | Address | Phone | Email
Hirohiko Inohiza | Canon |  |  | inohiza.hirohiko@mail.canon
Masatomo Ouchi |  |  |  | 
Yuki Tsujimaru |  |  |  | 
Kazuyuki Tota |  |  |  | 

## Slide 2: Introduction
As defined in IEEE Std 802.11ax™‐2021 spec, if a PHY entity receives a PPDU with a BSS color not containing an intended value, the PPDU shall be filtered out.
Joint Transmission is one of the Multi-AP technique which different APs transmit PPDUs simultaneously to a same non-AP STA[1][2][3]. If each AP transmits a PPDU with a different BSS color from each other, a PPDU with a BSS color not containing an intended value would be filtered out in the non-AP STA according to the baseline rule.
  Moreover, it may lead to PHY preamble collisions. [4]
This contribution proposes several ways to handle a BSS color for Multi-AP in 11bn.

## Slide 3: Problem Statement
When performing Joint Transmission, if each AP transmits a PPDU with a different BSS color from each other to a same non-AP STA, a PPDU with a BSS color not containing an intended value would be filtered out in the non-AP STA.
  Moreover, it may lead to PHY preamble collisions
AP1 (BSS color1)
AP2 (BSS color2)
Non-AP STA associated with AP1
PPDU with BSS color1 in PHY preamble
PPDU with BSS color2 in PHY preamble
This PPDU shall be filtered out in non-AP STA
Backhaul data sharing

## Slide 4: BSS color coordination among APs (1)
When performing Joint Transmission, a coordinator AP and a coordinated AP (or coordinated APs) transmit PPDUs with which the same BSS color values are set in PHY preambles.
A special BSS color value for Joint Transmission is used.(BSS color3 in the example below)
The APs may share information of the special BSS color during Multi-AP setup or Multi-AP coordination, or by Trigger frame to trigger Joint Transmission.
The information of the special BSS color may be notified to a non-AP STA by a Management frame as Association Response frame or Trigger frame to trigger Joint Transmission. The non-AP STA will not filter out PPDUs with the special BSS color.
Coordinator AP (BSS color1)
Coordinated AP (BSS color2)
Non-AP STA
receiving from multi-AP
PPDU with BSS color3 in PHY preamble
PPDU with BSS color3 in PHY preamble
This PPDU won’t be filtered out in Non-AP STA
Multi-AP setup, coordination
(BSS color3)
Non-AP STA
receiving from single AP
PPDU with BSS color2 in PHY preamble
Management frame
(BSS color3)

## Slide 5: BSS color coordination among APs (2)
When performing Joint Transmission, a coordinator AP and a coordinated AP (or coordinated APs) transmit PPDUs with both BSS colors of the coordinator AP and the coordinated AP set in PHY preambles.
New definition in PHY preamble (E.g. U-SIG, UHR-SIG…) to include additional BSS color field is necessary.
  It may also require to include multi-AP communication flag in PHY preamble
The APs may share information of their BSS colors during Multi-AP setup or Multi-AP coordination, or by Trigger frame to trigger Joint Transmission.
The information of the BSS colors may be notified to a non-AP STA by a Management frame as Association Response frame or Trigger frame to trigger Joint Transmission. The non-AP STA will not filter out PPDUs with the BSS colors.
Coordinator AP (BSS color1)
Coordinated AP (BSS color2)
Non-AP STA
receiving from multi-AP
PPDU with
BSS color1+BSS color2 in PHY preamble
PPDU with
BSS color1+BSS color2 in PHY preamble
This PPDU won’t be filtered out in Non-AP STA
Multi-AP setup, coordination
(BSS color1+BSS color2)
Non-AP STA
receiving from single AP
PPDU with BSS color2 in PHY preamble
Management frame
(BSS color1+BSS color2)

## Slide 6: Summary
BSS color handling in Multi-AP Joint Transmission should be considered to properly receive PPDUs in a non-AP STA.
We proposed several ways to handle a BSS color for Multi-AP Joint Transmission in 11bn.

## Slide 7: Reference
[1] A candidate feature: Multi-AP, 11-22-1515-00-0uhr-a-candidate-feature-multi-ap , https://mentor.ieee.org/802.11/dcn/22/11-22-1515-00-0uhr-a-candidate-feature-multi-ap.pptx
[2] Considerations on Multi-AP Coordination, 11-22-1516-00-0uhr-considerations-on-multi-ap-coordination, https://mentor.ieee.org/802.11/dcn/22/11-22-1516-00-0uhr-considerations-on-multi-ap-coordination.pptx
[3] Joint Transmission for UHR -A Refresher and New Results, 111-22-2188-00-0uhr-joint-transmission-for-uhr-a-refresher-and-new-results, https://mentor.ieee.org/802.11/dcn/22/11-22-2188-00-0uhr-joint-transmission-for-uhr-a-refresher-and-new-results.pptx
[4] Coordinated Transmission ID, 11-23-1469-00-0uhr-coordinated-transmission-id, https://mentor.ieee.org/802.11/dcn/23/11-23-1469-00-0uhr-coordinated-transmission-id.pptx

## Slide 8: IEEE Std 802.11ax™‐2021 spec