## Slide 1: Coordinated Spatial Reuse Design
Date: 2023-10-18
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Ross Jian Yu |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 

## Slide 2: Introduction
Multi-AP (MAP) coordination has been extensively discussed in TGbe, as well as the EHT SG [1-33].
Many modes of multi-AP coordination have been proposed and analyzed, including:
  Joint transmission (JT) ; Coordinated Beamforming (CBF) ; Coordinated UL MU MIMO (co-UL-MU-MIMO) ; Coordinated Spatial Reuse (CSR) ; Coordinated OFDMA (COFDMA), Coordinated TDMA (CTDMA), Coordinated RTWT
Among all the multi-AP coordination modes, Coordinated Spatial Reuse [16] is considered as the mode to provide throughput gain as well as latency gain, without bringing much complexity
In this contribution, we discuss a detailed design of the CSR mode.

## Slide 3: CSR Setup
One AP needs to setup CSR with another AP before the CSR transmission between the two APs
The CSR setup procedure is performed by exchanging request/response frames
Several parameters need to be determined during the CSR setup
  CSR Padding Delay: the time needed for the AP to respond after receiving a CSR Trigger frame addressed to it
  AP ID: a short identifier of the AP used as a shared AP to determine whether a CSR Trigger frame is addressed to it
    Note: the CSR Trigger frame needs to carry the shared AP’s identifier
  Other parameters may also be needed
  Timeout duration: the valid duration of the MAP coordination agreement for CSR
  Minimum TX power: the minimum TX power to use as a shared AP

## Slide 4: CSR Setup
Considering the setup procedure is also needed for other multi-AP coordination schemes, we assume a unified setup procedure can be used for all the schemes
We can define MAP Coordination Setup Request/Response frames to setup a MAP Coordination agreement
  Defined as a UHR Action frame
  The enabled schemes are indicated
  Corresponding parameters are carried
    Common parameters: AP ID; timeout value
    Specific parameters for CSR: CSR padding delay, min PWR
Order | Meaning
1 | Category
2 | UHR Action
3 | Dialog Token
4 | MAP Control
5 | CSR Parameter Set
 | ……
CSR Enabled
……
MAP Control field
Bits:
1
AP ID
Timeout
……
12
8

## Slide 5: Measurement
In CSR transmission, APs need to know the pathloss between the scheduled STAs and the interfering APs. Hence, a pathloss measurement needs to be done before the CSR transmission
  AP1 needs to know the pathloss between AP2 and its non-AP STA
  If AP1 is the sharing AP, AP1 needs to use the pathloss to control the power of AP2
  If AP1 is the shared AP, AP1 needs to use the pathloss to estimate the SINR at the non-AP STA
Existing measurement protocol can be used
  Beacon Request/Response
  Other procedures can also be defined
  NDP based measurement
Pathloss needs to be measured
1
2

## Slide 6: Data Transmission
If an MAP coordination agreement has been setup between two APs, one AP may transmit a CSR Trigger frame to the other AP to initiate CSR transmission within its TXOP.
  Note that if an AP has setup CSR with two or more other APs, then the AP may initiate CSR transmission with two or more APs using one CSR Trigger frame
The AP that transmits the CSR Trigger frame is the sharing AP, the AP that receives the CSR Trigger frame is the shared AP.
The CSR Trigger frame is a new type of Trigger frame,
  In the Common Info field:
    The Trigger Type field is set to a new value, e.g., 9
    The UL Length field (needs to be renamed) is set to the PPDU length of the PPDU transmitted by the shared AP
    The AP TX Power field is set to the sharing AP’s transmit power
    The settings of the other fields are TBD
  In the User Info field:
    The AID12 field is set to the AP ID of the shared AP
    Other bits (e.g., bits [20:38]) can be redefined to carry the Max TX power of the shared AP
  Dummy user info fields can serve as padding to satisfy the CSR padding delay indicated by the shared AP

## Slide 7: Conclusion
We propose several design aspects of CSR, including setup, measurement and data transmission
A unified setup procedure for multi-AP coordination can be defined to support CSR, as well as other modes
For measurement, the existing Beacon request/response procedure can be used, other procedures (NDP based measurement) may also need to be defined
For data transmission, we propose to define a new type of Trigger frame as CSR Trigger frame to initiate the CSR transmission

## Slide 8: Straw Poll
Do you agree to define Coordinated Spatial Reuse as a Multi-AP Coordination mode where
  A sharing AP can initiate simultaneous transmissions of more than one APs on the same frequency resource within its obtained TXOP
  The transmission duration and the transmit power of the APs are specified by the sharing AP
  The simultaneous transmissions are initiated by a CSR Trigger frame transmitted by the sharing AP

## Slide 9: References
[1] 11-20-1935-66-00be-Compendium of straw polls and potential changes to the Specification Framework Document - Part 2
[2] 11-22-1512-00-0uhr-Multi-AP Coordination for UHR
[3] 11-22-1515-00-0uhr-A candidate feature: Multi-AP
[4] 11-22-1516-00-0uhr-Considerations on Multi-AP Coordination
[5] 11-22-1567-00-0uhr-C-OFDMA throughput analysis in various mesh backhaul scenarios
[6] 11-22-1530-00-0uhr-Multi AP coordination for next-generation Wi-Fi
[7] 11-22-1556-00-0uhr-Multi-AP Coordination for Low Latency Traffic Delivery
[8] 11-22-1394-00-0uhr-Virtual BSS And Multi AP Transmissions
[9] 11-22-1822-00-0uhr-Recap on Coordinated Spatial Reuse Operation
[10] 11-22-1895-00-0uhr-Thoughts on M-AP Coordination Principles
[11] 11-22-1899-00-0uhr-Multi-AP Operation for Low Latency Traffic Delivery - Follow up
[12] 11-22-1821-00-0uhr-System Level Simulation of Co-BF and Joint Tx
[13] 11-22-2188-00-0uhr-Joint Transmission for UHR -A Refresher and New Results
[14] 11-23-0041-00-0uhr-Considerations on Coordinated TDMA
[15] 11-23-0058-00-0uhr-Spatial Reuse in Coordinated M-AP for UHR
[16] 11-19-0103-01-0eht-ap-coordination-in-eht
[17] 11-20-0576-01-00be-coordinated-spatial-reuse-protocol
[18] 11-20-0107-01-00be-multi-ap-coordination-for-spatial-reuse
[19] 11-23-0739-01-0uhr-follow-up-on-coordinated-tdma-c-tdma
[20] 11-23-0226-02-0uhr-coordination-of-r-twt-for-multi-ap-deployment
[21] 11-23-1037-00-0uhr-performance-of-coordinated-spatial-reuse
[22] 11-23-0297-00-0uhr-rtwt-for-multi-ap
[23] 11-23-0261-00-0uhr-tdma-for-wifi-8
[24] 11-23-0776-01-0uhr-performance-of-c-bf-and-c-sr
[25] 11-23-0250-00-0uhr-ap-coordination-with-r-twt
[26] 11-23-1023-02-0uhr-coordinated-spatial-reuse-in-a-4-ap-topoplogy
[27] 11-23-1085-00-0uhr-thoughts-on-coordinated-tdma
[28] 11-23-1087-00-0uhr-announcement-for-r-twt-coordination
[29] 11-22-1822-00-0uhr-recap-on-coordinated-spatial-reuse-operation
[30] 11-23-0616-00-0uhr-overhead-analysis-of-coordinated-spatial-reuse
[31] 11-23-0668-02-0uhr-coordinated-measurement
[32] 11-23-0860-00-0uhr-further-thoughts-on-coordinated-twt
[33] 11-23-0768-00-0uhr-discussion-on-c-ofdma-operation