## Slide 1: TGbi, OTA MAC Address transitions
Date: 2023-11
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: OTA MAC Address transitions
We have a set of Requirements that concern a non-AP STA changing its MAC address while associated with an AP.
Options discussed:
All STAs change address at once
AP proposes Epochs (minimum and maximum)
AP or STA controls
RA and TA independent

## Slide 3: All Change together
AP would issue command and all STAs change
Points:
Listener cannot know who is who
Needs command to change
  Could be on demand, or fixed time, and/or countdown.
Traffic interrupted
  May not be convenient for the STA, e.g., in a voice call
  Needs a period when old and new addresses still in use
Requires sets of calculations to be carried out
  Need to set some pre-known key or scheme to know new addresses.

## Slide 4: Epochs
AP indicates a minimum and maximum time interval for STAs to change.
Points:
STAs decide when they change, within limits set by AP
  Easy for listener to follow individual changes, hence STA needs to associate in order to confuse.
  Choosing limits may not be straightforward, e.g., if STA on video call
Requires sets of calculations to be carried out
  Need to set some pre-known key or scheme

## Slide 5: AP or STA decides?
Decision to change should be governed by what the STA is doing.
For examples:
If STA in video/voice call, then it should not be forced to change MAC address(es)
If STA is in any active use, then it should not be forced to change MAC address(es)
  YouTube, email, filing in a form, etc.
  If it does change and traffic is the same, makes it easier for listener to work out what happened.
BUT STA can decide.

## Slide 6: RA and TA
Proposal to use independent RA and TA addresses and change (one or both?).
STA transmits packets to AP using address A as TA
AP transmits packets to STA using address B as RA
  i.e., uses a different RA than the received TA.
Certainly increases privacy
Note: Control packets, e.g., ACK, CTS, BA must use same RA as the received packet TA.
  Otherwise, easy to identify the two addresses
  Should be straightforward to implement.
Requires derivation of two addresses per change

## Slide 7: Consider using IRM
IRM – STA provides a new MAC address to the AP during RSN association (4W HS, FILS, PASN). The new address to be used at the next association.
Procedure (very simple):
When STA decides it’s a good time to change, STA associates anew.
  STA would presumably choose time when inactive. STA stays connected
  Appears to listener as a new STA joining. Listener sees STAs joining all the time.
  STA itself decides if aggressive or not on changes
  No computations required,.
Supports individual TA RA
  STA simply provides two addresses each association (96 bits cf. 48)
  Needs separate support indication,, e.g., “IRM Dual capability”
No epoch or changeover period required, STA controls
  This seems right as STA is the device concerned with its privacy.

## Slide 8: IRM?
Meets the privacy requirements
STA decides when to change
Support dual MAC address TA and RA
Does not require new commands or actions
  If required, new ‘RA/TA capability supported’ needs to be added.
Does not require computations or key maintenance
DISCUSSION