## Slide 1: TGbi, OTA MAC Address transitions
Date: 2023-11
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com gsmith@wi-ficonsulting.org

## Slide 2: OTA MAC Address transitions
We have a set of Requirements that concern a non-AP STA changing its MAC address while associated with an AP.
Options being discussed:
All STAs change address at once
AP proposes Epochs (minimum and maximum)
AP or STA controls?
Independent and changing RA and TA

## Slide 3: All Change together Option
AP would issue command and all STAs change
Points:
Listener cannot know who is who
Needs command to change
  Could be on demand, or fixed time, and/or countdown.
Traffic interrupted
  May not be convenient for the STA, e.g., in a voice or video call
  Needs a period when old and new addresses still in use
Requires sets of calculations to be carried out
  Need to set some pre-known key or scheme to know new addresses.

## Slide 4: Epochs
AP indicates a minimum and maximum time interval for STAs to change.
Points:
STAs decide when they change, within limits set by AP
  STA needs to “associate” in order to confuse listener
    Easy for listener to follow individual changes if not
  Choosing limits may not be straightforward, e.g., if STA on video call
Requires sets of calculations to be carried out
  Need to set some pre-known key or scheme

## Slide 5: AP or STA decides?
STA is most interested in privacy.
Decision to change should be governed by what the STA is doing.
For examples:
If STA in video/voice call, then it should not be forced to change MAC address(es)
If STA is in any active use, then it should not be forced to change MAC address(es)
  Gaming, YouTube, email, filing in a form, etc.
  If it does change and traffic is the same, makes it easier for listener to work out what happened.
BUT STA will know if in a pause or such and can decide.

## Slide 6: RA and TA Option
Proposal to use independent RA and TA addresses and change (one or both?).
STA transmits packets to AP using address A as TA
AP transmits packets to STA using address B as RA
  i.e., uses a different RA than the received TA.
Certainly increases privacy
Note: Control packets, e.g., ACK, CTS, BA must use same RA as the received packet TA.
  Otherwise, easy to identify the two addresses
  Should be straightforward to implement.
Requires derivation of two addresses per change

## Slide 7: Consider using IRM
IRM – STA provides a new MAC address to the AP during RSN association (4W HS, FILS, PASN). The new address to be used at the next association.
Procedure:
When STA decides it’s a good time to change, STA associates anew – BUT stays connected
  STA would presumably choose time when inactive. STA stays connected
  Appears to listener as a new STA joining. Listener sees STAs joining all the time.
  STA itself decides if aggressive or not on changes
  No computations required,.
No epoch or changeover period required, STA controls
  This seems right as STA is the device concerned with its privacy.

## Slide 8: Individual TA RA
IRM Supports individual TA RA
  STA simply provides two addresses each association (96 bits cf. 48)
  Needs separate support indication,, e.g., “IRM Dual capability”
First time associates and uses single TA/RA
  Provides 96 bit IRMA in KDE or element
    First 48 bits TA, second 48 bits RA (or could specify two IRMA fields
    STA has option to change one or both addresses in KDE or IE.
Initiates new association (soon as practical)
  Uses previously provided TA IRMA to associate, AP recognizes STA and uses previously provided RA IRMA to transmit packets.
Subsequent new associations (after a disconnect) use TA/RA
NOTE: Control Packets should still use RA=TA
  Otherwise, simple to link the two
  Should be simple to implement as is ‘standard operation’ at a low level.

## Slide 9: IRM for connected MAC Address changes?
Meets the privacy requirements
STA decides when to change
Supports dual MAC address TA and RA
Does not require computations or key maintenance
DISCUSSION