## Slide 1: Design Considerations on IMMW
Date: 2023-11-10
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | jianhan.liu@mediatek.com
Julia Feng |  |  |  | 
Shengquan Hu |  |  |  | 
Thomas Pare |  |  |  | 

## Slide 2: Design range target
IMMW targets to enable high-rate short-range communications via assistance or coordination of links on sub-7GHz bands.
  Longer range needs large number of antennas and therefore increases the cost of IMMW products.
mmWave signals experience significant path loss when penetrating walls or other objects and mmWave signals can be easily blocked.
  IMMW group should focus on enabling line of sight (LOS) communications.
We recommend the design range targe should be 5-10m in LOS.

## Slide 3: Channel Bandwidth
IEEE 802.11ax/be can support maximum bandwidth 320MHz in one link.
60GHz has multi-Giga Hz bandwidth available.
IMMW should targets for higher data rate communications to gain market traction.
We suggest the base bandwidth of IMMW should be greater or equal to 320MHz.
Multiple channel bandwidth can be supported, for example, 320MHz, 320*2=640MHz, 320*4=1280MHz and 320*8=2560MHz.

## Slide 4: Channelization (1)
We can align IMMW channelization with 11ad/11ay channelization
Each 320 MHz channel is within a 360MHz frequency subblock.

## Slide 5: Channelization (2)
To achieve higher spectrum utilization, we can choose to not align IMMW channelization with 11ad/11ay channelization
We can have consecutive non-overlapping 320MHz, 640MHz, 1280MHz and 2560MHz channels or just overlapping the large channels with 640MHz.

## Slide 6: On Subcarrier Spacing
Due to large phase noise, large subcarrier spacing should be used in IMMW.
We can have the fixed subcarrier spacing for different channel bandwidths (like IEEE 802.11 standards)
  For example, the subcarrier spacing can be 78.125*2^5=2.5MHz
We can also introduce scalable subcarrier spacing (like 3GPP)
  For example, subcarrier spcating can be 78.125*2^n, n=4, 5, …
 | 11ax/be (Sub-7GHz) | 11ad/ay (60GHz) | 3GPP (60GHz)
Subcarrier Spacing | 78.125kHz | 5.15625MHz | • 120/240KHz for FR2, by Rel.15~16 • 480/960kHz for FR2-2, by Rel.17

## Slide 7: Supported Data Rates
Minimum data rate is associated with base channel bandwidth and the lowest MCS.
  For reasonable power efficiency of IMMW, we think the minimum data rate should be higher than 100Mbps.
Maximum data rate is associated with the largest channel bandwidth, the maximum number of spatial streams and the highest MCS.
  To reduce the complexity, we recommend the number of spatial streams are 2 or 4 and the highest modulation should be 64QAM or 256QAM.

## Slide 8: Summary
We present general thoughts on designs target, channel bandwidth, numerology and supported data rates.