## Slide 1: End-to-end QoS
Date: 2023-08
Authors:

## Slide 2: Introduction
There are several emerging use cases such as XR that requires end-to-end one-way latency
The use cases encompass the case where the two peers are connected through an AP
Problem statement
  The compute device may be a legacy/general purpose computer/mobile-phone device that may not be aware of the application QoS
    Hence the channel access at the compute device may use Best-Effort AC, which makes the latency worse in presence of other traffic

## Slide 3: Proposal
Introduce a new concept of end-to-end QoS with the following procedure
  Device A, which is aware of the application/QoS will setup a QoS with the AP for the peer generic device (Device B)
  AP applies the QoS specified by Device-A for DL access for the packets sent by Device A to Device B
  AP installs the QoS specified by Device A, onto Device B for the UL access of the IP data flows specified by Device A
    AP installs the QoS for the IP flow on Device-B based on the request the AP received from Device-A

## Slide 4: End-to-end QoS Setup: Signaling details
AP applies the QoS specified by Device-A for DL access for the packets sent by the Device A to Device B
  The above specified QoS will not be applied for other packets destined for Device B
  This part does not need to involve Device B at all so it applies even to legacy devices (just a note).
AP installs the QoS specified by Device A, onto Device B for the UL access of the IP data flows specified by Device A
  Device B to support AP configured QoS (i.e., AP installing UL packet filter) so Device B will need to be 11be or beyond
  Device A will need to prove to the AP that it is receiving UL packets from Device B (as opposed to some random device asking the AP to set things up in Device B). AP can verify that by checking the UL packets from Device B are indeed destined for Device A.
  AP installs the QoS for the IP flow on Device-B based on the request the AP received from Device-A
If Device B does not support UL QoS (UL packet filter) installation by the AP (e.g., Device B is pre-11be), the AP can use triggered based UL access to serve Device B to meet the end-to-end QoS

## Slide 5: 2 Cases: DL Flow and UL Flow

## Slide 6: Conclusion
In this presentation, we presented a mechanism to setup a QoS with the AP for a remote STA
This enables the AP to deliver the proper e2e QoS for the traffic between a STA and a remote STA via the AP