## Slide 1: Preemption techniques to meet low-latency (LL) targets
Date: 2024-01-10
Authors:

## Slide 2: Background & Problem Statement
One of the goals of UHR is to improve latency for latency sensitive traffic
Latency sensitive traffic can be classified into two groups:
  Periodic and aperiodic traffic
Techniques such as Coordinated AP/Medium Access could handle the periodic latency sensitive traffic
  The scope of this document is to consider aperiodic latency sensitive traffic
In the baseline, when a new latency sensitive packet arrives, the AP/non-AP STA will need to wait until the end of the ongoing TXOP (see [1-4])
  This document proposes mechanisms for the following two cases:
    Case 1: Preempt the DL TXOP to send UL latency sensitive traffic
    Case 2: Preempt the UL TXOP to send DL latency sensitive traffic

## Slide 3: Case 1: Preempt DL TXOP to Send UL
UL LL traffic arrived during a DL TXOP:
DL LL traffic arrived during a DL TXOP:
11bn need to address this issue (main focus in these slides)

## Slide 4: Solution for DL LL traffic arriving during a DL TXOP
Simple MAC solution using baseline mechanisms. Covers most of the cases.

## Slide 5: Solution for UL LL traffic arriving during a DL TXOP
Preemption using baseline mechanisms
Notes: Separate DL PPDU and NFRP

## Slide 6: Solution for UL LL traffic arriving during a DL TXOP
AP grants LL devices an opportunity to contend within its DL TXOP
  Handles the cases when AP doesn’t have the knowledge of which clients has LL traffic
Advantages of allowing EDCA explicitly by the AP
  Enables the AP to inject DL LL traffic that arrives during a DL TXOP
  AP’s announcement can be heard by all STAs in the BSS
  Reduces contention with DL access for LL data
AP sends a PR Enabled indication to LL clients
  could be sent in a PHY header of DL PPDU or BA sent by the AP
  AP includes the granted duration limit for the EDCA LL transmissions
Client starts contending after the DL PPDU/BA by ignoring the NAV set by the AP in previous frames (e.g., AP uses Multiple protection settings)
  Client use only a random backoff count with TBD max Time slots
EDCA-based Preemption mechanisms

## Slide 7: Solution for UL LL traffic arriving during a DL TXOP
EDCA-based Preemption mechanisms (Cont’d)

## Slide 8: Solution for UL LL traffic arriving during a DL TXOP
EDCA-based Preemption mechanisms (Cont’d)
Alternatively, to reduce hidden node problem, the AP can allocate one RU for all the LL clients to transmit the PRI along with the BA

## Slide 9: Case 2: Preempt UL TXOP to Send DL
DL LL traffic arrived during an UL TXOP:
11bn need to address this issue (main focus in these slides)

## Slide 10: Solution for DL low latency traffic arriving during a UL TXOP
AP takes over the rest of the TXOP if the client allows
Client grants Low Latency clients (“PR allowed”) an opportunity for AP to take over the rest of the TXOP

## Slide 11: Summary
We discussed the TXOP preemption to enhance the latency for event driven traffic use cases ([1]-[4])
The design should be simple, efficient, and scalable
Both Trigger-based as well as EDCA based preemption are considered
  Trigger-based comes for free from previous amendment
  EDCA based can be used in those cases when trigger-based is not possible/practical
EDCA based preemption enables TXOP preemption with SU PPDU transmissions within a PIFS duration using PR enabled/PRI
  This minimize the unnecessary overhead of polling the LL clients (e.g., NFRP/NFR, BSRP/BSR..)
  Significant gain from initial simulations

## Slide 12: References
[1] 11-23/0018, Low latency support in UHR
[2] 11-23/0092, Preemption
[3] 11-23/798, Low latency traffic report
[4] 11-23/1194, Overlapped Indication to Support Preemption

## Slide 13: SP
Do you support to define a mechanism in 11bn for a TXOP holder to allow a STA associated with the TXOP holder to preempt the TXOP holder's frame exchange sequence for delivery of low latency traffic
  NOTE: The TXOP holder can be an AP or a non-AP STA
  NOTE: The policy for TXOP holder allowing preemption is TBD

## Slide 14: Appendix

## Slide 15: Initial Simulation Results for Case 1
Scenario, simulation setup
1 AP
5 STAs: 1 DL legacy + N Uplink Low Lat(LL) devices (N= 1, 2, 4)
Non-LL STAs traffic: Full buffer (DL) between AP and Legacy clients; AC_VO
LL STAs traffic: 1500 bytes every 40 ms; AC_VO
  LL traffic uniformly randomized within interarrival interval
Preemption mode with xIFS = PIFS, AP TXOP limit = 5ms with PPDU limit = 1ms
No hidden nodes
No OBSS or other In-BSS loading

## Slide 16: Initial Simulation Results (Cont’d)
=> Significant Gain with AP permitted Low Latency EDCA Access
Chart: 95 Percentile Latency (ms)
| 1 LL STA | 2 LL STAs | 4 LL STAs
w/ TXOP Preemption (5 msecs TXOP) | 1.976 | 1.999 | 2.065
Legacy Long PPDU (5 msecs TXOP) | 32 | 51 | 105
UL/DL collision is one of the key contributors for bad latency for legacy operation