## Slide 1: MAC header protection – follow-up
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho |  |  |  | 
Jouni Malinen |  |  |  | 
Alfred Asterjadhi |  |  |  | 
George Cherian |  |  |  | 
Gaurang Naik |  |  |  | 
Date: 2023-11-02

## Slide 2: Background
UHR is focused on improving reliability, reducing latencies and lowering power consumption at devices.
In order to achieve these goals, UHR will rely on signaling information via the MAC header fields (such as A-Control) or via Control frames (e.g., Trigger etc).
  However, Control frames and several fields in the MAC header are not protected.
Several contributions have highlighted the need for protecting these fields and frames to help UHR meet its objectives [1, 2, 3, 4]
This contribution provides additional details on MAC header protection and considerations for selecting the security parameters to enable this protection.

## Slide 3: Factors to consider (recap)
The header protection scheme needs to account for field values getting updated when an MPDU is retried.
  Such as Retry bit, PM bit, A-Control field etc
In addition, the scheme must not require re-encryption of the payload of an MPDU during a retry
Consequently, MAC header protection cannot be combined with MPDU encryption.
  In other words, the two need to be separate processes and only the header protection step is performed when an MPDU is retried.

## Slide 4: Overview of the proposal
Protection is provided via integrity check
A MIC is generated based on (subset of) MAC header fields.
Since the contents of the header fields can change when an MPDU is retried, a fresh MIC is generated (only) for the header fields each time an MPDU is retried
  Note, the payload of the MPDU is not re-encrypted

## Slide 5: Parameters needed for MIC generation
MIC generation will require the following parameters:
  A temporal key (TK`)
  A packet number (PN`)
  Address 2 (A2) field which carries the transmitter MAC address
  Fields of the MAC header that need protection
A2||PN` is used to generate a Nonce
Next, we examine additional considerations for TK` and PN`

## Slide 6: Proposal for temporal key (TK`) for MIC computation
From security point of view, using the same key in two different algorithms is a bad practice
  As it can make related key attacks possible.
  Therefore, TK` cannot be the same as TK (which is used for encrypting the MPDU payload)
Therefore, a separate TK` is generated during association.
  TK` will be identified with the corresponding value in the Key ID field
The separate TK` can also be used for (individually addressed) Control frame protection

## Slide 7: Proposal for packet number (PN`) for MIC computation
The PN` provides protection against replay attacks
  Same functionality as PN used during the payload encryption
However, the usage of PN` differs from PN in the following aspects:
  The PN value remains the same when an encrypted MPDU is retransmitted. In contrast, a new PN` value is required each time an MPDU is (re)transmitted
    a new MIC is computed for each (re)transmission.
Packet number required for (individually addressed) Control frame protection can also be drawn from the PN` space

## Slide 8: In summary
This contribution proposes to protect fields in the MAC header via integrity check
  A new MIC is generated for the header fields each time an MPDU is (re)transmitted
A separate TK` is generated during association for header MIC generation
  Same TK` can be used for protecting Control frames
Packet Number (PN`) used for generating the MIC (for header field or Control frame protection) is drawn from a different space than that used for MPDU encryption

## Slide 9: References
[1] 11-23/286: Trigger frame protection [Po-Kai Huang et al. (Intel)]
[2] 11-23/352: Enhanced security discussion [Liwen Chu et al. (NXP)]
[3] 11-23/356: MAC Header Protection [Abhishek Patil et al. (Qualcomm)]
[4] 11-23/1102: Security Enhancement follow up [Liwen Chu et al. (NXP)]

## Slide 10: SP #1
Do you support to define a mechanism in TGbn that protects the MAC header for individually addressed Data and Management frames?