## Slide 1: Signaling details for header protection
Authors:
Name | Affiliations | Address | Phone | email
Abhishek Patil | Qualcomm |  |  | appatil@qti.qualcomm.com
Duncan Ho |  |  |  | 
Alfred Asterjadhi |  |  |  | 
George Cherian |  |  |  | 
Gaurang Naik |  |  |  | 
Date: 2023-11-03

## Slide 2: Introduction
Enhancing security in 802.11 is one of the goals of UHR
  To that effect, UHR will provide mechanisms to protect certain Control frames and fields within the MAC header.
Previous contribution (see 23/1888)
  proposed protection of the MAC header fields via integrity check
  explained the need for generating a separate key and deriving PN from a separate space
In this contribution we provide details on where, within a frame, the additional security information for header protection can be carried.

## Slide 3: Background: structure of a MAC frame

## Slide 4: Location for carrying header security info
The additional security information for header protection would consist of the following:
  Key ID (to identify the key used for generating the MIC for the header fields)
  PN
  MIC
The selected location must:
  Preserves the existing format of the initial fields in a frame (e.g,, RA, TA, BSSID, duration etc) so that other STAs in the neighborhood that receive this frame can derive the necessary information and take appropriate actions (such as setting the basic or intra NAV).
  Be able to provide an early indication to abort further processing (e.g., decryption) of the MPDU by the intended recipient if the header integrity check fails.

## Slide 5: Location for carrying header security info
Propose to include the above parameters in the early portion of the frame (before the GCMP header) so that the recipient can quickly generate a local MIC of the header fields and compare it with the received MIC. Applies to:
  An individually addressed Data or Mgmt frame sent to a UHR STA
    This frame does not have to be carried in a UHR PPDU
  May apply to some group addressed frames (see thoughts in later slides)

## Slide 6: Location for carrying header security info
For group addressed Mgmt frame:
  The security information is carried in a (new) element
    Similar to beacon protection
    Pre-UHR STAs will ignore the new IE while UHR STAs will process it
  Alternatively, if all the recipients are only UHR STAs, the information is carried before the GCMP header (previous slide).
    Not a preferred option since the recipient needs to guess the location of the information based on other factors such as:
      Frame sent in a UHR PPDU, or a frame carried in a group addressed RU that is specific to UHR STA(s)
For a group addressed Data frame whose recipients includes pre-UHR STAs.
  Option 1: no protection (preferred)
  Option 2: duplicate the contents of the frame in a UHR PPDU or UHR specific RU and include the security information before the GCMP header (previous slide).

## Slide 7: Summary
This contribution provides the signaling details for carrying the additional security information for header protection.
  Preserves the initial format of the frame for backward compatibility
  While providing the information sufficiently early enough for the intended recipient(s) to decide next course of actions for the received frame.
  Maintains legacy compliance for backward compability.

## Slide 8: SP #1
Do you support that an MPDU that has its MAC header fields protected will include the following fields
  A field to carry the PN used for generating the MIC for the fields in the MAC header
  A field to carry the key ID to identify the key used for generating the MIC for the fields in the MAC header
  A field to carry the MIC generated across the fields of the MAC header
  And that the above fields are different from the fields used to carry the PN, Key ID and MIC respectively for the encrypted payload of the MPDU?