## Slide 1: High Leve Thoughts on IMMW
Date: 2023-11-12
Authors:
Name | Affiliations | Address | Phone | email
Bin Tian | Qualcomm |  |  | btian@qti.qualcomm.com
George Cherian |  |  |  | 
Rolf De Vegt |  |  |  | 
Abhishek Patil |  |  |  | 
Lin Yang |  |  |  | 
Sameer Vermani |  |  |  | 

## Slide 2: Overview
Market trend demands WLAN solutions to support emerging high throughput and/or low latency applications, especially for high density device deployment in both enterprise and home environments
  XR, gaming, wireless display, device sharing/collaboration, etc.
mmwave band has many attractive advantages
  Abundant spectrum available in most geographical regions
  Directional transmission and large propagation loss lead to low interference level and more reuse opportunities
New integrated mmwave (IMMW) project needs to learn from past mmwave projects and defines its scope to focus on
  Integrated with sub-7GHz link to overcome the range, mobility and reliability challenges
  Minimizing the complexity and add-on cost from sub-7GHz support
  Enhancing link robustness and low latency performance

## Slide 3: Band Support
IMMW needs to support both 60 GHz and 45 GHz band
  But designs need to be harmonized across two bands
Country | Spectrum (GHz) | EIRP Limit | Notes
USA, Canada | 57-71 | 40dBm (avg)/43dBm/(peak) | 
Europe/CEPT | 57-71 | 40dBm (avg) | 
Japan, South Korea, Singapore, Austria, New Zealand, Southeast Asia | 57-66 |  | 
Mexico, Brazil | 57-64 |  | 
China | 59-64 | 44dBm(avg)/47dBm(peak) | Currently on hold
 | 42.3-49 | 36dBm (peak) | With 1080 or 540MHz channelization

## Slide 4: Thoughts on IMMW PHY
The highest design priorities: reduce complexity and power consumption
Leverage sub-7GHz PHY design
  Enable baseband hardware reuse and minimize add-on cost
Not chasing peak data rates. Few hundreds of Mbps to 1.5Gbps PHY rate can satisfy the need of most applications
  One or two bandwidth modes are enough. E.g. 320 and 640MHz
  Focus on the most useful MCSs (e.g. up to 16QAM)
    60/45GHz band has abundant spectrum but generally power limited. Higher order QAM is not a good trade off
    Higher phase noise in 60GHz/45GHz band also makes it more challenging to support high MCSs
  Single spatial stream. Open to discussion if more spatial stream is needed
Single user transmission only

## Slide 5: Thoughts on IMMW MAC
Leverage 11be MLO architecture
  Include mmwave link as part of MLO along with other sub7 links
  Seamless offloading to Sub-7 during inadequate mmwave coverage
Minimize the management frames in this band
  Conduct discovery, authentication, and other management procedures on sub7GHz links
  Helps to fully utilize the spectrum for delivering the payload
Enhance beam search process and management
  Assistance from sub-7 links for faster beam search
Utilize baseline mechanisms with added rules for reducing MAC inefficiencies
  Utilize the triggered mode operation with added rules (say, MU EDCA=0)
  Utilize TWT framework to improve power-save, and scheduling
  Make the band suitable for predictable latency operations

## Slide 6: Summary
IMMW project has an opportunity to design new mmwave solutions to utilize the abundant spectrum and address market need
However, the commercial success of IMMW technology depends on whether complexity, cost and power consumption are given high priorities in the design
  IMMW SG needs to define the project scope to reflect these priorities
We shared some high-level thoughts on the PHY and MAC directions

## Slide 7: References
22/0481, Integrated mmWave study group formation, Rolf de Vegt (Qualcomm)
22/0046, Next generation after 802.11be, Laurent Cariou (Intel)
22/1083, Next Generation SG formation, Ming Gan (Huawei)
22/1395, Thoughts on high frequency band, Myeongjin KIM (Samsung)
22/1580, a Perspective On Proposed Uhr Features For Enterprise Use Cases, Brian Hart (Cisco)
22/1398, RR-TAG mmWave Spectrum Survey, Rich Kennedy (Unlicensed Spectrum Advocates)
22/1466, Potential PHY Features for UHR, Eunsung Kim (LG)
22/1865, Considerations on the PHY for 60 GHz, Miguel Lopez (Ericsson)
22/1872, Considerations on PHY Designs for mmWave Band, Eunsung Park (LG)
22/1884, mmWave operation for UHR, Laurent Cariou (Intel)
23/0066, Thoughts on Utilizing mmWave, Mengshi Hu (Huawei)