## Slide 1: Transmission Method of Low Latency Traffic
Date: 2023-11-13
Authors:
Name | Affiliation | Address | Phone | Email
Insun Jang | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | 
 |  |  |  | js.choi@lge.com
Sunhee Baek |  |  |  | 
 |  |  |  | sunhee.baek@lge.com
Yelin Yoon |  |  |  | yl.yoon@lge.com
Geonhwan Kim |  |  |  | geonhwan.kim@lge.com
Dongju Cha |  |  |  | dongju.cha@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sanggook Kim |  | 10680 Treena St, San Diego CA 92131 , USA |  | sanggook.kim@lge.com

## Slide 2: Introduction
According to the PAR for 11bn (UHR), we have an important goal that is to improve the 95th percentile of the latency distribution
In UHR SG with the goal, many contributions have investigated method(s) based on different views in UHR, e.g.,
  Classification/Prioritization of low latency (LL) traffic [1]
  Preemption of low latency traffic in TXOP [2]-[7]
  Optimized Scheduling [8], [9]
  EDCA channel access for Low Latency [10]
  Low Latency Traffic Out-of-Delivery [11], [12]
In this contribution, we share our views on how to transmit low latency traffic (LLT) based on preemption in a TXOP

## Slide 3: Recap: Restricted TWT and SCS in 11be
In 11be, based on a lot of discussions on low latency, we had main mechanisms:
  Restricted TWT for transmitting LLT with negotiated TID and TXOP rules
  Enhanced SCS for specifying traffic characteristics/pattern and prioritizing the traffic with a QoS characteristics IE in terms of DL/UL/Direct
Thanks to those mechanisms, the AP can properly schedule frame transmission/rTWT by referencing QoS characteristics IE
  Even though those can reduce the latency on average, we still have some issues on the delivery of some LLT under target delay bound (e.g., non-deterministic/event-driven LLT) [13] on pre-determined schedule
  The detailed issue is shown in the next slide

## Slide 4: Basic Issue
A STA may need to transmit LLT to one or more target STA(s)
  Such LLT has just arrived or already queued with requirements (e.g., it should be transmitted TX within Xus, quickly)
Basically, while the STA would perform EDCA, the STA can experience the followings:
  Significantly congested channel and NAV by the (long) TXOP by another STA
  As a result, the LLT can be out-of-date before obtaining a TXOP
We can consider the issue on how a STA can transmit LLT to satisfy the LLT requirements even though another STA has already occupied the channel (called Preemption)

## Slide 5: What We Should Handle
Generally, we can have 3 phases
  1st Negotiation
    Capabilities for Preemption of LLT TX
    Restrictions, e.g., what kind of LLT can be transmitted or which STA can transmit based on the preemption (e.g., using SCS/rTWT, LLT classification) to avoid non-LLT TX
  2nd Preemption
    How a STA can transmit LLT in a TXOP of another STA
  3rd (Post) Management
    Depending on the case, we may give an incentive to TXOP holder (who triggered LLT TX) or may impose a penalty to TXOP responder (who transmitted LLT)

## Slide 6: Overview of Preemption Phase
Basically, a TXOP holder can transmit its LLT to one or more TXOP responder(s) anytime in its TXOP
However, without the aid of TXOP holder in most of cases,
  TXOP responder cannot transmit LLT to target STA(s) when needed
    e.g., to AP without Trigger frame
  Other STAs (not TXOP responder) cannot transmit LLT to target STA(s)
Therefore, we need mechanism(s) where the TXOP holder can provide opportunities for the TXOP responder or other STA(s) to transmit urgent LLT in its own TXOP
  In this document, we consider the cases, i.e., TXOPs obtained by AP or non-AP STA (DL TXOP or UL TXOP)

## Slide 7: Observations on UL TXOP
During an UL TXOP, an AP (TXOP responder) may need to transmit LLT to target STAs (including STA 1 (TXOP holder)), which requires that STA 1 needs to share the TXOP with the AP
On TXOP holder (STA 1) side,
  STA 1 needs to transmit Triggering Information that would indicate at least it asks if the TXOP responder (AP) needs to transmit LLT using its TXOP
On TXOP responder (AP) side,
  (In response to Triggering Information), AP needs to transmit LLT Information that would indicate at least it needs to transmit LLT using the current TXOP to STA
    TXOP responder may provide additional information, e.g., LLT buffer status, delay bound
    Such information could be transmitted in a unsolicited way without triggering info

## Slide 8: Preemption Signaling in UL TXOP
We should design where and how the Info can be carried carefully
  Triggering Info can be carried in a triggering PPDU/frame (e.g., PHY header, Trigger frame)
  LLT Info can be carried in a responding frame (e.g., control response frame)
    For example, the AP can utilize transmitting BA frames including the information of LLT presence

## Slide 9: Preemption Signaling in UL TXOP
As an alternative without Triggering Info, during frame exchanges, the AP may inform the TXOP holder (STA 1) of LLT presence, e.g., through BA frame
  It could help the STA grant its TXOP to the AP
  The STA identifying the information may transmit a frame that enables LLT transmission from the AP
    The STA may provide additional information, e.g., available duration in TXOP

## Slide 10: Observations on DL TXOP
During a DL TXOP, a STA 1 (TXOP responder) or other STAs may need to transmit LLT to AP (TXOP holder), which requires that the AP needs to trigger LLT TX
On TXOP holder (AP) side,
  AP needs to transmit a Triggering Information would indicate at least it asks if the TXOP responder and other STA(s) needs to transmit LLT
    TXOP holder may provide additional information, e.g., criteria of LLT Info TX
On TXOP responder (STA 1) or other STA(s) side,
  (In response to Triggering Information), the STAs need to transmit LLT Information that would indicate at least it needs to transmit LLT to AP
  Recipient STA(s) may provide additional information, e.g., LLT buffer status, delay bound
    Such information could be transmitted in a unsolicited way without triggering info

## Slide 11: Preemption Signaling in DL TXOP
Likewise, we should design where and how the Info can be carried
  Triggering Info can be carried in a triggering frame (e.g., Trigger frame, PHY header) that should be a method to trigger the LLT Info from multiple STAs
  LLT Info can be carried in a responding frame (e.g., using A-control, control response frame)
    Depending on the design of Triggering Info, channels on which STAs transmit LLT Info can be overlapped (e.g., PHY header) or non-overlapped (e.g., Trigger frame), which may require to identify STAs

## Slide 12: Discussion on LLT Info TX
TXOP holder can expect no response from any STA due to following reasons
  Any STA has no LLT to be transmitted, so no LLT Info TX
  TXOP responder(s) does not acknowledge (Triggering info is transmitted with QoS Data frame(s) with Ack policy not setting to implicit BAR or Normal Ack)
In this case, PIFS can be used between Triggering Info [2]-[6]
  However, the TXOP holder does not understand whether it is no LLT Info or failure that would degrade the performance
  Therefore, it should require CCA during PIFS, e.g., if BUSY (not decoding any LLT info), it will perform recovery procedures

## Slide 13: Discussion on LLT Info TX
If at least one TXOP responder performs acknowledgement (e.g., BA), SIFS can be used
  TXOP holder can understand it is failure if nothing is received and then recovery will be performed
  The TXOP responder could indicate LLT Info with acknowledgement (e.g., in BA)

## Slide 14: Further Issues for Preemption
Detailed Design
  Signaling of Triggering Info and LLT Info
  LLT Info Transmission with a Proper interval
Restrictions/Rules
  All STAs and their all traffic should not be involved in preemption all the time, e.g., a STA may request LLT TX for non-LLT
  We need to consider what kind of specific things are involved in preemption
Power Saving
  Some STAs may enter doze state during a preemption procedure, e.g., STAs that did not receive TIM indication in UL TXOP, which may be handled

## Slide 15: Conclusion
In this contribution, we’ve shared our views on how to transmit low latency traffic (LLT) based on preemption in a TXOP
  It efficiently enables LLT transmission of a STA in another STA’s TXOP
    UL TXOP and DL TXOP can be considered
  We need Triggering Info and LLT Info to enable preemption
    In addition, whether LLT Info is transmitted should be considered
Some further issues should be addressed
  How to signal Triggering Info and LLT Info
  How to handle LLT Info transmission with a proper interval
  How to participate/negotiate preemption based on restrictions/rules

## Slide 16: Straw Poll 1
Do you agree that 11bn supports a mechanism where
  A TXOP holder solicits the information about whether low latency traffic is desired to be transmitted from a STA associated with the TXOP holder so that the TXOP holder can allow the STA to transmit low latency traffic in its TXOP?
    TXOP holder can be an AP or a non-AP STA
    Signaling is TBD

## Slide 17: Straw Poll 2
Do you agree that 11bn supports a mechanism where
  A STA, which is not a TXOP holder and associated with the TXOP holder, indicates the information about whether low latency traffic is desired to be transmitted to the TXOP holder?
    TXOP holder can be an AP or a non-AP STA
    Signaling is TBD

## Slide 18: References
[1] 11-23/69r1, Considerations on Latency Improvement
[2] 11-23/18r1, Low latency support in UHR
[3] 11-23/1174r0, TXOP preemption follow up
[4] 11-23/92r0, Preemption for Low Latency Application
[5] 11-23/1229r1, Preemption for low latency application (Follow up)
[6] 11-23/798r0, Low latency traffic report
[7] 11-23/1434r2, Discussions on Low Latency Traffic Delivery in UHR [8] 11-23/936r0, Medium efficient scheduled channel access in next generation 802.11
[9] 11-22/1923r1, Enhanced Trigger-Based Uplink Transmission
[10] 11-22/1065r0, Low latency channel access
[11] 11-23/697r0, QoS enhancements for UHR
[12] 11-23/799r0, Low latency out-of-order delivery
[13] 11-22/1880, Latency and Reliability enhancements for UHR