## Slide 1: Control Frame Protection Follow Up
Date: 2023-11-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Security Enhancement
At least Trigger frame, BAR, BA are protected.
If the RTS frame is required between two peer devices that support control frame protection, the protected MU-RTS is transmitted.
If the Ack frame is required between two peer devices that support control frame protection, the protected MU-STA BA is transmitted.
CPPTK and CPGTK are defined and if the TXOP protection is not needed the CPPTK (through DL MU PPDU) is used.
The MAC header of unicast Data, Management frame is protected.

## Slide 3: Analysis of BA Type and BAR Type
The different BAR types and BA types are defined in 802.11 spec.
The various Trigger frames cover Compressed BAR, Multi-TID BAR, GCR BAR.
The BA solicited by various Trigger frames cover Compressed BA, Multi-STA BA, GCR BA.

## Slide 4: Protected BA Type and BAR Type
The following should be protected BAR types
  Compressed BAR
  Multi-TID BAR
The following should be protected BA types
  Multi-STA BA
    When the Compressed/Multi-STA BA is solicited and the control frame protection is required, the protected Multi-STA BA is used as the responding frame.
Whether GCR BAR and GCR BA are protected is TBD.

## Slide 5: PS-Poll Attack Analysis
For a STA that wakes up through listening interval, an attacker can transmit PS-Poll before the STA’s awaking to ask the AP to transmit the buffered frames for the STA.
  When the STA wakes up, the AP has no buffered frames for it.
The other attack through PS-Poll could also be possible.

## Slide 6: PS-Poll Protection
The QoS Null with protected header is used to replace PS-Poll.
The new defined protected Action (Action no Ack) frame is used to replace PS-Poll.

## Slide 7: Control Frame Protection Indication, KeyID, PN, MIC
For control frame protection indication, key ID:
  Option 1:
    Both the control frame protection indication and key ID are carried in the reserved bits of the Frame Control field of the protected Control frames.
      Unified for all protected control frame
      Justification of option 1: In Control frame, B13 in Frame Control field (More Data subfield) is changed from reserved bit in IEEE Std 802.11TM – 2012 to non reserved bit in IEEE Std 802.11TM - 2016
  Option 2:
    Both the control frame protection indication and key ID are carried before the information for specific recipient(s) in the frame body.
      The different protected Control frame carry the control frame protection indication and the Key ID in different fields.

## Slide 8: Control Frame Protection Indication, KeyID, PN, MIC
For PN, MIC:
  In a protected control frame with the pre-padding FCS, the PN and MIC are right before the pre-padding FCS.
  In a protected control frame without the pre-padding FCS but with the padding, the PN and MIC are right before the padding.
  Otherwise, the PN and MIC are before FCS.

## Slide 9: SP 1
Do you support to protect the Trigger frame?

## Slide 10: SP 2
Do you support to protect Multi-STA BA in 802.11bn and the other variant of BA is TBD?

## Slide 11: SP 3
Do you support to protect Compressed BAR and Multi-TID BAR in 802.11bn, and the other variant of BAR is TBD?