## Slide 1: In-Device Interference Mitigation Follow Up
Date: 2023-11-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: In-Device Interference Mitigation
We proposed the various in-device interference mitigation between wi-fi radio and non-wifi radio:
  The in-device interference in a non-AP/AP MLD is per link characteristics.
  Periodic and aperiodic non-wifi radio activity report to the peer device (AP or STA).
    Start time, duration, interval, influenced channels in unit of 20MHz channel for periodic activity.
  A TXOP responder can decide the duration of the TXOP which is shorter than the TXOP duration selected ty the TXOP holder. The notification can be in any responding frame.
    Such decision should be applied to SU, MU frame exchanges.

## Slide 3: Recap: Subchannel Switch and Dynamic Channel Switch
The subchannel switch works as follows:
  The BSS operating channel is divided by multiple subchannels: primary subchannel, non-primary subchannel(s).
  When the primary subchannel is occupied by an OBSS TXOP (OBSS TXOP 1), the STA/AP switch to a non-primary subchannel until the end of the OBSS TXOP 1.
    The medium recovery is needed when switching to a non-primary subchannel.
The dynamic channel switch works as follows:
  When an AP acquires the medium access right, the AP solicits one or more STAs to switch to the 20 channel(s) that are not covered by the STA’s operating channel.

## Slide 4: Duration in MAC Header (1)
Discussion:
  If the frame body of the unicast frame carries the available time of the responder, the neighbors of the TXOP responder may not be able to use the medium efficiently.
  The CF-End doesn’t help the neighbors of the TXOP responder when the TXOP holder is the AP.
BAR
BA
AP
STA
STA’s available time
A-MPDU
BA
CF-End
STA’s neighbors can’t do the frame exchange
BAR
BA
AP
STA
STA’s available time
A-MPDU
BA
CF-End
Both AP’s neighbors and STA’s neighbors can do the frame exchange
  With the Duration to indicate the available time, the medium usage efficiency can be improved

## Slide 5: Duration in MAC Header (2)
Discussion (cont’d):
  The Duration in MAC header is not suitable when multiple STAs are the TXOP responders when multiple TXOP responders transmit CTS.
  The AP as the TXOP holder may have multiple TXOP responders sequentially or through MU PPDU.

## Slide 6: Duration in MAC Header (3)
Proposal of available time 1:
  The Duration in MAC header is used to indicate the TXOP responder’s available time when the single TXOP responder is solicited.
  The Duration in MAC header of the solicited frame in TB PPDU is used to indicate the TXOP responder’s available time.
  Otherwise, the frame body or HE Control in frame header is used to indicate the TXOP responder’s available time.
Proposal of available time 2:
  The frame body is used to indicate the TXOP responder’s available time.

## Slide 7: In-device Non-wifi Radio Notification 1
When a STA enables dynamic channel switch and/or secondary channel usage operation and has active in-device non-WiFi radio, the STA can announce the interfered 20MHz channel(s) that are covered by the BSS operating channel if the AP enables the subchannel switch operation.
  The interfered 20MHz channel(s) may not be covered by the STA’s operating channel.
  The interfered 20MHz channel(s) can be reported because of the periodic non-WiFi activity or non-periodic non-WiFi activity.

## Slide 8: Tx Parameter Restriction per Non-WiFi Radio Activity
A STA notifies its Tx parameter restriction per its non-wifi radio activity. The AP selects the Tx parameters in the Trigger frame for the STA per STA’s request.
  The Tx parameters could be whether the TB PPDU can be solicited by the AP and the frame type being carried in the TB PPDU if the solicited TB PPDU is allowed.
  The Tx parameters could be (but not be restricted) BW, the location of useful channel, MCS restriction (maximal MCS, minimal MCS), the Tx power, the Nss.

## Slide 9: Rx Parameter Restriction per Non-WiFi Radio Activity
A STA notifies its Rx parameter restriction per its non-wifi radio activity to its peer device. The peer AP or STA selects appropriate Tx parameters to transmit its PPDUs to the STA.
  The Rx parameters could be (but not be restricted) BW and available channel bitmap, MCS restriction (maximal MCS, minimal MCS), the Rx power, the Nss.
An AP notifies its Rx parameter restriction per its non-wifi radio activity to its peer device(s). The associated STA selects appropriate Tx parameters to transmit its PPDUs to the STA.
  The Rx parameters could be (but not be restricted) BW, MCS restriction (maximal MCS, minimal MCS), the Rx power, the Nss