## Slide 1: AP MLD Power Save Follow-up
Date: 2023-11-16
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: AP Power Save
AP power save can be used by soft/mobile AP (MLD), normal AP MLD.
Various AP power management methods are discussed
  Intra-PPDU power save
  Dynamic SM power save
  Power management mode with TWT
  Power management mode without TWT
  Power management under AP MLD

## Slide 3: AP’s Intra-PPDU Power Save and Dynamic SM Power Save
Similar to STAs, an AP can stop its PPDU reception if the AP figures out the PPDU doesn’t carry the frames addressed to it.
  BSS Color in PHY header is not same as its BSS Color and no BSS color collision is detected.
  The DL PPDU is detected.
  A frame is received whose RA is not the AP’s BSSID.

## Slide 4: Power Management Mode Change and Buffered Frame Indication
When the associated AP is in power management (active mode, power save mode with awake state and doze state) through periodic SPs, e.g. broadcast TWT, the AP needs to announce its power management mode and if the AP is in power management mode, the STAs can announce whether it needs to be serviced and whether they still have buffered frames.
PM in frame header is not suitable for AP’s announcement of power management change.
  It is difficult for the associated STAs to figure out the AP’s new power management mode at the same time.
Instead, an AP can announce its power management mode change through an announced specific time, e.g. a future TBTT or a specific TSF time.
  With this method, all STAs assume the AP’s operating mode change at the same time.
  A variant to this is that an AP uses the Beacon to announce the power management change that is effective right away.
When the associated AP is in power management through periodic SPs, a STA can use QoS Control, BSR and More Data.

## Slide 5: Dynamic SM Power Save
An AP announces its dynamic SM power save through mandate STA’s (MU-)RTS/CTS to initiate the TXOP with the AP.
  A variant to this is that an AP announces its dynamic SM power enabling through a new defined field e.g. in UHR Operation element.
    The announcement of enabling/disabling dynamic power management takes effect right away.
    Another variant is that the enabling/disabling dynamic power management at the indicated TBTT.
The AP uses single RF chain to listen on its work channel.
After receiving the initial frame of a TXOP for it, the AP uses more than one RF chain to do the frame exchanges in the TXOP.
Conditions to exit from multiple active RF chains at an AP with dynamic SM power save being enabled:
  An AP as the TXOP responder switches back to medium monitoring through single RF chain at the end of the TXOP.

## Slide 6: Enhanced Dynamic SM Power Save
An AP can further save power by monitor the medium in 20MHz channel only.
The non-AP STA can transmit a non-HT duplicate PPDU to solicit the responding PPDU from the AP where the AP monitors the medium in 20MHz channel only.
The AP switch back to the wider BW at the end of the initial PPDU.
The full capacity of the AP is used until the end of the TXOP.