## Slide 1: Beacon design with and without multiple BSSID support
Date: 2023-12-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Yi-Ling Chao Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Critical Update
The Beacon frame, Probe Response carry the critical update of the reporting AP, the channel switch related elements, Quiet element of the reported AP that is affiliated with the same AP MLD as the reporting AP.
  The reported AP is on a link other than the link where the Beacon or Probe Response is transmitted.
The ML Probe Response frame carries the critical update of the reported AP where the reported AP is one of the following
  The reported AP is affiliated with the same AP MLD as the AP that transmits the ML Probe Response frame
  The reported AP is affiliated with the same AP MLD as a nontransmitted BSSID AP where the nontransmitted BSSID AP is in the same multiple BSSID set as the AP that transmits the ML Probe Response frame

## Slide 3: Recap: Beacon Optimization
The Beacon is used to carry the BSS management information.
  The UHR information is not carried in Beacon. An Indication of UHR support is carried in the Beacon frame.
  If all the association STAs are UHR STAs, the further optimization can be done, i.e. the Beacon can carry the dynamic information and the basic information for the association
    TIM, SSID, security related information, ….

## Slide 4: Active Scanning and Passive Scanning in 802.11
A STA may wait for Beacon in passive scanning procedure.
A STA may use active scanning procedure to acquire the AP’s full information.
  This is required under MLD by using one link to acquire the other link’s information.
  This is required when the light Beacon is used in the BSS and the UHR information is not carried in the Beacon.
  This is required when the light Beacon is used in the BSS with association from non-UHR-STA being disabled and the minimal necessary information not carried in the Beacon.

## Slide 5: Beacon Information Analysis
TIM, optional Multi-Link Traffic Indication
  These element are useful for power save STAs.
Optional MME
  This element is needed if the Beacon protection is required.
Optional Transmit Power Envelope (TPE)
  The information is useful for active scanning if the BSS operating channel has the Tx power restriction.
The BSS operating parameters
  BSS Color.
    These parameter is needed when UHR PPDU is used for active scanning.
  Primary 20MHz channel.
    These parameter is needed when the light Beacon is transmitted in duplicate PPDU.
  BSS operating channel and channel puncture information.
    These parameters are needed if the full BSS BW is used for active scanning.
SSID
  This parameter is needed if SSID is used for deciding whether the full BSS information is probed.
  Short SSID may be an alternative for shorter light Beacon.

## Slide 6: Beacon Information Analysis (Cont’d)
Critical update
  The Critical Update Flag, Nontranmsitted BSSIDs Critical Update Flag, BPCC are required for a STA and the non-AP MLD with which a STA is affiliated to probe the critical update.
Security information
  RSNE is useful for STA to decide whether it can associate with the AP.
Multiple BSSID information
  The SSID of each nontransmitted BSSID is required if SSID is used for deciding whether the full BSS information is probed.
  The Short SSID for each nontransmitted BSSID AP may be an alternative for shorter light Beacon.
  The other information in nontransmitted BSSDI profile is less useful
AP MLD information.
  The BPCC related to reported AP

## Slide 7: Light Beacon without Multiple BSSID Support
When an AP doesn’t support/enable Multiple BSSID and allows the non-UHR STA’s association, the AP transmit its Beacon with pre-UHR information and UHR support indication.
When an AP doesn’t support/enable Multiple BSSID and doesn’t allow the non-UHR STA’s association, the AP transmit its Beacon with minimal information:
  TIM, Multi-Link Traffic Indication if TID-to-Link mapping 3 is enabled.
  BSS operating channel information for at least primary 20MHz channel and BSS Color.
  MME for Beacon protection
  TPE
  RSNE
  Critical Update Flag and BPCC
    BPCC is useful for extreme low power STA.
  Additionally, the other information can also be considered
    SSID etc. information can help the STA to decide whether sending Probe Request is reasonable.

## Slide 8: Light Beacon with Multiple BSSID Support
When an AP has transmitted BSSID AP and at least one AP in the multiple BSSID set allows the non-UHR STA’s association, the AP transmit its Beacon with pre-UHR information and UHR support indication.
When an AP has transmitted BSSID AP and all APs in the multiple BSSID set don’t allow the non-UHR STA’s association, the AP transmit its Beacon with minimal information:
  TIM, Multi-Link Traffic Indication if TID-to-Link mapping 3 is enabled.
  BSS operating channel information for at least primary 20MHz channel and BSS Color.
  MME for Beacon protection
  TPE
  RSNE
  Critical Update Flag and BPCC
    BPCC is useful for extreme low power STA.
  Nontransmitted BSSID Update Flag, SSID, Critical Update Flag and BPCC for nontransmitted BSSID AP.
  Additionally, the other information can also be considered
    SSID etc. information for transmitted BSSID AP can help the STA to decide whether sending Probe Request is reasonable.