## Slide 1: Consideration of Industrial Automation Scenarios -Follow Up
Date: 2023-11-DD
Authors:
Name | Affiliations | Address | Phone | e-mail
Akira Kishida | NTT | 1-1, Hikarinooka Yokosuka-Shi, Kanagawa 239-0847, Japan | +81-46-859-2093 | akira.kishida@ntt.com
Yusuke Asai | NTT |  |  | 
Yasushi Takatori | NTT |  |  | 

## Slide 2: Introduction
The updated UHR PAR & CSD [1][2] are confirmed in the 2023 July Plenary, and TGbn will proceed to realize the Scope of the Project in the PAR.
The PAR indicates that measurements of comparison with Extremely High Throughput MAC/PHY operation will follow a similar approach as used in previous amendments [3].
In the IEEE 802.11bn, some scenarios such as industrial automation will be varied from existing home or enterprise scenarios.
  New types of STAs that require low latency will be introduced, such as AGV (Automated Ground Vehicle) or AMR (Autonomous Mobile Robot) [4][5].
This contribution considers clarification of industrial automation scenarios to verify the effect of the technologies under consideration, such as multi-AP and low latency technologies, etc.
  It is important to verify whether the UHR technologies can satisfy the requirements to open up a new attractive market.

## Slide 3: Updated UHR PAR [1]
5.2.b Scope of the project: This amendment defines modifications to both the IEEE Std 802.11 physical layer (PHY) and the IEEE Std 802.11 Medium Access Control (MAC). The amendment adds an Ultra High Reliability capability to a Wireless Local Area Network (WLAN). The Ultra High Reliability capability is defined for both an isolated Basic Service Set (BSS) and overlapping BSSs as:
• at least one mode of operation capable of increasing throughput by 25%, as measured at the MAC data service Access Point, in at least one Signal to Interference and Noise Ratio (SINR) level (Rate-vs-Range), compared to the Extremely High Throughput MAC/PHY operation, and
• at least one mode of operation capable of reducing latency by 25% for the 95th percentile of the latency distribution compared to the Extremely High Throughput MAC/PHY operation and
• at least one mode of operation capable of reducing MAC Protocol Data Unit (MPDU) loss by 25% compared to the Extremely High Throughput MAC/PHY operation for a given scenario, especially for transitions between BSSs.
5.5 Need for the Project: Use of WLANs based on IEEE 802.11 technology continues to grow and diversify over many market segments including residential, enterprise, industrial and agriculture. More stringent requirements are needed to meet the demands of new applications (including metaverse [1], augmented and virtual reality [2], robotics, industrial automation for industrial IoT, logistics and smart agriculture [3]).
8.1 Additional Explanatory Notes:
5.2b and 5.3
Extremely High Throughput operation is defined in IEEE P802.11be Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications Amendment: Extremely High Throughput.
Measurements of comparison with Extremely High Throughput MAC/PHY operation will follow a similar approach as used in previous amendments (see https://mentor.ieee.org/802.11/dcn/14/11-14-0980-16-00ax-simulationscenarios. docx).

## Slide 4: Recap: TGax Simulation Scenarios [3]
The Simulation Scenarios document in TGax [3] analyzes and summarizes topologies of distribution of APs and STAs in dense environment scenarios.
Though these considerations are also beneficial for the UHR, the enterprise scenario in the document cannot apply to industrial automation scenarios as is.
Therefore, we should consider a new topology for industrial automation.
 | Scenario Name | Topology | Management | Channel Model | Homogeneity | ~Traffic Model
1 | Residential | A - Apartment building e.g. ~10m x 10m apartments in a multi-floor building ~10s of STAs/AP, P2P pairs | Unmanaged | Indoor | Flat | Home
2 | Enterprise | B - Dense small BSSs with clusters e.g. ~10-20m inter AP distance, ~100s of STAs/AP, P2P pairs | Managed | Indoor | Flat | Enterprise
3 | Indoor Small BSS Hotspot | C - Dense small BSSs, uniform e.g. ~10-20m inter AP distance ~100s of STAs/AP, P2P pairs |  |  |  | Mobile
4 | Outdoor Large BSS Hotspot | D - Large BSSs, uniform e.g. 100-200m inter AP distance ~100s of STAs/AP, P2P pairs | Managed | Outdoor | Flat | Mobile
4a | Outdoor Large BSS Hotspot + Residential | D+A | Managed + Unmanaged |  | Hierarchical | Mobile + Home

## Slide 5: Types of STAs in the Industrial Automation Scenarios
New types of STAs that require low latency will be introduced in the industrial automation scenarios.
  Moreover, each STA handles different types of traffic.
The following four types of STAs will be essential and should be considered in the industrial automation scenarios according to references [6]-[12].
  Remote Controlled Robots / Machines:
    Fixed in place, latency sensitive traffic / periodic and sporadic
  AGVs/ AMRs:
    Moving along the movement path, latency sensitive traffic / periodic and sporadic
  Cameras:
    Fixed in place, latency sensitive traffic, extremely high throughput required / sporadic
  Sensors:
    Fixed in place, non-latency sensitive traffic / sporadic

## Slide 6: Traffic Profiles for each STA
According to Reference [12], we assume the traffic profiles for each type of STA are as follows.
  Notes: these values are under consideration and one of the examples.
Profile | Periodic or Sporadic | Traffic pattern | Range of data size | Notes
Robot | Periodic | Constant period, 2 -20 [ms] cycle | 50 – 1000 [bytes] | Correspond to Traffic Type II: Cyclic in [12]. Add random offset time (unit: us).
 | Sporadic | Exponential distribution, E(x) = α×(2-20) [ms] | 50 – 1500 [bytes] | Correspond to Traffic Type III: Alarms and Events in [12].
AGV/AMR | Periodic | Constant period, 2 -20 [ms] cycle | 50 – 1000 [bytes] | Correspond to Traffic Type II: Cyclic in [12]. Add random offset time (unit: us).
 | Sporadic | Exponential distribution, E(x) = α×(2-20) [ms] | 50 – 1500 [bytes] | Correspond to Traffic Type III: Alarms and Events in [12].
Camera | Sporadic | Normal distribution, depends on Input traffic | 1000 – 1500 [bytes] | Correspond to Traffic Type VII: Video in [12].
Sensor | Sporadic | Exponential distribution, E(x) = 500-2000 [ms] | 500 – 1500 [bytes] | Correspond to Traffic Type IV: Configuration & Diagnostics in [12].

## Slide 7: Floor Size and the Number of STAs
Typical factories are desirable to be assumed for the industrial automation scenario.
  According to Reference [5], 100m x 100m x 30m site is suitable for the scenario.
Regarding the number of STAs, the following number might be practical, but no concrete numbers exist in the references. (Our draft plan of a factory automation scenario is shown in next slide)
  Remote Controlled Robots / Machines: 72 STAs (12 STAs x 6 assembly lanes)
  AGVs/ AMRs: 9 STAs (1 STA x 9 moving paths)
  Cameras: 24 STAs (4 STAs x 6 assembly lanes)
  Sensors: 400 STAs (1 STA x 20 x 20 square cells)

## Slide 8: Draft Plan of Industrial Automation Scenarios (without APs)

## Slide 9: The Number and Types of APs
Regarding the number of APs, we assume at least 1 AP per from 15 to 20 m square cell.
  1 AP per 15 m x 15 m square cell: 44 APs
  1 AP per 16 m x 16 m square cell: 39 APs
  1 AP per 20 m x 20 m: 25 APs
    Notes: TGax simulation scenarios deploy 1 AP per 9m x 9m square cell.
In IEEE 802.11bn, multi-AP should be assumed because that feature will be the key for the UHR.
  However, detailed architecture and function of multi-AP are on the way to be determined. Therefore, which APs are sharing APs or shared APs are not specified.
  An example of the deployment of the APs overlayed on the draft plan is shown in the next slide.

## Slide 10: An example of deployment for APs

## Slide 11: Summary
To clarify the effectiveness of the UHR technologies, it is important to consider new scenarios, such as industrial automation, in addition to existing home or enterprise scenarios.
This contribution discusses and clarifies industrial automation scenarios that consider new types of STAs that require latency sensitive traffic.

## Slide 12: References
[1] Laurent Cariou, et al., “UHR proposed PAR,” IEEE 802.11-23/0480r3
[2] Laurent Cariou, et al., “IEEE 802.11 UHR Proposed CSD,” IEEE 802.11-23/0079r10
[3] Simone Merlin, et al., “Simulation Scenarios,” IEEE 802.11-14/0980r16
[4] Akira Kishida, et al., “Consideration of Industrial Automation Scenarios,” IEEE 802.11-23/0915r0
[5] Yue Xu, et al., “Latency Consideration of Industrial Scenarios,” IEEE 802.11-23/1570r0
[6] Kate Meng, et al., “RTA report draft,” IEEE 802.11-18/2009r6
[7] “5G for Connected Industries and Automation,” 5G-ACIA, Feb 2019.
[8] “Wi-Fi 6/6E for Industrial IoT,” WBA (Wireless Broadband Alliance), November 2018.
[9] “Wireless TSN — Definitions, Use Cases & Standards Roadmap White Paper,” Avnu Alliance, Mar 2020.
[10] “IOWN GF-Cyber-Physical System Use Case,” IOWN Global Forum, 2021.
[11] Belliardi Rudy, et al., “IEC/IEEE 60802 Use Cases for Industrial Automation (TSN-IA Profile for Industrial Automation),”
[12] “Time Sensitive Networks for Flexible Manufacturing Testbed - Description of Converged Traffic Types,” Industrial Internet Consortium, 2018.
[13] “Wireless TSN: Market Expectations, Capabilities, & Certification,” Avnu Alliance, Feb 2022.

## Slide 13
Backup slides

## Slide 14: Survey results of the references [6]-[8]
References | RTA report [6] | 5G-ACIA: 5G for Connected Industries and Automation [7] | WBA: Wi-Fi 6/6E for Industrial IOT [8]
Use cases | Warehousing Logistics | High-level use cases in factories | Factory, Warehouse, Logistics
Floor plan | (None) | (None) | (None)
Largeness of area | (None) | Typical service area | (None)
Topology | Brief overview | Network-level overview | Brief WTSN architectures
Type of STAs | Classified into 3 classes (AGV, mobile robotics, AR/VR, remote HMI, hard-real-time cyclic control, machine tools, production lines, Hard-real-time isochronous control, motion control, printing, packaging) | AGV, Assembly line, Sensors, Robot motion control, etc | AMR/AGV, Sensors, Safety controls, video-AMR fusion, AR/VR/XR, industrial automotive, WTSN
# of STAs | (None) | Each type of use cases | None
KPIs | Time synchronization, Latency bound, Reliability, Throughput | Availability, Cycle time | Latency, Jitter, Throughput, Seed, Reliability, Handoff times
Traffic profile | Periodic data, Event-based, Request/Response | Typical payload size of use cases | Deterministic traffic
Notes | AGVs are classified into class A. | We adopt typical service area pf printing machine for largeness of area. | KPIs are vary according to each type of use cases.

## Slide 15: Survey results of the references [9]-[11]
References | Avnu Alliance® White Paper [9] | IOWN: Reference Implementation Model (RIM) for the Remote Controlled Robotic Inspection Use Case [10] | Use Cases IEC/IEEE 60802 [11]
Use cases | Mobile Robots, Closed loop control, Live events, AR/VR | High-level use cases | Factory, Plant, Sensors, Logistics, etc (classified by trafic profiles)
Floor plan | (None) | (None) | (None)
Largeness of area | Brief classification (Large. Medium, Small) | Brief description | Brief description
Topology | Brief WTSN architectures | Network-level overview | Hierarchical structure
Type of STAs | Same as use cases | Remote Controlled Robots, Environmental Sensors, Presentation Devices | None (classified by traffic profiles)
# of STAs | Each type of use cases | Each type of use cases | None
KPIs | Time Synchronization, Bounded latency, Reliability, Security, Capacity | Latency, Reliability | Latency, Jitter, etc
Traffic profile | Each type of use cases (Cyclic, Event, Isochronous, Continuous stream, video) | Data size, Occurrence rate | Detailed traffic types and profiles
Notes | AGVs are classified into class A. | KPIs are vary according to each type of use cases. | “Wireless” is one of the use cases in this document.

## Slide 16: KPIs and Requirements for AGV/AMR in Whitepapers
 | RTA report[6] | WBA[8] | Avnu Alliance[9] | 5G-ACIA[7] | IOWN GF[10]
Latency | 10-50 ms | < 10-20 ms | 1-10 ms (cyclic) 10-100 ms (events) | 10-100 ms (Video-operated remote control) | 10-100 ms
Jitter |  | < 1ms | - | - | -
Reliability | 99 to 99.9% | 99.9999% | 99 to 99.99% | 99.9999% | 99.9999%
Speed | - | < 50 km/h | - | - | -
Number of AGVs/AMRs per area | - | - | 100 | 100 | 100 (300)
Note | Values are from Class A applications (AGV). | Another KPI (Handoff times) depend on latency and speed. | Values are cited by combining two documents [9] and [13]. | Cyclic time is adopted as latency, and availability is adopted as reliability. | Values are cited by combining two “Robot manipulator” domains in [10].