## Slide 1: Considerations on Preemption
Date: 2023-11-13
Authors:

## Slide 2: Abstract
Preemption was proposed in UHR [1]-[4]to solve the problem of large delays when a large PPDU is transmitted in a TXOP.
With preemption support, a STA may preempt an ongoing frame exchange to transmit a low latency frame.
Low latency frames must be transmitted with similar or better reliability as the preempted (non-low latency) frame exchange.
In this contribution, we discuss considerations to increase the reliability of low latency frames transmitted using preemption.

## Slide 3: TXOP Protection of Low Latency Frame Transmission (1/2)
Using baseline rules, a TXOP owner (e.g. AP in the figure) may protect its transmission with an RTS/CTS exchange to set the NAV of STAs hearing both the TXOP owner and TXOP responder (e.g. STA 1 in the figure).
When preemption occurs, the baseline RTS/CTS frame exchange may not protect the low latency frame exchange.
e.g. STAs exposed to STA 2 but are hidden from AP and STA 1 may still transmit.
AP
(TXOP Owner)
STA 1
NON-LL STA
STA2
LL STA
OBSS STAs near AP and STA1
RTS
CTS
PPDU 1
NAV (RTS)
NAV (CTS)
SIFS
SIFS
Arrival of LL Data to STA2
SIFS
PPDU 2
BA
PPDU 3
SIFS
SIFS
SIFS
Low latency frame exchange

## Slide 4: TXOP Protection of Low Latency Frame Transmission (2/2)
If an OBSS STA is hidden from both AP and STA 1, the OBSS STA may access the channel during the TXOP, this may cause STA 2 to receive PPDU 2 in error (i.e. if PPDU 4 interference is too strong).
AP
(TXOP Owner)
STA 1
NON-LL STA
STA2
LL STA
RTS
CTS
PPDU 1
SIFS
SIFS
Arrival of LL Data to STA2
SIFS
PPDU 2
Low latency frame exchange
OBSS STAs hidden from AP and STA 1
PPDU 4
Error

## Slide 5: Options for Low Latency Frame Protection
Option 1: (MU)RTS/CTS protection during the low latency frame exchange
Option 2: (MU)RTS/CTS protection prior to the low latency frame exchange (e.g. at the start of TXOP)

## Slide 6: Low Latency Frame Exchange Protection: Option 1
In this option, the preempting STA initiates the low latency frame exchange using RTS/CTS.
This solution protects the low latency frame exchange from STAs that may try to contend for channel access after the low latency frame exchange has already started.
This solution may not be as effective if the channel access occurs before the preempting frame exchange.
AP
(TXOP Owner)
STA 1
NON-LL STA
STA2
LL STA
RTS
CTS
PPDU 1
SIFS
SIFS
Arrival of LL Data to STA2
SIFS
RTS
Low latency frame exchange
OBSS STAs hidden from AP and STA 1
PPDU 3
Error
PPDU 2
PIFS
Discard LL Data

## Slide 7: Low Latency Frame Exchange Protection: Option 2
AP
(TXOP Owner)
STA 1
NON-LL STA
STA2
LL STA
MU-RTS*
CTS
PPDU 1
SIFS
SIFS
Arrival of LL Data to STA2
OBSS STAs hidden from AP and STA 1
CTS
NAV (CTS)
SIFS
PPDU 2
BA
PPDU 3
SIFS
SIFS
Low latency frame exchange
In this option, the TXOP owner solicits CTS frames from potential LL STAs.
soliciting of CTS frames from LL STAs may be by request from LL STAs or by TXOP owner’s decision.
a single user info field for a group of LL STAs may be used to indicate CTS request from TXOP owner.
LL STAs transmitting a CTS frame prior to the low latency frame exchange may provide stronger TXOP protection than Option 1. However, it could also silence STAs nearby LL STAs unnecessarily.
SIFS

## Slide 8: Discussion
Option 1
Simpler operation but may be ineffective for denser networks.
LL STAs responding to RTS frames must ignore the NAV set by prior non-LL transmissions.
Option 2
May require trigger frame type transmission that is currently supported only by APs.
MU-RTS* frames can be made more efficient by assigning a single user info field for a group of LL STAs.
Need to consider avoiding unnecessarily silencing nearby OBSS transmissions.

## Slide 9: Preemption Request for UL Low Latency Frame Transmissions
Low latency frame exchange
AP
(TXOP Owner)
STA 1
NON-LL STA
STA2
LL STA
PPDU 1
SIFS
Preemption Indication = 1
PR
SIFS
STA3
LL STA
BSR
PR
SIFS
Arrival of LL Data to AP
Arrival of LL Data to AP
A TXOP Owner indicates preemption allowance or a priority field in the PHY header to indicate to LL STAs whether they are allowed to transmit after the current PPDU.
An LL STA transmits a PR frame (e.g. CTS frame) to request the TXOP owner to initiate an UL low latency frame exchange.
Because multiple LL STA may transmit a PR frame, PPDUs carrying the PR frames should be identical to prevent collision (similar to baseline MU-RTS/CTS procedure).
SIFS
BSRP
BSR
SIFS
SIFS
SIFS
TF
PPDU 2
SIFS
SIFS
PPDU 3
Multi-STA BA
SIFS
SIFS
PPDU 4

## Slide 10: Consideration on PR frames
Assuming a similar mechanism with MU-RTS/CTS, a PR frame transmitting STA need to know a value of Scrambler_Initial_Value and TA of the prior non-LL PPDU.
Compared to MU-RTS/CTS frames, the prior non-LL PPDU may be a UHR PPDU format (presumably with similar extremely high rates as EHT PPDUs) wherein the rate of the DATA field may not be supported by the UL LL STA.
  A UL LL STA may still decode the PHY header of the prior non-LL PPDU (and know whether preemption is enabled or not) but may not decode a Scrambler_Initial_Value or a TA.
The following are candidate solutions
  Option 1: The Scrambler_Initial_Value and RA to be used in a PR frame are indicated explicitly in a SIG field of the current non-LL PPDU (e.g. U-SIG or UHR-SIG).
  Option 2: The Scrambler_Initial_Value and RA to be used in a PR frame are fixed values.
  Option 3: Disallow preemption if at least one MPDU is not decoded in the non-LL PPDU.

## Slide 11: Comparisons
 | Option 1 (Explicit PHY Header indication) | Option 2 (Fixed Values) | Option 3 (Must decode DATA field)
Requires Prior PPDU DATA field decoding | NO | NO | YES
Allows PR frame transmission from OBSS STAs | YES | YES | YES
High PHY Header Overhead | YES | NO | NO
PR frame ambiguity | NO | YES | NO
Notes:
PR frame transmissions may also be enabled for OBSS transmissions (e.g. negotiated within a Multi-AP group). This feature may need more discussion by the group but is supported by Options 1-3.
Regarding PR frame ambiguity, if the Scrambler_Initial_Value and RA are not based on the prior PPDU, the TXOP owner may not know if a received frame is a valid PR frame.

## Slide 12: Summary
In this contribution, we discussed the reliability of frames transmitted using preemption.
First, we considered methods on protecting low latency frame transmission.
Second, we considered how PR frames may be generated without requiring UL LL STAs to decode a possibly unsupported rate UHR PPDU.

## Slide 13: References
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-1229-00-0uhr-preemption-for-low-latency-application-follow-up.pptx
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-1174-00-0uhr-txop-preemption-follow-up.pptx
[3] https://mentor.ieee.org/802.11/dcn/23/11-23-1242-01-0uhr-considerations-on-inter-ppdu-based-preemption-scheme.pptx
[4] https://mentor.ieee.org/802.11/dcn/23/11-23-1434-01-0uhr-discussions-on-low-latency-traffic-delivery-in-uhr.pptx