## Slide 1: Concurrent CCA for Non- Primary Channel Access
Date: 2023-11-13
Authors:

## Slide 2: Abstract
Several contributions propose non-primary channel access as a feature for UHR [1-6].
Some UHR STAs may support concurrent CCA on the primary and non-primary channels while some UHR STAs may only support CCA on one channel at a time.
In this contribution, we present a possible unfairness situation when concurrent CCA STAs coexist with non-concurrent CCA STAs and a proposed solution.

## Slide 3: Thoughts on Non-Primary Channel Access
Medium synchronization after switching to non-primary channel may severely limit the gains of non-primary channel access.
  Encourage use of concurrent CCA of primary and auxiliary channels to minimize the need for non-primary channel medium synchronization.
Prevent unfair advantages of STAs with concurrent CCA capability regarding non-primary channel access.

## Slide 4: Non-Primary Channel Access for Non-Concurrent CCA STAs
P80
S80
DATA
BA
auxiliary primary channel CCA
Channel Busy
switch to auxiliary primary channel
return to primary channel
PHY header or PPDU
BO
primary channel CCA
A STA that can only perform CCA one channel at a time needs to perform medium synchronization after switching to the auxiliary primary channel.
After the sensing duration, the STA may start contending on the channel and initiate a backoff procedure.
Unknown Channel State

## Slide 5: Auxiliary Primary Channel Access for Concurrent CCA capable STAs
switch to auxiliary primary channel
A STA that can perform concurrent CCA (e.g. primary channel on P80 and auxiliary primary channel on S80) may know the state of the auxiliary primary channel during the channel switch.
The STA may start contending on the channel right after the channel switch and initiate a backoff procedure.
Non-concurrent CCA STAs may often lose channel contention to concurrent CCA STAs.
non-concurrent CCA STAs can only contend much later due to medium sync procedure
P80
S80
DATA
BA
auxiliary primary channel CCA
Channel Busy
PHY header or PPDU
BO
primary channel CCA
concurrent CCA capable STAs contend here
medium sync duration

## Slide 6: Proposal
To prevent concurrent CCA capable STAs to monopolize the auxiliary primary channel, concurrent CCA capable STAs may be required to transmit a sync frame (e.g. CTS, short PPDU) first before transmitting a DATA frame.
  The sync frame may be transmitted with a higher priority (e.g. no or short backoff if the channel is already idle) than the DATA frame.
An AP capable of concurrent CCA may transmit sync frame transmission (regardless of downlink traffic) in case there are no other concurrent CCA capable STA exists.
P80
S80
DATA
BA
Channel Busy
PHY header or PPDU
Sync
BO
STAs (regardless of concurrent CCA capability) start contending here
auxiliary primary channel CCA
primary channel CCA

## Slide 7: Discussions
The proposed method allows fair channel access for both concurrent CCA capable STAs and concurrent CCA incapable STAs.
The proposed method is transparent to concurrent CCA incapable STAs which means no additional complexity to these STAs.
A concurrent CCA capable AP can help non-concurrent CCA capable STAs minimize the need for medium synchronization during auxiliary primary channel access.
  In such a scenario, a concurrent CCA capable non-AP STA still has incentive to implement concurrent CCA in cases when the AP sees channel activity but the non-AP STA does not.

## Slide 8: Conclusion
In this presentation, we discussed concurrent CCA capability for multiple primary channels.
We showed how this capability may result in unfair advantage for STAs that are capable vs STAs that are not capable.
We proposed a simple solution to prevent the unfairness.

## Slide 9: References
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-0034-00-0uhr-non-primary-channel-utilization.pptx
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-0285-00-0uhr-txop-protection-of-non-primary-channel.pptx
[3] https://mentor.ieee.org/802.11/dcn/23/11-23-0797-00-0uhr-non-primary-channel-access.pptx
[4] https://mentor.ieee.org/802.11/dcn/23/11-23-0961-00-0uhr-uhr-secondary-channel-access.pptx
[5] https://mentor.ieee.org/802.11/dcn/23/11-23-1112-00-0uhr-thoughts-on-secondary-channel-access.pptx
[6] https://mentor.ieee.org/802.11/dcn/23/11-23-1419-00-0uhr-nonprimary-channel-access-discussions.pptx