## Slide 1: Two Dimensional A-PPDU
Date: 2023-09-11
Authors:
Name | Affiliations | Address | Phone | email
Srinivas Kandala | Samsung |  |  | srini.k1@samsung.com
Myeongjin Kim | Samsung |  |  | mj1108.kim@samsung.com

## Slide 2: Introduction
One of the main objectives in UHR is low latency as described in UHR proposed PAR document [1].
Various latency reduction technologies were introduced in many UHR contributions [2-9].
We briefly proposed two dimensional (2D) A-PPDU in [2] as one of solutions to support low latency application.
In this contribution, we discuss 2D A-PPDU for downlink in more detail, with the ability of inserting PPDUs in the middle of a PPDU.

## Slide 3: Recap: FD A-PPDU
In [3], forward compatible OFDMA was proposed.
  Multiplexing between different generations of 802.11 PPDUs in frequency domain
  To improve scheduling flexibility and efficiency
In [4], aggregated PPDU for large BW was proposed.
  Multiplexing between different BW capable STAs in a PPDU in frequency domain
PPDU-3
PPDU-2
PPDU-1
Aggregated PPDU
160MHz
80MHz
80MHz

## Slide 4: Recap: Requirements for FD A-PPDU
Transparent to legacy STAs
PHY
  OFDM numerology including symbol duration shall be aligned
    EHT MU PPDU + HE MU PPDU
    EHT TB PPDU + HE TB PPDU
    UHR PPDUs (TBD)
    AP can align these using explicit signaling, such as “Number of EHT-SIG Symbols”, “Number of EHT-LTF Symbols”, “GI+LTF Size”,
  SIG design to support frequency domain multiplexing of different PPDUs
    Per 80 MHz U-SIG, EHT-SIG and UHR-SIG
  HE PPDU shall be 160 MHz, otherwise HE STA may decode wrong L-Length
  EHT and EHT+ PPDU multiplexing, there is no such restriction as long as it is 80MHz granularity
MAC
  Trigger frame design to support frequency domain multiplexing of different PPDUs
    Refer Trigger frame design
  SST operation together with TWT

## Slide 5: Recap: Pre-emptible PPDU Aggregation (1/2)
In [5], pre-emptible PPDU aggregation was proposed:
  Multiplexing between different PPDUs in time domain
  To improve latency for time sensitive MSDUs
Detail mechanism is as follows:
  The transmitter can end the ongoing PPDU after the nearest slot with a PPDU end marker, and then send latency-sensitive traffic within the TXOP.
  The PPDU end marker could be a rotation of L-LTF or some other predefined sequences.
Examples,
  When no latency sensitive traffic arrived
  When latency sensitive traffic arrived

## Slide 6: Recap: Pre-emptible PPDU Aggregation (2/2)
[6] proposes:
  TXOP preemption indication that indicates if preemption is allowed
  Time gap preemption indication will signal if preemption is allowed after a gap period.
  Mechanism provides flexibility for both UL and DL to be able to transmit low-latency frames amidst a TXOP.
  Breaks the TXOP into multiple PPDUs, which increases the overhead.
[7] enhances the basic concepts in [6] after considering some of its limitations.
[8] proposes the indication of low latency indication frame amidst an on-going TB PPDU transmission through a pre-agreed signal.
[9] builds on [6] on preemption coordination, channel access and resource allocation.

## Slide 7: Recap: 11ay A-PPDU
In section 28.3.2.2 of [10], EDMG A-PPDU is defined as follows
  Only to a single user and shall not be transmitted to multiple users.
  Each subsequent PPDU includes EDMG Header A and Data field only.
  Actual A-PPDU duration is unknown at the time of L-Header transmission.
  Each EDMG-Header-A includes PSDU length and Additional EDMG PPDU subfield.
  It seems A-PPDU is to same user as there is no EDMG-CEF for the subsequent PPDUs.

## Slide 8: Two Dimensional A-PPDU (1/5)
Requirement of inserted PPDU for latency sensitive MSDUs
  Transparent to legacy STA including 11be R1 STA
  We want to transmit latency sensitive MSDU on on-going PPDU including FD A-PPDU as much as possible so that we can reduce latency.
  Using only necessary subchannel(s). Entire 320 MHz PPDU is quite wasteful given the size of latency sensitive traffic is typically small.
Considering these requirements, we propose two dimensional (2D) A-PPDU as the following example.
PPDU-3
PPDU-2
PPDU-1
Aggregated PPDU
160MHz
80MHz
80MHz
Inserted PPDU (Latency Sensitive PSDU)
Traffic arrives
Inserted at predetermined location

## Slide 9: Two Dimensional A-PPDU (2/5)
Another example is within one DL OFDMA MU PPDU
RU 1
RU 2
RU 3
2D OFDMA
40MHz
20MHz
20MHz
Inserted PSDU (Latency Sensitive PSDU)
RU 1
RU 2
RU 3
Normal OFDMA
40MHz
20MHz
20MHz
Traffic arrives
Inserted at predetermined location

## Slide 10: Two Dimensional A-PPDU (3/5)
Can we insert latency sensitive MSDU on going PPDU without any legacy problem?
  We shall ensure that there is no impact on operation of the original PPDU receiver.
  Shall be no change in original PPDU or RU reception procedure.
  Entire PPDU shall be as indicated by the L-Length.
  ACK or BA and other procedure followed by a PPDU shall remain same. The original PPDU recipient can send ACK/BA as instructed.
  Data portion of inserted PPDU will be failed. Already happens in IEEE 802.11 system, e.g. by OBSS interference.
  UHR STA may detect the start of inserted PPDU and stop decoding until the end of the inserted PPDU.
  ACK/BA for latency sensitive PPDU can be multiplexed using MU-BAR included separately in the inserted PPDU (Need some empty resource in the MU-BAR in the original PPDU)
  Or ACK/BA for latency sensitive PPDU can be set to delayed ACK

## Slide 11: Two Dimensional A-PPDU (4/5)
High level design criteria
  Inserted PPDU start indication
    Time-domain (auto/cross) correlation method may not work unless we process only the potential subchannel.
    Thus, we can consider indicating it using frequency-domain method. E.g. by two repeated LTFs and CRC of SIG.
  Predetermined start time
    In order to reduce complexity at latency sensitive MSDU receiver, we want to use slot based start time.
    For example, we can define a fixed number of OFDM symbol for a potential start of TD PPDU.
  Potential indication of existence of inserted PPDU
    We can also include potential inclusion of inserted PPDU in SIG field of original UHR PPDU.
    It is possible to insert PPDU in UHR or EHT or HE or even VHT/HT/non-HT PPDU .

## Slide 12: Two Dimensional A-PPDU (5/5)
Structure
  Bandwidth
    To simplify receiver of latency sensitive MSDU receiver, we want to limit maximum bandwidth to 80 MHz, so, potential bandwidth can be 20/40/60/80 MHz.
    Should include predetermined 20 MHz, e.g. primary 20 MHz.
  OFDMA
    May enable OFDMA within inserted PPDU with limited resource sizes, e.g. 242-tone RU, 484-tone RU, 484+242-tone MRU, 996-tone RU
  UHR LTF and SIG (Header) can be served as start indication.
    Number of symbol for UHR LTF should be fixed, e.g. 2
    Number of symbol for SIG should be fixed, e.g. 1
    Note: numerology for UHR LTF and SIG should be same as the original data symbol numerology.
DATA
LTF
SIG

## Slide 13: Header of Inserted PPDU in Two Dimensional A-PPDU
LTF
  Latency sensitive STA may check existence of UHR LTF in the inserted PPDU.
  No beamforming
  Single stream LTF
    Repeated single stream UHR LTF to enable easy LTF detection as well as CFO/CPE correction
SIG
  A receiver can confirm existence of inserted PPDU using CRC in the SIG .
  SIG can be encoded within 20 MHz bandwidth of the inserted PPDU, and duplicated for different 20 MHz within the bandwidth of inserted PPDU.
  The following fields can be included in SIG.
    PHY Version Identifier
    LDPC Extra Symbol Segment
    Pre-FEC Padding Factor
    PE Disambiguity
    RU Allocation subfield: This tells BW and puncturing information of inserted PPDU.

## Slide 14: Example of 2D A-PPDU Structure
L-Length
Potential Start Position
PPDU-3
PPDU-2
PPDU-1
Aggregated PPDU
160MHz
80MHz
80MHz
Inserted PPDU-4
Preamble
Preamble
Preamble
Potential Start Position
Potential Start Position
Header
ACK-3 (&4)
ACK2
ACK1

## Slide 15: Summary and Conclusions
Introduced the details of two dimensional PPDU, where RUs are not only assigned in frequency domain but also in time domain for downlink transmissions to improve latency for time sensitive MSDU.
Having the ability for a STA to access an inserted PPDU in the middle of PPDU would enable transmission of late-arriving low-latency MSDUs to be transmitted in a timely manner.

## Slide 16: Straw Poll
Are you in favor of supporting the concept of two dimensional PPDUs for downlink transmissions in TGbn?
Yes:
No:
Abstain:

## Slide 17: References
[1] 11-23/0480r3, UHR Proposed PAR
[2] 11-22/1393r0, Latency Reduction Scheme for UHR
[3] 11-20/674r3, “Forward Compatible OFDMA”
[4] 11-20/693r1, “Aggregated PPDU for Large BW”
[5] 11-21/670r0, “Further Improve Latency Performance in 11be”
[6] 11-23/1229r1, “Preemption for low latency application (Follow up)”
[7] 11-23/1174r0, “TXOP preemption follow up”
[8] 11-23/1194r0, “Overlapped indication to support preemption”
[9] 11-23/1242r1, “Considerations on Inter-PPDU based Preemption Scheme”
[10] Draft P802.11ay_D5.0