## Slide 1: Enhanced replay detection for header protection
Authors:
Name | Affiliations | Address | Phone | email
Abhishek Patil | Qualcomm |  |  | appatil@qti.qualcomm.com
Duncan Ho |  |  |  | 
Alfred Asterjadhi |  |  |  | 
George Cherian |  |  |  | 
Gaurang Naik |  |  |  | 
Date: 2023-11-03

## Slide 2: Background
Enhancing security in 802.11 is one of the goals of UHR
  To that effect, UHR will provide mechanisms to protect certain Control frames and fields within the MAC header.
Previous proposals (see 23/1888) discuss protection the MAC header via integrity check
  A MIC is generated based on the fields of the MAC header.
    Since the contents of the header fields can change when an MPDU is retried, a fresh MIC is generated (only) for the header fields each time an MPDU is retried
      The payload of the MPDU is not re-encrypted
  Control frames are also protected via a MIC
In this contribution we look at attack scenarios that warrant the need for adding a time component to the security algorithm.
  Specifically, we propose to have the PN be based on portion of the TSF

## Slide 3: Issue
A packet number (PN) is used for replay detection
  A frame is considered as replayed if the received PN is <= the last received PN
    In other words, the PN needs to be monotonically increasing.
  Note – The PN is included in plaintext within the frame so that the receiver knows the PN that was used for protection.
There can be attack scenarios where a rogue device is able to jam the recipient from receiving the frame, while recording the frame.
  Later, the attacker replays the recorded frame (unmodified).
    This is a jam, record and replay attack
  Since the recipient did not receive the original frame, it does not have a record of the PN carried in that frame.
    As a result, the attack is successful (i.e., the attacker manages to fool the replay detection logic).
  The attack is especially possible when there is sparse or bursty traffic
  When the frame is received, the recipient can get into an undesirable state or perform unwanted actions depending on the contents of the MAC header fields
    For example, when the original frame indicates changes to some operational parameters, the receiver would apply them at the wrong time which would cause the transmitter and receiver to be in different states.

## Slide 4: Potential attack scenarios

## Slide 5: Solution and challenges
Solution summary:
  The remedy for such a jam, record and replay attack is to have a time component in the PN so that the receiver can discard a ‘stale’ frame.
    Using TSF as PN is an option
Although the approach will preserve the requirement that a PN is monotonically increasing, there are challenges to this approach as described below
Challenge:
  At the receiving device, the time based PN needs to match with the local time
  However, a client device is allowed to have extend periods of doze state to conserve battery.
    For example, a client that has indicated a listen interval (LI) of 10 is allowed to skip up to 10 beacons.
      TBTT occurs every 100 ms  a client with LI of 10 will skip beacons for up to 1 second (10 BIs).
  Since the clocks run independently on each device, they will drift overtime. The standard requires an accuracy of +/-100ppm
    Therefore, in the worst-case drift between an AP and a client can be ± 200 ppm (see 11.1.3.9)
  As an example, a client with an LI of 10 can have its local TSF off by 200 µs with respect to its AP after skipping 10 beacons (1sec).
    In such case, if the client has a slower clock, it will be 200 µs behind the AP’s TSF and a UL frame from the client will have a PN that will be 200 µs in the past.
    This will cause the AP to discard a genuine frame since the TSF appears to be stale

## Slide 6: Addressing drift
Solution:
  Reduce the granularity of time by ignoring lower bits of TSF to mask the clock drift
    The number of LSBs ‘x’ to ignore is TBD.
    In this contribution, we provided some examples with x=8.
    The x value could be standardized or can be negotiated between the two devices based on their capability
      i.e., LI and expected drift.
  For example, by not including the lower 8 bits, the timing granularity reduces to 256 µs which would be sufficient to address majority of the clock drift scenarios.
However, the reduced time granularity means multiple packets sent within a 256 µs window would be stamped with the same TSF.
  This will cause the receiver to drop packets
To address this, append a counter to the partial TSF
  Counter increments each time a packet is transmitted with the same TSF value and resets to 0 when LSB of the partial TSF rolls over
  The overall PN is a concatenation of partial TSF + an x bit counter
  Assuming PN size remains unchanged (48 bits) and the lower 1 octet represent a counter:
    PN[0:7] = 8bit counter
    PN[8:47] = TSF[8:47]
  TSF[48:63] is not signaled

## Slide 7: Multiple tx with the same (partial) TSF
At the receiving device, the replay check is performed as follows:
  compare the (partial) TSF with current local time and
    If the received value is lower than the current local (partial) TSF, drop the packet*.
    Else, if the received TSF is the same as the TSF received in the most recent packet, compare the received counter value:
      If the received counter value is equal or less than previously received counter, drop the packet
      Else, process the packet further
    Else process the packet further
  Record the received (partial) TSF and the counter values as the last know values (respectively) for a packet that passed replay check and subsequent checks (e.g., MIC validation)
    These are used for comparison with the immediately next received packet
* there is a corner case when the (x+1)th bit of the TSF has recently flipped.
  For example (assuming x=8), receiver’s 9 bits of TSFR[0:8] = 100000001; while transmitter is TSFT[0:8] = 011111101)  off by 4 us
  In such case, since the PN value used for header protection is carried within the frame, the recipient will know that the transmitter clock is slightly behind and will still accept the frame.
    There can be some tolerance built into the system.

## Slide 8: PN rollover
Today, when the PN wraps around (i.e., all the values are exhausted), both devices perform a rekeying operation to generate a new security key.
For TSF[8:47] the wraparound would occur after 2^48 µs = 3258 days
  Therefore, in most scenarios, TSF/PN wraparound will not be the reason for rekeying
    In other words, the TSF space is sufficiently long
In MLO, each affiliated AP is allowed to have an independent clock
  As a result, TSF on each link can be a different value
    Consequently, a TSF based PN would be link specific
  This would be OK since the contents of the MAC header and Control frames are specific to a link.
  We could consider adding link ID as part of the PN (not strictly needed).
    Assuming upper byte is reserved for link ID
See appendix for some calculation

## Slide 9: Summary
In summary, this contribution proposes to use portion of the TSF as PN to prevent jam, record, replay attacks.
  The proposal accounts for clock drift and MLO considerations
  Proposes to add a short counter to account for loss in TSF granularity
The proposal maintains the monotonically increasing properties of PN

## Slide 10: Appendix

## Slide 11: PN rollover computation
If lower 8 bits of the PN is used for signaling a counter, then the PN[8:39] will carry the partial TSF:
PN[0] PN[1] PN[2] PN[3] PN[4] PN[5]
2^48 | 2.81475E+14 |  | 2^40 | 1.09951E+12
sec | 281474976.7 |  | sec | 1099511.628
hrs | 78187.49353 |  | hrs | 305.4198966
days | 3257.81223 |  | days | 12.72582903
yrs | 8.92551296 |  | yrs | 0.034865285