## Slide 1: Gain analysis for coordinated AP transmissions
Authors:
Name | Affiliations | Address | Phone | email
Abhishek Patil | Qualcomm |  |  | 
George Cherian |  |  |  | 
Gaurang Naik |  |  |  | 
Duncan Ho |  |  |  | 
Alfred Asterjadhi |  |  |  | 
Sanket Kalamkar |  |  |  | 
Giovanni Chisci |  |  |  | 
Sherief Helwa |  |  |  | 
Date: 2023-11-02

## Slide 2: Objective
Background
  Previous contributions in TGbe provides gain analysis for C-TDMA with full buffer traffic (see 11-19/1879)
Objectives of this contribution
  Provide gain analysis for coordinated AP transmissions with focus on tail latency gain for aperiodic traffic in IEEE Enterprise R3 network.

## Slide 3: Topology: IEEE Enterprise R3 (reduced)
1
2
3
4
5
6
IEEE Ent R3 topology reduced to 40x40m square

## Slide 4: Simulation setup
6 AP’s (BSS1 to 6) each having 2 STAs. Config per BSS:
  LL DL for 1 STA (Poisson arrival)
    Short (1500 bytes) LL packets w/ mean arrival of ~0.7ms
  UL full buffer from the other STA
C-TDMA scheduling scheme:
  TXOP owner shares TXOP with nearest AP(s) that have pending LL traffic
    Buffer checked at start of TXOP and shared TXOP duration is based on the buffer size
  TXOP can be shared with up to 2 other APs
C-RTWT scheduling scheme:
  SPs are assigned in round-robin fashion among the 6 APs
    12 ms split into six 2 ms SPs.
C-RTWT + C-TDMA scheduling scheme:
  SP owner (equivalent to TXOP owner) can share TXOP with other APs
    TXOP sharing scheme same as the C-TDMA schedule scheme
  12 ms split into six 2 ms SPs.
Sim drops/duration: 10 drops for 20sec each
Max TXOP = 4ms

## Slide 5: Simulation results
Total latency indicates the e2e 1-way latency and accounts for channel access and queuing delays.
Total latency (usec) | Mean | Median | P95
Baseline | 16283 | 9268 | 56478
CTDMA | 8917 | 6436 | 25286
CRTWT | 4862 | 3457 | 12638
CTDMA + CRTWT | 2306 | 1639 | 6558
Chart: Coordinated AP Tx Gains
| Mean | Median | P95
CTDMA | 1.8261 | 1.44 | 2.2336
CRTWT | 3.349 | 2.6809 | 4.4689
CTDMA + CRTWT | 7.0611 | 5.6547 | 8.6121

## Slide 6: Summary
The contribution provides simulation results for IEEE enterprise R3 topology for C-TDMA, C-RTWT and the combined scheme.
  The results show gains for all 3 coordination schemes with higher gains when both schemes are applied together.