## Slide 1: Periodical NSS Adjustment for an MLD
Date: 2023-11-03
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yue Zhao |  |  |  | 
Maolin Zhang |  |  |  | 
Ming Gan |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
There are some scenarios that a STA can not, or is not allowed to do a transmission during certain time periods, due to
  In-device coexistence with a non-Wi-Fi system
  Co-TDMA with OBSS
  Periodically scheduled by AP
It is a waste if the radio chains can not be used during such time periods;
For a single link device, it is hard to use the radio chains under such cases;
The introduction of multiple links in 11be provides an opportunity to use these radio chains. An MLD can dynamically switch radio chains among multiple links.

## Slide 3: Existing Mechanisms to adjust NSS
Operating Mode
  A STA can reduce the number of SS for power saving through OM;
  OM signaling is carried in an A-Control field of a QoS data or QoS null frame, or in an Operating Mode Notification frame, or in an Operating Mode Notification element.
EMLSR;
  Listen on EMLSR links with single SS and limited receiving capability;
  Switch to multiple SS transmitting and receiving capability after receiving an initial control frame on the link that the initial control frame was received;
  Switch back to listening mode after the frame exchanges.
EMLMR
  Operating with per-link NSS capability on EMLMR links;
  Switch to EMLMR NSS capabilities after receiving an initial control frame on the link that initial frame was received;
  Switch back to per-link NSS after the frame exchanges.
SMPS
  Operating on single SS;
  Switch to multiple SS after receiving a initial frame;
  Switch back to single SS after the frame exchanges.

## Slide 4: Why not Existing Mechanisms
None of existing mechanisms mentioned in the previous slide are designed in a periodical way;
OM adjusts the NSS semi-statically, it is not suitable to change NSS so frequently on a tens of milliseconds level;
When EMLSR/EMLMR/SMPS are operating as a mode, the NSS changes dynamically depending on when to obtain an TXOP.

## Slide 5: Periodical NSS for an MLD
Below is an example of periodical NSS for an MLD.
An MLD announces max NSS = m and n on link 1 and link 2 respectively through an UHR Operation element in Association Request frame;
During the first part of each time period (equal to T), the STA on link 1 can not transmit due to Co-TDMA with an OBSS. The NSS = 0 on link 1, and the MLD switches the m radio chains from link 1 to link 2, and the NSS on link 2 becomes m+n accordingly;
During the second part of each time period, the STA on link 1 resumes its transmission capability. The MLD switches the m radio chains back to link 1. NSS on link 1 and link 2 return to m and n respectively.

## Slide 6: Summary
A STA may not able to transmit during some time periods, and the radio chains may be wasted;
An MLD can switch radio chains from one link to another link to fully use the radio chains;
Current NSS adjustment mechanisms are not designed in a periodical way;
This idea enables a periodical NSS adjustment that will help to fully use the MLD radio chains.

## Slide 7: Straw Poll 1
Do you think a periodical NSS adjustment mechanism will benefit an MLD to fully use its radio chains?
  Yes
  No
  Need more time to think about it
  Abstain